## Slide 1: kathara lab
Subnetting IPv4
Version | 2.0
Author(s) | T. Caiazzi, G. Di Battista
E-mail | contact@kathara.org
Web | http://www.kathara.org/
Description | Exercises on IPv4 subnetting

## Slide 2: copyright notice
All the pages/slides in this presentation, including but not limited to, images, photos, animations, videos, sounds, music, and text (hereby referred to as “material”) are protected by copyright.
This material, with the exception of some multimedia elements licensed by other organizations, is property of the authors and/or organizations appearing in the first slide.
This material, or its parts, can be reproduced and used for didactical purposes within universities and schools, provided that this happens for non-profit purposes.
Information contained in this material cannot be used within network design projects or other products of any kind.
Any other use is prohibited, unless explicitly authorized by the authors on the basis of an explicit agreement.
The authors assume no responsibility about this material and provide this material “as is”, with no implicit or explicit warranty about the correctness and completeness of its contents, which may be subject to changes.
This copyright notice must always be redistributed together with the material, or its portions.

## Slide 3: lab-1-lan: analyze the scenario
router 1
200.100.50.0/24
router 2
10.0.0.0/30
eth0
1
eth1
2
eth0
1
A
eth0
2
eth0
3
pc1
pc2
B

## Slide 4: lab-1-lan: configurations
router1[0]="A/00:00:00:00:00:a1"
router1[1]="B/00:00:00:00:00:b1"
router1[image]="kathara/core"
router1[ipv6]="false"
router2[0]="B/00:00:00:00:00:b2"
router2[image]="kathara/core"
router2[ipv6]="false"
pc1[0]="A/00:00:00:00:00:01"
pc1[image]="kathara/core"
pc1[ipv6]="false"
lab.conf
pc2[0]="A/00:00:00:00:00:01"
pc2[image]="kathara/core"
pc2[ipv6]="false"
lab.conf

## Slide 5: lab-1-lan: configurations
ip address add 195.11.14.5/24 dev eth0
ip route add default via 195.11.14.1
pc1.startup
ip address add 200.1.1.7/24 dev eth0
ip route add default via 200.1.1.1 dev eth0
pc2.startup
ip address add 200.100.50.1/24 dev eth0
ip address add 10.0.0.2/30 dev eth1
ip route add default via 10.0.0.1
router1.startup
ip address add 10.0.0.1/30 dev eth0
router2.startup

## Slide 6: lab-1-lan: questions
router 1
200.100.50.0/24
router 2
10.0.0.0/30
eth0
1
eth1
2
eth0
1
A
eth0
2
eth0
3
pc1
pc2
B
Inspect the routing table of router 1, how many entries are there?
What is the broadcast address for LAN A?
What is the broadcast address for LAN B?

## Slide 7: lab-1-lan: inspecting the routing table
router 1
200.100.50.0/24
router 2
10.0.0.0/30
eth0
1
eth1
2
eth0
1
A
eth0
2
eth0
3
pc1
pc2
B
root@router1:/# ip route
default via 10.0.0.1 dev eth1
10.0.0.0/30 dev eth1 proto kernel scope link src 10.0.0.2
200.100.50.0/24 dev eth0 proto kernel scope link src 200.100.50.1
router1
Default route towards router2

## Slide 8: lab-1-lan: inspecting the routing table
router 1
200.100.50.0/24
router 2
10.0.0.0/30
eth0
1
eth1
2
eth0
1
A
eth0
2
eth0
3
pc1
pc2
B
root@router1:/# ip route
default via 10.0.0.1 dev eth1
10.0.0.0/30 dev eth1 proto kernel scope link src 10.0.0.2
200.100.50.0/24 dev eth0 proto kernel scope link src 200.100.50.1
router1
Directly connected routes

## Slide 9: lab-1-lan: checking the broadcast address
router 1
200.100.50.0/24
router 2
10.0.0.0/30
eth0
1
eth1
2
eth0
1
A
eth0
2
eth0
3
pc1
pc2
B
root@router1:/# routel
Dst Gateway Prefsrc Protocol Scope Dev Table
default 10.0.0.1 eth1
10.0.0.0/30 10.0.0.2 kernel link eth1
200.100.50.0/24 200.100.50.1 kernel link eth0
10.0.0.2 10.0.0.2 kernel host eth1 local
10.0.0.3 10.0.0.2 kernel link eth1 local
127.0.0.0/8 127.0.0.1 kernel host lo local
127.0.0.1 127.0.0.1 kernel host lo local
127.255.255.255 127.0.0.1 kernel link lo local
200.100.50.1 200.100.50.1 kernel host eth0 local
200.100.50.255 200.100.50.1 kernel link eth0 local
router1
Broadcast address for LAN A

## Slide 10: lab-1-lan: checking the broadcast addresses
router 1
200.100.50.0/24
router 2
10.0.0.0/30
eth0
1
eth1
2
eth0
1
A
eth0
2
eth0
3
pc1
pc2
B
root@router1:/# routel
Dst Gateway Prefsrc Protocol Scope Dev Table
default 10.0.0.1 eth1
10.0.0.0/30 10.0.0.2 kernel link eth1
200.100.50.0/24 200.100.50.1 kernel link eth0
10.0.0.2 10.0.0.2 kernel host eth1 local
10.0.0.3 10.0.0.2 kernel link eth1 local
127.0.0.0/8 127.0.0.1 kernel host lo local
127.0.0.1 127.0.0.1 kernel host lo local
127.255.255.255 127.0.0.1 kernel link lo local
200.100.50.1 200.100.50.1 kernel host eth0 local
200.100.50.255 200.100.50.1 kernel link eth0 local
router1
Broadcast address for LAN B

## Slide 11: lab-2-lan: complete the configurations
router 1
X.X.X.X/25
router 2
10.0.3.0/30
eth0
2
eth2
x
eth0
x
A1
eth0
3
pc1
B
A2
eth0
130
pc2
X.X.X.X/25
eth1
x

## Slide 12: lab-2-lan: complete the configurations
router 1
X.X.X.X/25
router 2
10.0.3.0/30
eth0
2
eth2
x
eth0
x
A1
eth0
3
pc1
B
A2
eth0
130
pc2
X.X.X.X/25
eth1
x
Open the lab folder and complete the configuration
by filling in the fields marked with Xs.
There is only one solution.
Once the configuration is complete,
each device should reach the others.

## Slide 13: lab-2-lan: modify router2 commands
router 1
X.X.X.X/25
router 2
10.0.3.0/30
eth0
2
eth2
x
eth0
x
A1
eth0
3
pc1
B
A2
eth0
130
pc2
X.X.X.X/25
eth1
x
In the provided configuration router2 has two different entries (corresponding to the /25 prefixes) in the routing table. Can we provide the same connectivity adding a single entry in the routing table?
Modify router 2 commands and try to see if it works.

## Slide 14: lab-4-lan: complete the configurations
router 1
router 2
10.0.13.0/30
eth0
1
eth0
2
B
A4
eth0
87
pc1
100.50.25.X/26
A1
eth0
214
pc2
100.50.25.X/26
eth0
16
pc3
100.50.25.X/26
eth0
156
pc4
100.50.25.X/26
A2
A3
eth1
76
eth2
206
eth3
11
eth4
145
The configuration of router2 is not complete. Complete the configuration by filling in the
fields marked with Xs.
Verify your work by pinging the PCs from
router2.