## Slide 1: kathara lab
rip with FRRouting
Version | 1.1
Author(s) | G. Di Battista, M. Patrignani, M. Pizzonia, L. Ariemma, M. Scazzariello, T. Caiazzi
E-mail | contact@kathara.org
Web | http://www.kathara.org/
Description | experiences with the ripv2 distance vector routing protocol – derives from kathara rip lab ver. 1.2 which, in turns, derives from netkit rip lab ver. 2.4

## Slide 2: copyright notice
All the pages/slides in this presentation, including but not limited to, images, photos, animations, videos, sounds, music, and text (hereby referred to as “material”) are protected by copyright.
This material, with the exception of some multimedia elements licensed by other organizations, is property of the authors and/or organizations appearing in the first slide.
This material, or its parts, can be reproduced and used for didactical purposes within universities and schools, provided that this happens for non-profit purposes.
Information contained in this material cannot be used within network design projects or other products of any kind.
Any other use is prohibited, unless explicitly authorized by the authors on the basis of an explicit agreement.
The authors assume no responsibility about this material and provide this material “as is”, with no implicit or explicit warranty about the correctness and completeness of its contents, which may be subject to changes.
This copyright notice must always be redistributed together with the material, or its portions.

## Slide 3: the RIP protocol
RIP is a routing protocol
RIPS is a distance-vector routing protocol
  approach: send all your information to a few
  update your routing information based on what you hear
in this lab we will see an example of RIPv2 protocol on the FRRouting Suite

## Slide 4: sample frr.conf configuration file
root@pc1:~$ cat /etc/frr/frr.conf
!
! FRRouting configuration file
!
!
! RIP CONFIGURATION
!
router rip
redistribute connected
network 100.1.0.0/24
!
log file /var/log/frr/frr.log
talk rip on some interface
redistribute to rip neighbors' information about all directly connected subnets
send rip multicast packets to interfaces falling into this prefix

## Slide 5: about redistribute connected
by default (i.e., without further configuration) RIP already propagates information about all directly connected subnets attached to RIP-speaking interfaces
redistribute connected forces RIP to propagate information about all connected subnets
the semantic of redistribute connected applies to all routing protocols
the default behavior does not
  some protocols (e.g., bgp) are lazier, and do not propagate anything unless explicitly told to do so

## Slide 6: small network connected to Internet
r5
r4
r1
r3
r2

## Slide 7: the involved ip subnets
each circle represents a subnet
r5
r4
r1
r3
r2
L
B
A
H
E
C
D
G
F
I
legend

## Slide 8: assigning ip numbers to subnets
100.1.4.0/24
r5
L
r4
r1
r3
B
100.1.2.0/24
A
100.1.1.0/24
H
100.1.0.12/30
E
100.1.0.0/30
100.2.0.0/30
r2
C
100.1.3.0/24
D
G
F
I
100.1.0.4/30
100.1.0.16/30
100.1.0.8/30
legend
ip subnet
assigned prefix
L
100.2.0.0/30

## Slide 9: assigning ip numbers to interfaces
r5
eth0
1
eth0
2
L
eth2
18
r4
eth3
14
eth1
9
eth2
1
eth0
6
eth1
10
r1
r3
eth3
1
eth2
1
B
100.1.2.0/24
A
100.1.1.0/24
H
100.1.0.12/30
E
100.1.0.0/30
100.2.0.0/30
r2
eth2
17
C
100.1.3.0/24
eth0
13
D
100.1.4.0/24
eth1
1
G
F
I
eth3
1
eth0
2
eth1
5
100.1.0.4/30
100.1.0.16/30
100.1.0.8/30
dev
ip
legend
last byte of ip address
network interface

## Slide 10: launching the lab
the lab configuration is such that the frr routing daemon is not automatically started
root@localhost:~$ cd kathara-lab_rip
root@localhost:~/kathara-lab_rip$ kathara lstart

## Slide 11: checking connectivity
towards a directly connected destination
r4:~# ping 100.1.0.13
PING 100.1.0.13 (100.1.0.13) 56(84) bytes of data.
64 bytes from 100.1.0.13: icmp_seq=1 ttl=64 time=1.23 ms
64 bytes from 100.1.0.13: icmp_seq=2 ttl=64 time=0.592 ms
64 bytes from 100.1.0.13: icmp_seq=3 ttl=64 time=0.393 ms
--- 100.1.0.13 ping statistics ---
3 packets transmitted, 3 received, 0% packet loss, time 2032ms
rtt min/avg/max/mdev = 0.393/0.741/1.238/0.360 ms
r4:~# █
r4

## Slide 12: checking connectivity
towards a remote destination
what’s going on?
r4:~# ping 100.1.2.1
connect: Network is unreachable
r4:~# █
r4

## Slide 13: examining the kernel routing table
since no routing daemon is currently running, only directly connected destinations are known to the router
root@r4:/# route
Kernel IP routing table
Destination Gateway Genmask Flags Metric Ref Use Iface
100.1.0.12 0.0.0.0 255.255.255.252 U 0 0 0 eth3
100.1.0.16 0.0.0.0 255.255.255.252 U 0 0 0 eth2
100.1.4.0 0.0.0.0 255.255.255.0 U 0 0 0 eth1
100.2.0.0 0.0.0.0 255.255.255.252 U 0 0 0 eth0
root@r4:/#
r4

## Slide 14: starting the routing daemons
on each router (but r5) issue the following command:
r4:~# /etc/init.d/frr start
[ ok ] Started watchfrr.
r4:~# █
*

## Slide 15: checking connectivity (again)
towards a remote destination
after a while, all remote destinations are reachable
r4:~# ping 100.1.2.1
PING 100.1.2.1 (100.1.2.1) 56(84) bytes of data.
64 bytes from 100.1.2.1: icmp_seq=1 ttl=63 time=0.743 ms
64 bytes from 100.1.2.1: icmp_seq=2 ttl=63 time=0.875 ms
64 bytes from 100.1.2.1: icmp_seq=3 ttl=63 time=0.685 ms
--- 100.1.2.1 ping statistics ---
3 packets transmitted, 3 received, 0% packet loss, time 2005ms
rtt min/avg/max/mdev = 0.685/0.767/0.875/0.085 ms
r4:~# █
r4

## Slide 16: checking the routing table
the routing table is now updated
root@r4:/# route
Kernel IP routing table
Destination Gateway Genmask Flags Metric Ref Use Iface
100.1.0.0 100.1.0.13 255.255.255.252 UG 20 0 0 eth3
100.1.0.4 100.1.0.17 255.255.255.252 UG 20 0 0 eth2
100.1.0.8 100.1.0.17 255.255.255.252 UG 20 0 0 eth2
100.1.0.12 0.0.0.0 255.255.255.252 U 0 0 0 eth3
100.1.0.16 0.0.0.0 255.255.255.252 U 0 0 0 eth2
100.1.1.0 100.1.0.13 255.255.255.0 UG 20 0 0 eth3
100.1.2.0 100.1.0.17 255.255.255.0 UG 20 0 0 eth2
100.1.3.0 100.1.0.17 255.255.255.0 UG 20 0 0 eth2
100.1.4.0 0.0.0.0 255.255.255.0 U 0 0 0 eth1
100.2.0.0 0.0.0.0 255.255.255.252 U 0 0 0 eth0
root@r4:/#
r4

## Slide 17: a look at ripv2 packets
let’s sniff ripv2 packets
r4:~# tcpdump -i eth2 -v -n -s 1518 █
r4
display packet details
(enable full protocol decoding)
don’t resolve numbers to names
sniff entire ethernet packets (by default, only the first 68 bytes are captured)

## Slide 18: a look at ripv2 packets
let’s sniff ripv2 packets
r4:~# tcpdump -i eth2 -v -n -s 1518
tcpdump: listening on eth2, link-type EN10MB (Ethernet), capture size 1518 bytes
16:47:48.333986 IP (tos 0x0, ttl 1, id 0, offset 0, flags [DF], length: 152) 100.1.0.17.520 > 224.0.0.9.520: [udp sum ok]
RIPv2, Response, length: 124, routes: 6
AFI: IPv4: 100.1.0.0/30, tag 0x0000, metric: 2, next-hop: self
AFI: IPv4: 100.1.0.4/30, tag 0x0000, metric: 1, next-hop: self
AFI: IPv4: 100.1.0.8/30, tag 0x0000, metric: 1, next-hop: self
AFI: IPv4: 100.1.1.0/24, tag 0x0000, metric: 2, next-hop: self
AFI: IPv4: 100.1.2.0/24, tag 0x0000, metric: 2, next-hop: self
AFI: IPv4: 100.1.3.0/24, tag 0x0000, metric: 1, next-hop: self
1 packets captured
1 packets received by filter
0 packets dropped by kernel
r4:~# █
r4

## Slide 19: a traceroute
last update: Sept 2018
kathara – [ lab: rip ]
r5
eth2
18
r4
eth0
6
r1
r3
eth2
1
B
100.1.2.0/24
r2
eth2
17
F
I
eth1
5
100.1.0.4/30
100.1.0.16/30
r4:~# traceroute 100.1.2.1
traceroute to 100.1.2.1 (100.1.2.1), 64 hops max, 40 byte packets
1 100.1.0.17 (100.1.0.17) 10 ms 3 ms 1 ms
2 100.1.2.1 (100.1.2.1) 15 ms 1 ms 1 ms
r4:~# █
r4
© Computer Networks Research Group Roma Tre

## Slide 20: inspecting the rip routing table
kathara – [ lab: rip ]
root@r4:/# vtysh
r4-frr# show ip rip
Codes: R - RIP, C - connected, S - Static, O - OSPF, B - BGP
Sub-codes:
(n) - normal, (s) - static, (d) - default, (r) - redistribute,
(i) - interface
Network Next Hop Metric From Tag Time
R(n) 100.1.0.0/30 100.1.0.13 2 100.1.0.13 0 02:47
R(n) 100.1.0.4/30 100.1.0.17 2 100.1.0.17 0 02:37
R(n) 100.1.0.8/30 100.1.0.17 2 100.1.0.17 0 02:37
C(i) 100.1.0.12/30 0.0.0.0 1 self 0
C(i) 100.1.0.16/30 0.0.0.0 1 self 0
R(n) 100.1.1.0/24 100.1.0.13 2 100.1.0.13 0 02:47
R(n) 100.1.2.0/24 100.1.0.17 3 100.1.0.17 0 02:37
R(n) 100.1.3.0/24 100.1.0.17 2 100.1.0.17 0 02:37
C(r) 100.1.4.0/24 0.0.0.0 1 self 0
C(r) 100.2.0.0/30 0.0.0.0 1 self 0
r4-frr#
r4

## Slide 21: static routing
our network is a stub network (i.e., it has just one connection to an external router, r5); hence, static routes are enough for connecting it to the internet
r4
r1
r3
r2
inbound traffic
(to 100.1.0.0/16)
r5
outbound traffic
(to 0.0.0.0/0)

## Slide 22: adding a static route to r5
r5:~# route add -net 100.1.0.0/16 gw 100.2.0.1
r5:~# ping 100.1.2.1
PING 100.1.2.1 (100.1.2.1) 56(84) bytes of data.
64 bytes from 100.1.2.1: icmp_seq=1 ttl=62 time=24.1 ms
64 bytes from 100.1.2.1: icmp_seq=2 ttl=62 time=1.11 ms
--- 100.1.2.1 ping statistics ---
2 packets transmitted, 2 received, 0% packet loss, time 1023ms
rtt min/avg/max/mdev = 1.117/12.634/24.151/11.517 ms
r5:~# █
r5

## Slide 23: checking connectivity
last update: Sept 2018
kathara – [ lab: rip ]
r5
eth0
1
eth0
2
L
eth2
18
r4
eth0
6
r1
r3
eth2
1
B
100.1.2.0/24
100.2.0.0/30
r2
eth2
17
F
I
eth3
1
eth1
5
100.1.0.4/30
100.1.0.16/30
r5:~# traceroute 100.1.2.1
traceroute to 100.1.2.1 (100.1.2.1), 64 hops max, 40 byte packets
1 100.2.0.1 (100.2.0.1) 75 ms 1 ms 2 ms
2 100.1.0.17 (100.1.0.17) 7 ms 1 ms 1 ms
3 100.1.2.1 (100.1.2.1) 24 ms 3 ms 1 ms
r5:~# █
r5
© Computer Networks Research Group Roma Tre

## Slide 24: configuring r4
step 1: configuring the default route
r4:~# route add default gw 100.2.0.2
root@r4:/# route
Kernel IP routing table
Destination Gateway Genmask Flags Metric Ref Use Iface
default 100.2.0.2 0.0.0.0 UG 0 0 0 eth0
100.1.0.0 100.1.0.13 255.255.255.252 UG 20 0 0 eth3
100.1.0.4 100.1.0.17 255.255.255.252 UG 20 0 0 eth2
100.1.0.8 100.1.0.17 255.255.255.252 UG 20 0 0 eth2
100.1.0.12 0.0.0.0 255.255.255.252 U 0 0 0 eth3
100.1.0.16 0.0.0.0 255.255.255.252 U 0 0 0 eth2
100.1.1.0 100.1.0.13 255.255.255.0 UG 20 0 0 eth3
100.1.2.0 100.1.0.17 255.255.255.0 UG 20 0 0 eth2
100.1.3.0 100.1.0.17 255.255.255.0 UG 20 0 0 eth2
100.1.4.0 0.0.0.0 255.255.255.0 U 0 0 0 eth1
100.2.0.0 0.0.0.0 255.255.255.252 U 0 0 0 eth0
root@r4:/#
r4

## Slide 25: configuring r4
step 2: propagating the default route into rip
last update: Sept 2018
kathara – [ lab: rip ]
root@r4:/# vtysh
Hello, this is FRRouting (version 8.0.1).
Copyright 1996-2005 Kunihiro Ishiguro, et al.
r4-frr# configure terminal
r4-frr(config)# router rip
r4-frr(config-router)# route 0.0.0.0/0
r4-frr(config-router)# quit
r4-frr(config)# quit
r4-frr# disable
r4-frr> exit
root@r4:/#
r4
begin configuration
configure the rip protocol
statically configure the default route
end of rip configuration
end configuration
abandon privileges
© Computer Networks Research Group Roma Tre

## Slide 26: the default route
after a while, the default route has been injected (via rip) into the network
kathara – [ lab: rip ]
root@r1:/etc/frr# route
Kernel IP routing table
Destination Gateway Genmask Flags Metric Ref Use Iface
default 100.1.0.14 0.0.0.0 UG 20 0 0 eth0
100.1.0.0 0.0.0.0 255.255.255.252 U 0 0 0 eth2
100.1.0.4 100.1.0.2 255.255.255.252 UG 20 0 0 eth2
100.1.0.8 0.0.0.0 255.255.255.252 U 0 0 0 eth1
100.1.0.12 0.0.0.0 255.255.255.252 U 0 0 0 eth0
100.1.0.16 100.1.0.10 255.255.255.252 UG 20 0 0 eth1
100.1.1.0 0.0.0.0 255.255.255.0 U 0 0 0 eth3
100.1.2.0 100.1.0.2 255.255.255.0 UG 20 0 0 eth2
100.1.3.0 100.1.0.10 255.255.255.0 UG 20 0 0 eth1
100.1.4.0 100.1.0.14 255.255.255.0 UG 20 0 0 eth0
100.2.0.0 100.1.0.14 255.255.255.252 UG 20 0 0 eth0
root@r1:/etc/frr#
r1

## Slide 27: checking connectivity
kathara – [ lab: rip ]
r5
eth0
1
eth0
2
L
r4
eth3
14
r1
H
100.1.0.12/30
100.2.0.0/30
eth0
13
towards any unknown destination
r1:~# ping 193.204.161.1
PING 193.204.161.1 (193.204.161.1) 56(84) bytes of data.
From 100.2.0.2 icmp_seq=1 Destination Net Unreachable
From 100.2.0.2 icmp_seq=2 Destination Net Unreachable
--- 193.204.161.1 ping statistics ---
2 packets transmitted, 0 received, +2 errors, 100% packet loss, time 999ms
r1:~# █
r1
any (even non-existing) destination
© Computer Networks Research Group Roma Tre

## Slide 28: checking connectivity
r5 is actually receiving echo request packets
kathara – [ lab: rip ]
r5:~# tcpdump -i eth0 -n -s 1518
tcpdump: verbose output suppressed, use -v or -vv for full protocol decode
listening on eth0, link-type EN10MB (Ethernet), capture size 1518 bytes
11:38:43.822503 arp who-has 100.2.0.2 tell 100.2.0.1
11:38:43.824221 arp reply 100.2.0.2 is-at fe:fd:64:02:00:02
11:38:43.825890 IP 100.1.0.13 > 193.204.161.1: icmp 64: echo request seq 1
11:38:43.827139 IP 100.2.0.2 > 100.1.0.13: icmp 92: net 193.204.161.1 unreachable
11:38:44.841566 IP 100.1.0.13 > 193.204.161.1: icmp 64: echo request seq 2
11:38:44.841651 IP 100.2.0.2 > 100.1.0.13: icmp 92: net 193.204.161.1 unreachable
6 packets captured
6 packets received by filter
0 packets dropped by kernel
r5:~# █
r5

## Slide 29: shutting down an interface
kathara – [ lab: rip ]
r5
r4
eth1
9
eth1
10
r1
r3
r2
G
r1:~# traceroute 100.1.0.10
traceroute to 100.1.0.10 (100.1.0.10), 64 hops max, 40 byte packets
1 100.1.0.10 (100.1.0.10) 24 ms 1 ms 1 ms
r1:~# ifconfig eth1 down █
r1
100.1.0.8/30

## Slide 30: shutting down an interface
kathara – [ lab: rip ]
r5
eth2
18
r4
eth3
14
eth1
9
eth2
1
eth1
10
r1
r3
H
100.1.0.12/30
r2
eth2
17
eth0
13
G
I
100.1.0.16/30
100.1.0.8/30
r1:~# traceroute 100.1.0.10
traceroute to 100.1.0.10 (100.1.0.10), 64 hops max, 40 byte packets
1 100.1.0.14 (100.1.0.14) 1 ms 1 ms 1 ms
2 * * *
3 * * * █
r1
r1 attempts forwarding the packet using the default route
?

## Slide 31: shutting down an interface
kathara – [ lab: rip ]
r5
eth2
18
r4
eth3
14
eth1
9
eth2
1
eth1
10
r1
r3
H
100.1.0.12/30
r2
eth2
17
eth0
13
G
I
100.1.0.16/30
100.1.0.8/30
r1:~# traceroute 100.1.0.10
traceroute to 100.1.0.10 (100.1.0.10), 64 hops max, 40 byte packets
1 100.1.0.14 (100.1.0.14) 1 ms 1 ms 1 ms
2 100.1.0.10 (100.1.0.10) 5 ms 2 ms 1 ms
r1:~# █
r1
after a while, routing information has been updated

## Slide 32: shutting down an interface
r1’s routing table has been updated
r1:~# route
Kernel IP routing table
Destination Gateway Genmask Flags Metric Ref Use Iface
100.1.0.16 100.1.0.14 255.255.255.252 UG 2 0 0 eth0
100.1.0.0 * 255.255.255.252 U 0 0 0 eth2
100.2.0.0 100.1.0.14 255.255.255.252 UG 2 0 0 eth0
100.1.0.4 100.1.0.2 255.255.255.252 UG 2 0 0 eth2
100.1.0.8 100.1.0.14 255.255.255.252 UG 3 0 0 eth0
100.1.0.12 * 255.255.255.252 U 0 0 0 eth0
100.1.4.0 100.1.0.14 255.255.255.0 UG 2 0 0 eth0
100.1.2.0 100.1.0.2 255.255.255.0 UG 2 0 0 eth2
100.1.3.0 100.1.0.14 255.255.255.0 UG 3 0 0 eth0
100.1.1.0 * 255.255.255.0 U 0 0 0 eth3
default 100.1.0.14 0.0.0.0 UG 2 0 0 eth0
r1:~# █
r1