## Slide 1: kathara lab
dns
Version | 2.0
Author(s) | L. Ariemma, G. Di Battista, M. Patrignani, M. Pizzonia, F. Ricci, M. Rimondini
E-mail | contact@kathara.org
Web | http://www.kathara.org/
Description | using the domain name system – kathara version of an existing netkit lab

## Slide 2: copyright notice
All the pages/slides in this presentation, including but not limited to, images, photos, animations, videos, sounds, music, and text (hereby referred to as “material”) are protected by copyright.
This material, with the exception of some multimedia elements licensed by other organizations, is property of the authors and/or organizations appearing in the first slide.
This material, or its parts, can be reproduced and used for didactical purposes within universities and schools, provided that this happens for non-profit purposes.
Information contained in this material cannot be used within network design projects or other products of any kind.
Any other use is prohibited, unless explicitly authorized by the authors on the basis of an explicit agreement.
The authors assume no responsibility about this material and provide this material “as is”, with no implicit or explicit warranty about the correctness and completeness of its contents, which may be subject to changes.
This copyright notice must always be redistributed together with the material, or its portions.

## Slide 3: about the dns
takes care of associating names with ip addresses
the name system is distributed over several nodes (hosts) that are hierarchically organized to form a tree
each node in the hierarchy corresponds to a name
a domain in the name system is a subtree
a node in the hierarchy may be delegated to handle names for a particular zone
  such a node is an authoritative server for that zone
a zone is a domain which is devoid of those nodes having a different authoritative server (i.e., a tree without subtrees)

## Slide 4: the dns name hierarchy
each node corresponds
to a name
pc1
pc2
lugroma3
nanoinside
org
net
“”
dnsroot
dnsorg
dnslug
dnsnano
dnsnet
this node is nanoinside.net
this node is pc1.lugroma3.org

## Slide 5: the dns name hierarchy
leaves always correspond to real hosts
dnslug
lugroma3
nanoinside
org
net
“”
pc1
pc2
intermediate nodes may correspond to real hosts (in this example they do not)
dnsorg
dnsroot
dnsnet
dnsnano

## Slide 6: domains
lugroma3
org
pc1
net domain
nanoinside.net domain
“”
nanoinside
net
pc2
dnslug
dnsorg
dnsroot
dnsnet
dnsnano
domains are subtrees
  their name is the name of the root node
  every node (including leaves) defines a domain
  domains do overlap

## Slide 7: zones
a zone is a domain without the delegated subdomains
lugroma3
nanoinside
org
net
“”
pc1
pc2
zones cannot overlap
  each node falls into a single zone
dnslug
dnsorg
dnsroot
dnsnet
dnsnano

## Slide 8: zones
zones have name servers
  they are not constrained to be inside the zone they serve
last update: Nov 2018
kathara – [ lab: dns ]
lugroma3
nanoinside
org
net
“”
pc1
pc2
served by dnsroot
served by
dnsorg.org
served by
dnsnet.net
served by dnslug.lugroma3.org
served by dnsnano.nanoinside.net
dnslug
NS
dnsorg
NS
dnsroot
NS
dnsnet
NS
dnsnano
NS
© Computer Networks Research Group Roma Tre

## Slide 9: more about the dns
the dns hierarchy is orthogonal with respect to the actual network topology
in order to focus on the behavior of the dns we choose a flat topology, consisting of a single collision domain

## Slide 10: step 1 – network topology
192.168.0.0/24
pc1
pc2
.2
dnslug
dnsnano
dnsorg
dnsnet
dnsroot
.5
.22
.222
.1
.11
.111
abc
machine name

## Slide 11: step 1 – dns (zone) hierarchy
pc1
pc2
lugroma3
org
net
“”
served by
dnsroot
served by
dnsorg.org
served by
dnsnet.net
served by
dnslug.lugroma3.org
served by
dnsnano.nanoinside.net
domain name
abc
nanoinside

## Slide 12: step 2 – starting the lab
the lab is configured to
  start all the 7 vms
  automatically configure the network interfaces
  automatically configure the name servers
  automatically start the name server software (bind) on each name server

## Slide 13: step 2 – exploring the configuration
root@pc1:~$ cat /etc/resolv.conf
nameserver 192.168.0.11
search lugroma3.org
root@pc2:~$ cat /etc/resolv.conf
nameserver 192.168.0.22
search nanoinside.net
configuration on the pcs consists of the specification of the default name server
dnslug.lugroma3.org
suffix to append to unqualified names (e.g. asking to resolve dummy results in querying for dummy.lugroma3.org)
dnsnano.nanoinside.net

## Slide 14: step 2 – exploring the configuration
configuration on the name servers specifies
  associations between zones and name servers
  information about the root name servers
  authoritative information
  associations between names and IP addresses

## Slide 15: step 2 – exploring the configuration
root@dnslug:~$ cat /etc/bind/named.conf
include "/etc/bind/named.conf.options";
zone "." {
type hint;
file "/etc/bind/db.root";
};
zone "lugroma3.org" {
type master;
file "/etc/bind/db.org.lugroma3";
};
configuration on the name servers specifies
  associations between zones and name servers
kathara – [ lab: dns ]
where to find information about the root name server
we are the primary master for zone lugroma3.org
where to find data about the names in this zone
include some additional configuration

## Slide 16: step 2 – exploring the configuration
configuration on the name servers specifies
  additional configuration
root@dnsorg:~$ cat /etc/bind/named.conf.options
options {
directory "/var/cache/bind";
};
use this folder to store the cache.
COMPULSORY, otherwise, bind wont ‘t start

## Slide 17: step 2 – exploring the configuration
configuration on the name servers specifies
  allowing recursive queries
root@dnslug:~$ cat /etc/bind/named.conf.options
options {
directory "/var/cache/bind";
allow-recursion { 192.168.0.0/24; };
dnssec-validation no;
};
allow recursive queries from 192.168.0.0/24
do not validate DNSSEC over the recursive queries

## Slide 18: format of a resource record
<domain> <class> <type> <rdata>
domain: the record owner (=domain to which the record refers)
class: usually IN (=Internet system); may be HS (=hesiod) or CH (=chaos)
type: see next slide...
rdata: record data (depends on the record type)

## Slide 19: step 2 – exploring the configuration
last update: Nov 2018
kathara – [ lab: dns ]
available record types
A a host address.
A6 an IPv6 address.
AAAA Obsolete format of IPv6 address
AFSDB (x) location of AFS database servers. Experimental.
CERT holds a digital certificate.
CNAME identifies the canonical name of an alias.
DNAME for delegation of reverse addresses. Replaces the domain name specified with
another name to be looked up. Described in RFC 2672.
GPOS Specifies the global position. Superseded by LOC.
HINFO identifies the CPU and OS used by a host.
ISDN (x) representation of ISDN addresses. Experimental.
KEY stores a public key associated with a DNS name.
KX identifies a key exchanger for this DNS name.
LOC (x) for storing GPS info. See RFC 1876. Experimental.
MX identifies a mail exchange for the domain. See RFC 974 for details.
NAPTR name authority pointer.
NSAP a network service access point.
NS the authoritative nameserver for the domain.
NXT used in DNSSEC to securely indicate that RRs with an owner name in a certain
name interval do not exist in a zone and indicate what R
PTR a pointer to another part of the domain name space.
PX provides mappings between RFC 822 and X.400 addresses.
RP (x) information on persons responsible for the domain. Experimental.
RT (x) route-through binding for hosts that do not have their own direct wide area
network addresses. Experimental.
SIG ("signature") contains data authenticated in the secure DNS. See RFC 2535 for
details.
SOA identifies the start of a zone of authority.
SRV information about well known network services (replaces WKS).
TXT text records.
WKS (h) information about which well known network services, such as SMTP, that a
domain supports. Historical, replaced by newer RR SRV.
X25 (x) representation of X.25 network addresses. Experimental
© Computer Networks Research Group Roma Tre

## Slide 20: step 2 – exploring the configuration
configuration on the name servers specifies
  information about the root name servers
kathara – [ lab: dns ]
root@dnslug:~$ cat /etc/bind/db.root
. IN NS ROOT-SERVER.
ROOT-SERVER. IN A 192.168.0.5
a resource record

## Slide 21: step 2 – exploring the configuration
configuration on the name servers specifies
  authoritative information
root@dnslug:~$ cat /etc/bind/db.org.lugroma3
$TTL 60000
time to live, in seconds (determines how long a resource record should be cached)

## Slide 22: step 2 – exploring the configuration
configuration on the name servers specifies
  authoritative information
root@dnslug:~$ cat /etc/bind/db.org.lugroma3
$TTL 60000
@ IN SOA dnslug.lugroma3.org. root.dnslug.lugroma3.org. (
2006031201 ; serial
28 ; refresh
14 ; retry
3600000 ; expire
0 ; negative cache ttl
)
Start of Authority record
must be all on a single line; line breaks can only be introduced when using parentheses
a zone data file can contain only one SOA record

## Slide 23: step 2 – exploring the configuration
configuration on the name servers specifies
  authoritative information
root@dnslug:~$ cat /etc/bind/db.org.lugroma3
$TTL 60000
@ IN SOA dnslug.lugroma3.org. root.dnslug.lugroma3.org. (
2006031201 ; serial
28 ; refresh
14 ; retry
3600000 ; expire
0 ; negative cache ttl
)
this record is referred to the current origin (lugroma3.org)
all domain names in this data file that are not fully qualified (do not end with a ‘.’) are relative to the origin
the origin is the domain name in the zone statement of the server configuration file:
  zone "lugroma3.org" {
  type master;
  file "/etc/bind/db.org.lugroma3";
  };

## Slide 24: step 2 – exploring the configuration
configuration on the name servers specifies
  authoritative information
root@dnslug:~$ cat /etc/bind/db.org.lugroma3
$TTL 60000
@ IN SOA dnslug.lugroma3.org. root.dnslug.lugroma3.org. (
2006031201 ; serial
28 ; refresh
14 ; retry
3600000 ; expire
0 ; negative cache ttl
)
primary master (=authority) server for this zone (dnslug.lugroma3.org);
don’t forget the trailing dot, or the origin name (lugroma3.org) would be appended!

## Slide 25: step 2 – exploring the configuration
configuration on the name servers specifies
  authoritative information
root@dnslug:~$ cat /etc/bind/db.org.lugroma3
$TTL 60000
@ IN SOA dnslug.lugroma3.org. root.dnslug.lugroma3.org. (
2006031201 ; serial
28 ; refresh
14 ; retry
3600000 ; expire
0 ; negative cache ttl
)
mail address of the person that is responsible for the zone
(root@dnslug.lugroma3.org)
the first ‘.’ must be replaced by a ‘@’
only meant to be used by humans; has no use within the dns service

## Slide 26: step 2 – exploring the configuration
configuration on the name servers specifies
  authoritative information
root@dnslug:~$ cat /etc/bind/db.org.lugroma3
$TTL 60000
@ IN SOA dnslug.lugroma3.org. root.dnslug.lugroma3.org. (
2006031201 ; serial
28 ; refresh
14 ; retry
3600000 ; expire
0 ; negative cache ttl
)
make sense for master/slave server configurations

## Slide 27: step 2 – exploring the configuration
configuration on the name servers specifies
  authoritative information
root@dnslug:~$ cat /etc/bind/db.org.lugroma3
$TTL 60000
@ IN SOA dnslug.lugroma3.org. root.dnslug.lugroma3.org. (
2006031201 ; serial
28 ; refresh
14 ; retry
3600000 ; expire
0 ; negative cache ttl
)
serial number
determines how recent the information is
influences all data within the zone
conventional format: YYYYMMDDNN (year, month, day, # of changes within that day)

## Slide 28: step 2 – exploring the configuration
configuration on the name servers specifies
  authoritative information
root@dnslug:~$ cat /etc/bind/db.org.lugroma3
$TTL 60000
@ IN SOA dnslug.lugroma3.org. root.dnslug.lugroma3.org. (
2006031201 ; serial
28 ; refresh
14 ; retry
3600000 ; expire
0 ; negative cache ttl
)
refresh interval
(seconds)
tells a slave how often to check that the data for this zone is up to date

## Slide 29: step 2 – exploring the configuration
configuration on the name servers specifies
  authoritative information
root@dnslug:~$ cat /etc/bind/db.org.lugroma3
$TTL 60000
@ IN SOA dnslug.lugroma3.org. root.dnslug.lugroma3.org. (
2006031201 ; serial
28 ; refresh
14 ; retry
3600000 ; expire
0 ; negative cache ttl
)
interval (seconds) between subsequent attempts to contact the master

## Slide 30: step 2 – exploring the configuration
configuration on the name servers specifies
  authoritative information
root@dnslug:~$ cat /etc/bind/db.org.lugroma3
$TTL 60000
@ IN SOA dnslug.lugroma3.org. root.dnslug.lugroma3.org. (
2006031201 ; serial
28 ; refresh
14 ; retry
3600000 ; expire
0 ; negative cache ttl
)
slave expire time
(seconds)
if the slave fails to contact the master for this amount of time, it considers the zone data too old and stops giving answers about it

## Slide 31: step 2 – exploring the configuration
configuration on the name servers specifies
  authoritative information
root@dnslug:~$ cat /etc/bind/db.org.lugroma3
$TTL 60000
@ IN SOA dnslug.lugroma3.org. root.dnslug.lugroma3.org. (
2006031201 ; serial
28 ; refresh
14 ; retry
3600000 ; expire
0 ; negative cache ttl
)
ttl for negative responses from authoritative name servers

## Slide 32: step 2 – exploring the configuration
configuration on the name servers specifies
  associations between names and ip addresses
root@dnslug:~$ cat /etc/bind/db.org.lugroma3
$TTL 60000
@ IN SOA dnslug.lugroma3.org. root.dnslug.lugroma3.org. (
2006031201 ; serial
28 ; refresh
14 ; retry
3600000 ; expire
0 ; negative cache ttl
)
@ IN NS dnslug.lugroma3.org.
dnslug IN A 192.168.0.11
pc1 IN A 192.168.0.111
record type NS
(name server)
the authoritative name server for this zone (lugroma3.org) is dnslug.lugroma3.org

## Slide 33: step 2 – exploring the configuration
configuration on the name servers specifies
  associations between names and ip addresses
root@dnslug:~$ cat /etc/bind/db.org.lugroma3
$TTL 60000
@ IN SOA dnslug.lugroma3.org. root.dnslug.lugroma3.org. (
2006031201 ; serial
28 ; refresh
14 ; retry
3600000 ; expire
0 ; negative cache ttl
)
@ IN NS dnslug.lugroma3.org.
dnslug IN A 192.168.0.11
pc1 IN A 192.168.0.111
two machines in this zone:
dnslug.lugroma3.org
pc1.lugroma3.org
(the origin name is automatically appended)
record type A
(address)

## Slide 34: step 2 – exploring the configuration
configuration on the name servers specifies
  associations between names and ip addresses
root@dnsorg:~$ tail –n 5 /etc/bind/db.org
@ IN NS dnsorg.org.
dnsorg IN A 192.168.0.1
lugroma3 IN NS dnslug.lugroma3.org.
dnslug.lugroma3 IN A 192.168.0.11
dnsorg.org is the authority for this zone (org)
dnslug.lugroma3.org is the authority for zone lugroma3(.org)

## Slide 35: step 3 – experiment setting
kathara – [ lab: dns ]
.222
pc1
pc2
.2
dnslug
dnsnano
dnsorg
dnsnet
.5
.22
.1
.11
.111
dnsroot
root@pc1:~$ ping pc2.nanoinside.net
root@pc2:~$ tcpdump –tnni eth0 port 53

## Slide 36: step 3 – the sniffer output
root@pc2:~$ tcpdump –tnni eth0 port 53
no need to view MAC Addresses, so no “e” option specified
capture packets to/from 53

## Slide 37: step 3 – the sniffer output
root@pc2:~$ tcpdump –tnni eth0 port 53
IP 192.168.0.111.45446 > 192.168.0.11.53: 42909+ A? pc2.nanoinside.net. (36)
IP 192.168.0.111.45446 > 192.168.0.11.53: 10901+ AAAA? pc2.nanoinside.net. (36)
IP 192.168.0.11.43013 > 192.168.0.5.53: 37549 [1au] NS? . (40)
IP 192.168.0.11.45845 > 192.168.0.5.53: 49303% [1au] NS? net. (44)
IP 192.168.0.5.53 > 192.168.0.11.43013: 37549* 1/0/1 NS ROOT-SERVER. (80)
IP 192.168.0.5.53 > 192.168.0.11.45845: 49303 0/1/2 (97)
IP 192.168.0.11.52887 > 192.168.0.5.53: 15232% [1au] AAAA? dnsnet.net. (67)
IP 192.168.0.5.53 > 192.168.0.11.52887: 15232 0/1/2 (97)
IP 192.168.0.11.36506 > 192.168.0.2.53: 54346% [1au] NS? nanoinside.net. (55)
IP 192.168.0.11.58879 > 192.168.0.2.53: 33932% [1au] AAAA? dnsnet.net. (51)
IP 192.168.0.2.53 > 192.168.0.11.58879: 33932* 0/1/1 (108)
IP 192.168.0.2.53 > 192.168.0.11.36506: 54346 0/1/2 (109)
IP 192.168.0.11.35324 > 192.168.0.5.53: 59471% [1au] AAAA? dnsnano.nanoinside.net. (79)
IP 192.168.0.5.53 > 192.168.0.11.35324: 59471 0/1/2 (119)
IP 192.168.0.11.41035 > 192.168.0.22.53: 15656% [1au] A? pc2.nanoinside.net. (59)
IP 192.168.0.11.48612 > 192.168.0.22.53: 10092% [1au] AAAA? pc2.nanoinside.net. (59)
IP 192.168.0.11.59707 > 192.168.0.2.53: 29359% [1au] AAAA? dnsnano.nanoinside.net. (79)
IP 192.168.0.2.53 > 192.168.0.11.59707: 29359 0/1/2 (109)
IP 192.168.0.22.53 > 192.168.0.11.48612: 10092* 0/1/1 (124)
IP 192.168.0.22.53 > 192.168.0.11.41035: 15656* 1/1/2 A 192.168.0.222 (129)

## Slide 38: step 3 – the sniffer output
root@pc2:~$ tcpdump –tnni eth0 port 53
IP 192.168.0.111.45446 > 192.168.0.11.53: 42909+ A? pc2.nanoinside.net. (36)
IP 192.168.0.11.43013 > 192.168.0.5.53: 37549 [1au] NS? . (40)
IP 192.168.0.11.45845 > 192.168.0.5.53: 49303% [1au] NS? net. (44)
IP 192.168.0.5.53 > 192.168.0.11.43013: 37549* 1/0/1 NS ROOT-SERVER. (80)
IP 192.168.0.5.53 > 192.168.0.11.45845: 49303 0/1/2 (97)
IP 192.168.0.5.53 > 192.168.0.11.52887: 15232 0/1/2 (97)
IP 192.168.0.11.36506 > 192.168.0.2.53: 54346% [1au] NS? nanoinside.net. (55)
IP 192.168.0.2.53 > 192.168.0.11.58879: 33932* 0/1/1 (108)
IP 192.168.0.2.53 > 192.168.0.11.36506: 54346 0/1/2 (109)
IP 192.168.0.5.53 > 192.168.0.11.35324: 59471 0/1/2 (119)
IP 192.168.0.11.41035 > 192.168.0.22.53: 15656% [1au] A? pc2.nanoinside.net. (59)
IP 192.168.0.2.53 > 192.168.0.11.59707: 29359 0/1/2 (109)
IP 192.168.0.22.53 > 192.168.0.11.48612: 10092* 0/1/1 (124)
IP 192.168.0.22.53 > 192.168.0.11.41035: 15656* 1/1/2 A 192.168.0.222 (129)
query
answer

## Slide 39: step 3 – the sniffer output
root@pc2:~$ tcpdump –tnni eth0 port 53
IP 192.168.0.111.45446 > 192.168.0.11.53: 42909+ A? pc2.nanoinside.net. (36)
query
answer
query id
(+=recursion desired)
query type
(address)
query value
packet size
(not including UDP and IP headers)

## Slide 40: step 3 – the sniffer output
root@pc2:~$ tcpdump –tnni eth0 port 53
IP 192.168.0.111.45446 > 192.168.0.11.53: 42909+ A? pc2.nanoinside.net. (36)
IP 192.168.0.11.43013 > 192.168.0.5.53: 37549 [1au] NS? . (40)
query
answer
dnslug.lugroma3.org
(192.168.0.11)
asks the root server
(192.168.0.5)
the query carries an additional record for authentication purposes (DNSSEC)

## Slide 41: step 3 – the sniffer output
root@pc2:~$ tcpdump –tnni eth0 port 53
IP 192.168.0.111.45446 > 192.168.0.11.53: 42909+ A? pc2.nanoinside.net. (36)
IP 192.168.0.11.43013 > 192.168.0.5.53: 37549 [1au] NS? . (40)
IP 192.168.0.11.45845 > 192.168.0.5.53: 49303% [1au] NS? net. (44)
query
answer
The % symbol in a DNS query indicates that the DNS query is a non-recursive query

## Slide 42: step 3 – the sniffer output
root@pc2:~$ tcpdump –tnni eth0 port 53
IP 192.168.0.111.45446 > 192.168.0.11.53: 42909+ A? pc2.nanoinside.net. (36)
IP 192.168.0.11.43013 > 192.168.0.5.53: 37549 [1au] NS? . (40)
IP 192.168.0.11.45845 > 192.168.0.5.53: 49303% [1au] NS? net. (44)
IP 192.168.0.5.53 > 192.168.0.11.43013: 37549* 1/0/1 NS ROOT-SERVER. (80)
query
answer
the root server (192.168.0.5) answers with:
1 answer in this reply
0 authoritative nameservers provided
1 additional record

## Slide 43: step 3 – the sniffer output
root@pc2:~$ tcpdump –tnni eth0 port 53
IP 192.168.0.111.45446 > 192.168.0.11.53: 42909+ A? pc2.nanoinside.net. (36)
IP 192.168.0.11.43013 > 192.168.0.5.53: 37549 [1au] NS? . (40)
IP 192.168.0.11.45845 > 192.168.0.5.53: 49303% [1au] NS? net. (44)
IP 192.168.0.5.53 > 192.168.0.11.43013: 37549* 1/0/1 NS ROOT-SERVER. (80)
IP 192.168.0.5.53 > 192.168.0.11.45845: 49303 0/1/2 (97)
query
answer
the root server (192.168.0.5) answers with:
0 answers
1 authority (=name server) record (dnsnet.net)
2 additional records (dnsnet.net’s IP address 192.168.0.2, and an OPT record)

## Slide 44: step 3 – the sniffer output
pc2:~# tcpdump –n –t port domain
tcpdump: verbose output suppressed, use -v or -vv for full protocol decode
listening on eth0, link-type EN10MB (Ethernet), capture size 96 bytes
IP 192.168.0.111.3072 > 192.168.0.11.53:
29753+ A? pc2.nanoinside.net. (36)
IP 192.168.0.11.3073 > 192.168.0.5.53:
18164 [1au] A? pc2.nanoinside.net. (47)
IP 192.168.0.5.53 > 192.168.0.11.3073:
18164 0/1/2 (84)
IP 192.168.0.11.3073 > 192.168.0.2.53:
19071 [1au] A? pc2.nanoinside.net. (47)
█
pc2
query
answer
dnslug.lugroma3.org
(192.168.0.11)
asks dnsnet.net
(192.168.0.2)
the query carries an additional OPT record

## Slide 45: step 3 – the sniffer output
last update: Nov 2018
kathara – [ lab: dns ]
pc2:~# tcpdump –n –t port domain
tcpdump: verbose output suppressed, use -v or -vv for full protocol decode
listening on eth0, link-type EN10MB (Ethernet), capture size 96 bytes
IP 192.168.0.111.3072 > 192.168.0.11.53:
29753+ A? pc2.nanoinside.net. (36)
IP 192.168.0.11.3073 > 192.168.0.5.53:
18164 [1au] A? pc2.nanoinside.net. (47)
IP 192.168.0.5.53 > 192.168.0.11.3073:
18164 0/1/2 (84)
IP 192.168.0.11.3073 > 192.168.0.2.53:
19071 [1au] A? pc2.nanoinside.net. (47)
IP 192.168.0.2.53 > 192.168.0.11.3073:
19071 0/1/2 (85)
█
pc2
query
answer
dnsnet.net (192.168.0.2) answers with:
0 answers
1 authority (=name server) record (dnsnano.nanoinside.net)
2 additional records (dnsnano.nanoinside.net’s IP address 192.168.0.22, and an OPT record)
© Computer Networks Research Group Roma Tre

## Slide 46: step 3 – the sniffer output
last update: Nov 2018
kathara – [ lab: dns ]
pc2:~# tcpdump –n –t port domain
tcpdump: verbose output suppressed, use -v or -vv for full protocol decode
listening on eth0, link-type EN10MB (Ethernet), capture size 96 bytes
IP 192.168.0.111.3072 > 192.168.0.11.53:
29753+ A? pc2.nanoinside.net. (36)
IP 192.168.0.11.3073 > 192.168.0.5.53:
18164 [1au] A? pc2.nanoinside.net. (47)
IP 192.168.0.5.53 > 192.168.0.11.3073:
18164 0/1/2 (84)
IP 192.168.0.11.3073 > 192.168.0.2.53:
19071 [1au] A? pc2.nanoinside.net. (47)
IP 192.168.0.2.53 > 192.168.0.11.3073:
19071 0/1/2 (85)
IP 192.168.0.11.3073 > 192.168.0.22.53:
64854 [1au] A? pc2.nanoinside.net. (47)
█
pc2
query
answer
dnslug.lugroma3.org
(192.168.0.11)
asks dnsnano.nanoinside.net
(192.168.0.22)
the query carries an additional OPT record
© Computer Networks Research Group Roma Tre

## Slide 47: step 3 – the sniffer output
pc2:~# tcpdump –n –t port domain
tcpdump: verbose output suppressed, use -v or -vv for full protocol decode
listening on eth0, link-type EN10MB (Ethernet), capture size 96 bytes
IP 192.168.0.111.3072 > 192.168.0.11.53:
29753+ A? pc2.nanoinside.net. (36)
IP 192.168.0.11.3073 > 192.168.0.5.53:
18164 [1au] A? pc2.nanoinside.net. (47)
IP 192.168.0.5.53 > 192.168.0.11.3073:
18164 0/1/2 (84)
IP 192.168.0.11.3073 > 192.168.0.2.53:
19071 [1au] A? pc2.nanoinside.net. (47)
IP 192.168.0.2.53 > 192.168.0.11.3073:
19071 0/1/2 (85)
IP 192.168.0.11.3073 > 192.168.0.22.53:
64854 [1au] A? pc2.nanoinside.net. (47)
IP 192.168.0.22.53 > 192.168.0.11.3073:
64854* 1/1/2 A 192.168.0.222 (101)
█
pc2
query
answer
dnsnano.nanoinside.net (192.168.0.22) answers with:
1 answer (pc2.nanoinside.net’s IP address 192.168.0.222)
1 authority (=name server) record (dnsnano.nanoinside.net)
2 additional records (dnsnano.nanoinside.net’s IP address 192.168.0.22, and an OPT record)

## Slide 48: step 3 – the sniffer output
pc2:~# tcpdump –n –t port domain
tcpdump: verbose output suppressed, use -v or -vv for full protocol decode
listening on eth0, link-type EN10MB (Ethernet), capture size 96 bytes
IP 192.168.0.111.3072 > 192.168.0.11.53:
29753+ A? pc2.nanoinside.net. (36)
IP 192.168.0.11.3073 > 192.168.0.5.53:
18164 [1au] A? pc2.nanoinside.net. (47)
IP 192.168.0.5.53 > 192.168.0.11.3073:
18164 0/1/2 (84)
IP 192.168.0.11.3073 > 192.168.0.2.53:
19071 [1au] A? pc2.nanoinside.net. (47)
IP 192.168.0.2.53 > 192.168.0.11.3073:
19071 0/1/2 (85)
IP 192.168.0.11.3073 > 192.168.0.22.53:
64854 [1au] A? pc2.nanoinside.net. (47)
IP 192.168.0.22.53 > 192.168.0.11.3073:
64854* 1/1/2 A 192.168.0.222 (101)
IP 192.168.0.11.53 > 192.168.0.111.3072:
29753 1/1/1 (108)
pc2
query
answer
dnslug.lugroma3.org (192.168.0.11) answers with:
1 answer (pc2.nanoinside.net’s IP address 192.168.0.222)
1 authority (=name server) record (dnsnano.nanoinside.net)
1 additional record (dnsnano.nanoinside.net’s IP address 192.168.0.22)

## Slide 49: step 3 – exchanged messages
192.168.0.0/24
pc1
pc2
.2
dnslug
dnsnano
dnsorg
dnsnet
dnsroot
.5
.22
.222
.1
.11
.111
abc
machine name

## Slide 50: step 3 – exchanged messages
192.168.0.0/24
pc1
pc2
.2
dnslug
dnsnano
dnsorg
dnsnet
dnsroot
.5
.22
.222
.1
.11
.111
abc
machine name

## Slide 51: step 3 – exchanged messages
192.168.0.0/24
pc1
pc2
.2
dnslug
dnsnano
dnsorg
dnsnet
dnsroot
.5
.22
.222
.1
.11
.111
abc
machine name

## Slide 52: step 3 – exchanged messages
192.168.0.0/24
pc1
pc2
.2
dnslug
dnsnano
dnsorg
dnsnet
dnsroot
.5
.22
.222
.1
.11
.111
abc
machine name

## Slide 53: step 3 – exchanged messages
192.168.0.0/24
pc1
pc2
.2
dnslug
dnsnano
dnsorg
dnsnet
dnsroot
.5
.22
.222
.1
.11
.111
abc
machine name

## Slide 54: step 3 – exchanged messages
192.168.0.0/24
pc1
pc2
.2
dnslug
dnsnano
dnsorg
dnsnet
dnsroot
.5
.22
.222
.1
.11
.111
abc
machine name

## Slide 55: step 3 – exchanged messages
192.168.0.0/24
pc1
pc2
.2
dnslug
dnsnano
dnsorg
dnsnet
dnsroot
.5
.22
.222
.1
.11
.111
abc
machine name

## Slide 56: step 3 – exchanged messages
192.168.0.0/24
pc1
pc2
.2
dnslug
dnsnano
dnsorg
dnsnet
dnsroot
.5
.22
.222
.1
.11
.111
abc
machine name
recursive behavior

## Slide 57: step 4 – repeating the experiment
kathara – [ lab: dns ]
.222
192.168.0.0/24
pc1
pc2
.2
dnslug
dnsnano
dnsorg
dnsnet
.5
.22
.1
.11
.111
pc1:~# ping pc2.nanoinside.net █
pc1
dnsroot
pc2:~# tcpdump –n –t port domain █
pc2

## Slide 58: step 4 – repeating the experiment
pc2:~# tcpdump –n –t port domain
tcpdump: verbose output suppressed, use -v or -vv for full protocol decode
listening on eth0, link-type EN10MB (Ethernet), capture size 96 bytes
IP 192.168.0.111.3072 > 192.168.0.11.53: 54784+ A? pc2.nanoinside.net. (36)
IP 192.168.0.11.53 > 192.168.0.111.3072: 54784 1/1/1 A 192.168.0.222 (90)
█
pc2
query
answer
the name server cache helps reducing traffic

## Slide 59: step 4 – repeating the experiment
192.168.0.0/24
pc1
pc2
.2
dnslug
dnsnano
dnsorg
dnsnet
dnsroot
.5
.22
.222
.1
.11
.111
abc
machine name

## Slide 60: step 5 – restarting the name server
the restart operation cleans up caches
  a new client query triggers the complete sequence of iterative queries
upon startup, the name server checks its root server configuration
dnslug:~# /etc/init.d/bind restart
Stopping domain name service: named.
Starting domain name service: named.
dnslug:~# █
dnslug
pc2:~# tcpdump -n -t port domain
tcpdump: verbose output suppressed, use -v or -vv for full protocol decode
listening on eth0, link-type EN10MB (Ethernet), capture size 96 bytes
IP 192.168.0.11.3078 > 192.168.0.5.53: 15318 [1au] NS? . (28)
IP 192.168.0.5.53 > 192.168.0.11.3078: 15318* 1/0/2 NS ROOT-SERVER. (68)
█
pc2

## Slide 61: step 6 – non-existent target
kathara – [ lab: dns ]
.222
192.168.0.0/24
pc1
pc2
.2
dnslug
dnsnano
dnsorg
dnsnet
.5
.22
.1
.11
.111
pc1:~# ping pluto.nanoinside.net █
pc1
dnsroot
pc2:~# tcpdump –n –t port domain █
pc2

## Slide 62: step 6 – non-existent target
last update: Nov 2018
kathara – [ lab: dns ]
pc2:~# tcpdump -n -t port domain
tcpdump: verbose output suppressed, use -v or -vv for full protocol decode
listening on eth0, link-type EN10MB (Ethernet), capture size 96 bytes
IP 192.168.0.111.3072 > 192.168.0.11.53:
52975+ A? pluto.nanoinside.net. (38)
IP 192.168.0.11.3078 > 192.168.0.5.53:
35274 [1au] A? pluto.nanoinside.net. (49)
IP 192.168.0.5.53 > 192.168.0.11.3078:
35274 0/1/2 (86)
IP 192.168.0.11.3078 > 192.168.0.2.53:
52429 [1au] A? pluto.nanoinside.net. (49)
IP 192.168.0.2.53 > 192.168.0.11.3078:
52429 0/1/2 (87)
IP 192.168.0.11.3078 > 192.168.0.22.53:
11940 [1au] A? pluto.nanoinside.net. (49)
IP 192.168.0.22.53 > 192.168.0.11.3078:
11940 NXDomain* 0/1/1 (98)
IP 192.168.0.11.53 > 192.168.0.111.3072:
52975 NXDomain 0/1/0 (101)
......
pc2
query
answer
© Computer Networks Research Group Roma Tre

## Slide 63: step 6 – non-existent target
last update: Nov 2018
kathara – [ lab: dns ]
pc2:~# tcpdump -n -t port domain
tcpdump: verbose output suppressed, use -v or -vv for full protocol decode
listening on eth0, link-type EN10MB (Ethernet), capture size 96 bytes
IP 192.168.0.111.3072 > 192.168.0.11.53:
52975+ A? pluto.nanoinside.net. (38)
IP 192.168.0.11.3078 > 192.168.0.5.53:
35274 [1au] A? pluto.nanoinside.net. (49)
IP 192.168.0.5.53 > 192.168.0.11.3078:
35274 0/1/2 (86)
IP 192.168.0.11.3078 > 192.168.0.2.53:
52429 [1au] A? pluto.nanoinside.net. (49)
IP 192.168.0.2.53 > 192.168.0.11.3078:
52429 0/1/2 (87)
IP 192.168.0.11.3078 > 192.168.0.22.53:
11940 [1au] A? pluto.nanoinside.net. (49)
IP 192.168.0.22.53 > 192.168.0.11.3078:
11940 NXDomain* 0/1/1 (98)
IP 192.168.0.11.53 > 192.168.0.111.3072:
52975 NXDomain 0/1/0 (101)
......
pc2
query
answer
all the iterative queries are performed again because of the cache flush
© Computer Networks Research Group Roma Tre

## Slide 64: step 6 – non-existent target
last update: Nov 2018
kathara – [ lab: dns ]
pc2:~# tcpdump -n -t port domain
tcpdump: verbose output suppressed, use -v or -vv for full protocol decode
listening on eth0, link-type EN10MB (Ethernet), capture size 96 bytes
IP 192.168.0.111.3072 > 192.168.0.11.53:
52975+ A? pluto.nanoinside.net. (38)
IP 192.168.0.11.3078 > 192.168.0.5.53:
35274 [1au] A? pluto.nanoinside.net. (49)
IP 192.168.0.5.53 > 192.168.0.11.3078:
35274 0/1/2 (86)
IP 192.168.0.11.3078 > 192.168.0.2.53:
52429 [1au] A? pluto.nanoinside.net. (49)
IP 192.168.0.2.53 > 192.168.0.11.3078:
52429 0/1/2 (87)
IP 192.168.0.11.3078 > 192.168.0.22.53:
11940 [1au] A? pluto.nanoinside.net. (49)
IP 192.168.0.22.53 > 192.168.0.11.3078:
11940 NXDomain* 0/1/1 (98)
IP 192.168.0.11.53 > 192.168.0.111.3072:
52975 NXDomain 0/1/0 (101)
......
pc2
query
answer
the requested domain (pluto.nanoinside.net) does not exist (NXDomain)
*=authoritative answer
© Computer Networks Research Group Roma Tre

## Slide 65: step 6 – non-existent target (cont’d)
......
IP 192.168.0.111.3072 > 192.168.0.11.53:
52976+ A? pluto.nanoinside.net.lugroma3.org. (51)
IP 192.168.0.11.53 > 192.168.0.111.3072:
52976 NXDomain* 0/1/0 (99)
pc2
query
answer
since the query has failed, pc1 tries once more with the domain search path configured inside its /etc/resolv.conf:
nameserver 192.168.0.11
search lugroma3.org

## Slide 66: step 6 – repeating the experiment
kathara – [ lab: dns ]
.222
192.168.0.0/24
pc1
pc2
.2
dnslug
dnsnano
dnsorg
dnsnet
.5
.22
.1
.11
.111
pc1:~# ping pluto.nanoinside.net █
pc1
dnsroot
pc2:~# tcpdump –n –t port domain █
pc2

## Slide 67: step 6 – repeating the experiment
pc2:~# tcpdump -n -t port domain
tcpdump: verbose output suppressed, use -v or -vv for full protocol decode
listening on eth0, link-type EN10MB (Ethernet), capture size 96 bytes
IP 192.168.0.111.3072 > 192.168.0.11.53:
2449+ A? pluto.nanoinside.net. (38)
IP 192.168.0.11.53 > 192.168.0.111.3072:
2449 NXDomain 0/1/0 (87)
IP 192.168.0.111.3072 > 192.168.0.11.53:
2450+ A? pluto.nanoinside.net.lugroma3.org. (51)
IP 192.168.0.11.53 > 192.168.0.111.3072:
2450 NXDomain* 0/1/0 (99)
█
pc2
query
answer
the name server negative cache has stored the negative answer

## Slide 68: step 7 – advanced queries
resource records can be searched by using dig
  highly customizable queries
  detailed responses
pc1:~# dig pc2.nanoinside.net █
pc1

## Slide 69: step 7 – advanced queries
pc1:~# dig pc2.nanoinside.net
; <<>> DiG 9.3.1 <<>> pc2.nanoinside.net
;; global options: printcmd
;; Got answer:
;; ->>HEADER<<- opcode: QUERY, status: NOERROR, id: 25601
;; flags: qr rd ra; QUERY: 1, ANSWER: 1, AUTHORITY: 1, ADDITIONAL: 1
;; QUESTION SECTION:
;pc2.nanoinside.net. IN A
;; ANSWER SECTION:
pc2.nanoinside.net. 47861 IN A 192.168.0.222
;; AUTHORITY SECTION:
nanoinside.net. 47861 IN NS dnsnano.nanoinside.net.
;; ADDITIONAL SECTION:
dnsnano.nanoinside.net. 48956 IN A 192.168.0.22
;; Query time: 129 msec
;; SERVER: 192.168.0.11#53(192.168.0.11)
;; WHEN: Tue Apr 17 14:49:56 2007
;; MSG SIZE rcvd: 90
█
pc1
© Computer Networks Research Group Roma Tre

## Slide 70: step 7 – advanced queries
pc1:~# dig pc2.nanoinside.net
; <<>> DiG 9.3.1 <<>> pc2.nanoinside.net
;; global options: printcmd
;; Got answer:
;; ->>HEADER<<- opcode: QUERY, status: NOERROR, id: 25601
;; flags: qr rd ra; QUERY: 1, ANSWER: 1, AUTHORITY: 1, ADDITIONAL: 1
;; QUESTION SECTION:
;pc2.nanoinside.net. IN A
;; ANSWER SECTION:
pc2.nanoinside.net. 47861 IN A 192.168.0.222
;; AUTHORITY SECTION:
nanoinside.net. 47861 IN NS dnsnano.nanoinside.net.
;; ADDITIONAL SECTION:
dnsnano.nanoinside.net. 48956 IN A 192.168.0.22
;; Query time: 129 msec
;; SERVER: 192.168.0.11#53(192.168.0.11)
;; WHEN: Tue Apr 17 14:49:56 2007
;; MSG SIZE rcvd: 90
█
pc1
© Computer Networks Research Group Roma Tre
answer flags:
qr: query response
rd: recursion desired (the user asked for a recursive lookup)
ra: recursion available (the server allows recursive lookups)

## Slide 71: step 7 – advanced queries
pc1:~# dig pc2.nanoinside.net
; <<>> DiG 9.3.1 <<>> pc2.nanoinside.net
;; global options: printcmd
;; Got answer:
;; ->>HEADER<<- opcode: QUERY, status: NOERROR, id: 25601
;; flags: qr rd ra; QUERY: 1, ANSWER: 1, AUTHORITY: 1, ADDITIONAL: 1
;; QUESTION SECTION:
;pc2.nanoinside.net. IN A
;; ANSWER SECTION:
pc2.nanoinside.net. 47861 IN A 192.168.0.222
;; AUTHORITY SECTION:
nanoinside.net. 47861 IN NS dnsnano.nanoinside.net.
;; ADDITIONAL SECTION:
dnsnano.nanoinside.net. 48956 IN A 192.168.0.22
;; Query time: 129 msec
;; SERVER: 192.168.0.11#53(192.168.0.11)
;; WHEN: Tue Apr 17 14:49:56 2007
;; MSG SIZE rcvd: 90
█
pc1
© Computer Networks Research Group Roma Tre
these sections correspond to those contained in DNS packets

## Slide 72: step 7 – advanced queries
pc1:~# dig pc2.nanoinside.net
; <<>> DiG 9.3.1 <<>> pc2.nanoinside.net
;; global options: printcmd
;; Got answer:
;; ->>HEADER<<- opcode: QUERY, status: NOERROR, id: 25601
;; flags: qr rd ra; QUERY: 1, ANSWER: 1, AUTHORITY: 1, ADDITIONAL: 1
;; QUESTION SECTION:
;pc2.nanoinside.net. IN A
;; ANSWER SECTION:
pc2.nanoinside.net. 47861 IN A 192.168.0.222
;; AUTHORITY SECTION:
nanoinside.net. 47861 IN NS dnsnano.nanoinside.net.
;; ADDITIONAL SECTION:
dnsnano.nanoinside.net. 48956 IN A 192.168.0.22
;; Query time: 129 msec
;; SERVER: 192.168.0.11#53(192.168.0.11)
;; WHEN: Tue Apr 17 14:49:56 2007
;; MSG SIZE rcvd: 90
█
pc1
© Computer Networks Research Group Roma Tre
records being searched
(class: IN, type: A  address records)
a dns message never contains more than one question section

## Slide 73: step 7 – advanced queries
pc1:~# dig pc2.nanoinside.net
; <<>> DiG 9.3.1 <<>> pc2.nanoinside.net
;; global options: printcmd
;; Got answer:
;; ->>HEADER<<- opcode: QUERY, status: NOERROR, id: 25601
;; flags: qr rd ra; QUERY: 1, ANSWER: 1, AUTHORITY: 1, ADDITIONAL: 1
;; QUESTION SECTION:
;pc2.nanoinside.net. IN A
;; ANSWER SECTION:
pc2.nanoinside.net. 47861 IN A 192.168.0.222
;; AUTHORITY SECTION:
nanoinside.net. 47861 IN NS dnsnano.nanoinside.net.
;; ADDITIONAL SECTION:
dnsnano.nanoinside.net. 48956 IN A 192.168.0.22
;; Query time: 129 msec
;; SERVER: 192.168.0.11#53(192.168.0.11)
;; WHEN: Tue Apr 17 14:49:56 2007
;; MSG SIZE rcvd: 90
█
pc1
© Computer Networks Research Group Roma Tre
records that form the answer to the question
may be more than one
time to live of a resource record that is cached on the server
try invoking dig once more to see it decreasing
constant if the record is not cached (i.e., it is stored on the name server being queried – by default the one configured in /etc/resolv.conf)

## Slide 74: step 7 – advanced queries
pc1:~# dig pc2.nanoinside.net
; <<>> DiG 9.3.1 <<>> pc2.nanoinside.net
;; global options: printcmd
;; Got answer:
;; ->>HEADER<<- opcode: QUERY, status: NOERROR, id: 25601
;; flags: qr rd ra; QUERY: 1, ANSWER: 1, AUTHORITY: 1, ADDITIONAL: 1
;; QUESTION SECTION:
;pc2.nanoinside.net. IN A
;; ANSWER SECTION:
pc2.nanoinside.net. 47861 IN A 192.168.0.222
;; AUTHORITY SECTION:
nanoinside.net. 47861 IN NS dnsnano.nanoinside.net.
;; ADDITIONAL SECTION:
dnsnano.nanoinside.net. 48956 IN A 192.168.0.22
;; Query time: 129 msec
;; SERVER: 192.168.0.11#53(192.168.0.11)
;; WHEN: Tue Apr 17 14:49:56 2007
;; MSG SIZE rcvd: 90
█
pc1
© Computer Networks Research Group Roma Tre
records describing authoritative name servers are returned here
additional records are returned here

## Slide 75: step 8 – an iterative query
pc1:~# dig +noquestion +noadditional +norecurse pc2.nanoinside.net █
pc1
avoid displaying question and additional sections
disable recursion

## Slide 76: step 8 – an iterative query
pc1:~# dig +noquestion +noadditional +norecurse pc2.nanoinside.net
;; global options: printcmd
;; Got answer:
;; ->>HEADER<<- opcode: QUERY, status: NOERROR, id: 63298
;; flags: qr ra; QUERY: 1, ANSWER: 0, AUTHORITY: 1, ADDITIONAL: 1
;; AUTHORITY SECTION:
. 59995 IN NS ROOT-SERVER.
;; Query time: 21 msec
;; SERVER: 192.168.0.11#53(192.168.0.11)
;; WHEN: Tue Apr 17 16:07:48 2007
;; MSG SIZE rcvd: 76
pc1:~# █
pc1
the server answers by specifying the authoritative name server to be contacted to get the desired information

## Slide 77: step 8 – an iterative query
pc1:~# dig +noquestion +noadditional +norecurse @192.168.0.5 pc2.nanoinside.net
; <<>> DiG 9.3.1 <<>> +noquestion +noadditional +norecurse @192.168.0.5 pc2.nanoinside.net
; (1 server found)
;; global options: printcmd
;; Got answer:
;; ->>HEADER<<- opcode: QUERY, status: NOERROR, id: 40091
;; flags: qr ra; QUERY: 1, ANSWER: 0, AUTHORITY: 1, ADDITIONAL: 1
;; AUTHORITY SECTION:
net. 60000 IN NS dnsnet.net.
;; Query time: 22 msec
;; SERVER: 192.168.0.5#53(192.168.0.5)
;; WHEN: Tue Apr 17 16:14:23 2007
;; MSG SIZE rcvd: 73
pc1:~# █
pc1
query a specific name server (dnsroot)
dnsnet.net is the authoritative name server for zone net

## Slide 78: step 8 – an iterative query
pc1:~# dig +noquestion +noadditional +norecurse @192.168.0.2 pc2.nanoinside.net
; <<>> DiG 9.3.1 <<>> +noquestion +noadditional +norecurse @192.168.0.2 pc2.nanoinside.net
; (1 server found)
;; global options: printcmd
;; Got answer:
;; ->>HEADER<<- opcode: QUERY, status: NOERROR, id: 49875
;; flags: qr ra; QUERY: 1, ANSWER: 0, AUTHORITY: 1, ADDITIONAL: 1
;; AUTHORITY SECTION:
nanoinside.net. 60000 IN NS dnsnano.nanoinside.net.
;; Query time: 22 msec
;; SERVER: 192.168.0.2#53(192.168.0.2)
;; WHEN: Tue Apr 17 16:21:47 2007
;; MSG SIZE rcvd: 74
pc1:~# █
pc1
query a specific name server (dnsnet.net)
dnsnano.nanoinside.net is the authoritative name server for zone nanoinside.net

## Slide 79: step 8 – an iterative query
pc1:~# dig +noquestion +noadditional +norecurse @192.168.0.22 pc2.nanoinside.net
; <<>> DiG 9.3.1 <<>> +noquestion +noadditional +norecurse @192.168.0.22 pc2.nanoinside.net
; (1 server found)
;; global options: printcmd
;; Got answer:
;; ->>HEADER<<- opcode: QUERY, status: NOERROR, id: 55152
;; flags: qr aa ra; QUERY: 1, ANSWER: 1, AUTHORITY: 1, ADDITIONAL: 1
;; ANSWER SECTION:
pc2.nanoinside.net. 60000 IN A 192.168.0.222
;; AUTHORITY SECTION:
nanoinside.net. 60000 IN NS dnsnano.nanoinside.net.
;; Query time: 24 msec
;; SERVER: 192.168.0.22#53(192.168.0.22)
;; WHEN: Tue Apr 17 16:23:46 2007
;; MSG SIZE rcvd: 90
pc1
query a specific name server (dnsnano.nanoinside.net)

## Slide 80: step 8 – an iterative query
just to confirm that name servers cache information during recursive queries...
pc1:~# dig +noquestion +noadditional pc2.nanoinside.net
[...]
pc1:~# █
pc1
© Computer Networks Research Group Roma Tre
a recursive query
(default behavior of dig)

## Slide 81: step 8 – an iterative query
just to confirm that name servers cache information during recursive queries...
pc1:~# dig +noquestion +noadditional pc2.nanoinside.net
[...]
pc1:~# dig +noquestion +noadditional +norecurse pc2.nanoinside.net █
pc1
© Computer Networks Research Group Roma Tre
an iterative query

## Slide 82: step 8 – an iterative query
just to confirm that name servers cache information during recursive queries...
pc1:~# dig +noquestion +noadditional pc2.nanoinside.net
[...]
pc1:~# dig +noquestion +noadditional +norecurse pc2.nanoinside.net
; <<>> DiG 9.3.1 <<>> +noquestion +noadditional +norecurse pc2.nanoinside.net
;; global options: printcmd
;; Got answer:
;; ->>HEADER<<- opcode: QUERY, status: NOERROR, id: 55689
;; flags: qr ra; QUERY: 1, ANSWER: 0, AUTHORITY: 1, ADDITIONAL: 1
;; AUTHORITY SECTION:
nanoinside.net. 59989 IN NS dnsnano.nanoinside.net.
;; Query time: 19 msec
;; SERVER: 192.168.0.11#53(192.168.0.11)
;; WHEN: Tue Apr 17 16:45:50 2007
;; MSG SIZE rcvd: 74
pc1
© Computer Networks Research Group Roma Tre

## Slide 83: step 8 – an iterative query
just to confirm that name servers cache information during recursive queries...
pc1:~# dig +noquestion +noadditional pc2.nanoinside.net
[...]
pc1:~# dig +noquestion +noadditional +norecurse pc2.nanoinside.net
; <<>> DiG 9.3.1 <<>> +noquestion +noadditional +norecurse pc2.nanoinside.net
;; global options: printcmd
;; Got answer:
;; ->>HEADER<<- opcode: QUERY, status: NOERROR, id: 55689
;; flags: qr ra; QUERY: 1, ANSWER: 0, AUTHORITY: 1, ADDITIONAL: 1
;; AUTHORITY SECTION:
nanoinside.net. 59989 IN NS dnsnano.nanoinside.net.
;; Query time: 19 msec
;; SERVER: 192.168.0.11#53(192.168.0.11)
;; WHEN: Tue Apr 17 16:45:50 2007
;; MSG SIZE rcvd: 74
pc1
© Computer Networks Research Group Roma Tre
the ttl is expiring
( this is a cached information)
dnslug.lugroma3.org immediately answers with the authoritative name server for zone nanoinside.net, which it has learned during the recursive query