## Slide 1: data centers’ routing
Version | 3.1
Author(s) | L. Ariemma, G. Di Battista, M. Patrignani, M. Scazzariello, T. Caiazzi
E-mail | contact@kathara.org
Web | http://www.kathara.org/
Description | Data Centers’ Routing: Fat-Trees, BGP

## Slide 2: copyright notice
all the pages/slides in this presentation, including but not limited to, images, photos, animations, videos, sounds, music, and text (hereby referred to as “material”) are protected by copyright
this material, with the exception of some multimedia elements licensed by other organizations, is property of the authors and/or organizations appearing in the first slide
this material, or its parts, can be reproduced and used for didactical purposes within universities and schools, provided that this happens for non-profit purposes
any other use is prohibited, unless explicitly authorized by the authors on the basis of an explicit agreement
this copyright notice must always be redistributed together with the material, or its portions

## Slide 3: routing in Fat-Trees
why BGP?

## Slide 4: overview – routing
why routing and not switching?
the choice of the routing protocols
why using BGP in Fat-Tree data centers?
inter-domain routing VS data center routing
BGP in the data center

## Slide 5: why routing and not switching?
 | Pros | Cons
Switching (L2) | No configuration needed | STP protocol has no multipath support Using VLANs for load balancing is tricky Broadcast traffic flooding the network
Routing (L3) | Multipath support | Need of routing protocols Complex configuration Need of automating the configuration

## Slide 6: choosing a routing protocol
there are many possibilities, among them
  a classical IGP protocol (e.g., OSPF, IS-IS)
  BGP (most used in Hyperscale data centers)
  RIFT (Routing In Fat-Trees)
    Under standardization at IETF
    Designed for Fat-Trees topologies
  OpenFabric
    IS-IS variant created for Clos topologies
  SDN Protocols

## Slide 7: why using BGP in Fat-Trees?
BGP has several stable and robust implementations, even open-source
  e.g., FRRouting, Quagga
BGP generates less flooding than common IGPs (IS-IS, OSPF, etc.)
  if a received update does not change the best route, a BGP speaker does not propagate the update
BGP natively supports ECMP (Equal-Cost Multi-Path)
  Fat-Trees have many paths with the same length

## Slide 8: why using eBGP? (and not iBGP)
the most obvious choice would be to use iBGP since the data center networks is under the same administration
however, eBGP is always used because
  eBGP is easier to setup, no need for IGP
    with iBGP, the IGP would compute routes
  iBGP multipath support has some limitations
    can be overcame, but it is complex

## Slide 9: inter-domain routing VS DC routing
inter-domain routing | data centers’ routing
the internet has relatively sparse connectivity | data centers’ networks have very dense connectivity
stability is preferred over quick convergence | quick convergence is preferred over stability
the aim is computing a single best path for each destination | the aim is computing multiple paths to each destination

## Slide 10: BGP in the data center
BGP was primarily devised for inter-domain routing
  default configurations are not suitable in a data center
needs some tweaks described in RFC-7938
  AS numbers assignment
  ECMP policy relax
  timer adjustment

## Slide 11: AS numbers assignment
global ASNs are not used in the data center
  they can be misleading
    because operators associate them with names
  they are dangerous
    an accidental leakage of the internal BGP notifications to the internet may be disruptive
private ASNs are generally used
  the 2-byte ASNs allow only 1,023 private ASes in the range 64512–65534
  the 4-byte ASNs support almost 95 million private ASes

## Slide 12: ASes and routers
the most obvious choice would be assigning a different ASN to each node
however, this approach would lead to BGP path exploration issues

## Slide 13: BGP path exploration
immediately after a fault there is a transient period when inconsistent AS-paths are propagated in the network
  routers have plenty of alternatives and jump from one to another before all alternatives are withdrawn
  each best route change is propagated again by the routers
  lots of useless BGP updates are transmitted
since data centers’ topologies are dense and hence have a lot of cycles this problem has to be addressed

## Slide 14: the problem of BGP path exploration
*>193.204.0.0/15 [L2]
[L1,S1,L2]
*>193.204.0.0/15 [L2]
S2
S1
L2
L1
because of the adopted AS scheme several fake routes could be possible during path exploration
193.204.0.0/15
[L2]
[L2]
[S1,L2]
[S2,L2]
*>193.204.0.0/15 [S1,L2]
*= [S2,L2]
X
[L1,S1,L2]
*>193.204.0.0/15 [L2]

## Slide 15: the ASes scheme of choice
each Leaf is a different AS
the Spine nodes of each PoD belong to the same AS
the ToF nodes of the same plane belong to the same AS
BEWARE: there are NO iBGP peerings

## Slide 16: the ASes scheme of choice – multi-plane
Server Farm
Plane A
Plane B

## Slide 17: multiple paths between Leaves
the adopted AS scheme allows for multiple paths between pairs of Leaves
  in a FT(K=2,R=2) only two paths are possible between two Leaves of the same PoD
    they don’t leave the PoD

## Slide 18: multiple paths between Leaves
the adopted AS scheme allows for multiple paths between pairs of Leaves
  in a FT(K=2,R=2) eight paths are possible between two Leaves of different PoDs

## Slide 19: BGP and ECMP
BGP natively supports ECMP
by default, BGP considers two announcement of the same prefix “equal” if they are equal in each best-path selection criterion except for the last one
  lowest router-id of the announcing peer
to enable multi-path, BGP requires that the AS-paths selected for multi-path match exactly
  not just they have equal-length but equal AS numbers inside

## Slide 20: BGP multi-path relax
when the AS_PATH lengths of different announcements for the same prefix are the same, the best-path algorithm skips checking for exact match of the AS numbers
this modification is often called “as-path multipath-relax”
  different vendors may use different names
really needed for using dual attached servers and multi-plane Fat-Trees

## Slide 21: tuning BGP timers
there are four main timers that are responsible for BGP behaviour
  advertisement interval timer
  keepalive timer
  hold timer
  connect timer

## Slide 22: advertisement interval timer
announcements that need to be sent to a neighbor are bunched together and sent together only when the interval expires
  then the timer is reset for that neighbor
the default value for eBGP is 30s
  in interdomain routing this improves stability and reduces the number of multiple updates for the same prefix
in data centers is set to 0s
  it is required for fast convergence

## Slide 23: keepalive and hold timers
each BGP peer sends periodic keepalive messages to its neighbors according to the keepalive timer
when a peer doesn’t receive a keepalive for a period greater than the hold timer
  the connection is dropped
  all the announcements received are considered invalid
  the peer tries to re-establish the connection
by default, the keepalive timer is 60s and the hold timer is 180s
in data centers timers of 3s and 9s are used, respectively

## Slide 24: connect timer
when a connection to a peer fails, BGP waits for the connect timer expiration before attempting to reconnect
  the connect timer by default is 60s
  this can delay session re-establishment when a link recovers from a failure or a node powers up
in data centers it is set to 10s

## Slide 25: automating the configuration
unnumbered interfaces
  used to establish peerings specifying the interface name rather than the IP address and the remote AS number
peer groups
  used to specify policies for groups of peers

## Slide 26: connecting the servers
Servers
Containers or VMs
Prefixes are assigned directly to the servers
each Leaf announces its server’s prefix

## Slide 27: basic Fat-Tree lab
hands on Kathará

## Slide 28: lab pre-conditions
Linux and macOS
  no specific requirement
Windows
  WSL 2 does not support Multi-Path
  need to fallback to Hyper-V Docker backend
    open Docker Desktop and go to Settings (cog in the top-right corner)
    unselect the “Use the WSL 2 based engine” checkbox
    click “Apply & restart”
  or create a VM with a Linux distribution

## Slide 29: lab pre-conditions
FRR handles unnumbered interface only with IPv6 link-local addresses
  all the routers in the fabric must have IPv6 enabled in order to work
    to enable IPv6 for machine “router”, add router[ipv6]=True to the lab.conf file

## Slide 30: naming convention
tof_x_y_z
  x: plane number
  y: level, always 2
  z: ToF number
spine_x_y_z
  x: PoD number
  y: level, always 1
  z: Spine number
leaf_x_y_z
  x: PoD number
  y: level, always 0
  z: Leaf number
server_x_y_z
  x: PoD number
  y: corresponding Leaf number
  z: server number

## Slide 31: lab topology
spine_1_1_2
spine_1_1_1
leaf_1_0_1
leaf_1_0_2
spine_2_1_1
spine_2_1_2
tof_1_2_1
tof_1_2_2
server_1_1_1
server_1_1_2
server_1_2_1
server_1_2_2
server_2_1_1
server_2_1_2
server_2_2_1
server_2_2_2
leaf_2_0_1
leaf_2_0_2
A
C
U
V
Z
M
F
P
W
O
L
N
K
E
B
D
Q
R
S
T
10.0.0.16/30
10.0.0.0/30
10.0.0.12/30
10.0.0.8/30
10.0.0.4/30
10.0.0.44/30
10.0.0.32/30
10.0.0.40/30
10.0.0.36/30
10.0.0.24/30
10.0.0.20/30
10.0.0.28/30
10.0.0.60/30
10.0.0.52/30
10.0.0.56/30
10.0.0.48/30
201.1.1.0/24
201.1.2.0/24
201.2.2.0/24
201.2.1.0/24
202.2.2.0/24
202.2.1.0/24
I
G
H
J
202.1.1.0/24
202.1.2.0/24
AS64512
AS64514
AS64513
AS64515
AS64516
AS64517
AS64518

## Slide 32: ToF configuration example
router bgp 64518
timers bgp 3 9
bgp router-id 192.168.0.14
no bgp ebgp-requires-policy
bgp bestpath as-path multipath-relax
neighbor fabric peer-group
neighbor fabric remote-as external
neighbor fabric advertisement-interval 0
neighbor fabric timers connect 10
neighbor eth0 interface peer-group fabric
neighbor eth1 interface peer-group fabric
neighbor eth2 interface peer-group fabric
neighbor eth3 interface peer-group fabric
address-family ipv4 unicast
neighbor fabric activate
maximum-paths 64
exit-address-family
bgpd.conf
set keepalive and hold timers
BGP multi-path relax
create a peer-group
all peers of the group are eBGP. The remote ASN is inferred
set advertisement interval timer
set connect timer
add interfaces to peer-group for unnumbered peering
enable A.F. to peer-group
maximum Multi-Path possibilities

## Slide 33: Spine configuration example
router bgp 64514
timers bgp 3 9
bgp router-id 192.168.0.5
no bgp ebgp-requires-policy
bgp bestpath as-path multipath-relax
neighbor TOR peer-group
neighbor TOR remote-as external
neighbor TOR advertisement-interval 0
neighbor TOR timers connect 10
neighbor eth0 interface peer-group TOR
neighbor eth1 interface peer-group TOR
neighbor fabric peer-group
neighbor fabric remote-as external
neighbor fabric advertisement-interval 0
neighbor fabric timers connect 10
neighbor eth2 interface peer-group fabric
neighbor eth3 interface peer-group fabric
bgpd.conf – part 1
address-family ipv4 unicast
neighbor fabric activate
neighbor TOR activate
maximum-paths 64
exit-address-family
bgpd.conf – part 2

## Slide 34: Leaf configuration example
router bgp 64512
timers bgp 3 9
bgp router-id 192.168.0.1
no bgp ebgp-requires-policy
bgp bestpath as-path multipath-relax
neighbor TOR peer-group
neighbor TOR remote-as external
neighbor TOR advertisement-interval 0
neighbor TOR timers connect 10
neighbor eth0 interface peer-group TOR
neighbor eth1 interface peer-group TOR
address-family ipv4 unicast
neighbor TOR activate
network 201.1.1.0/24 network 201.1.2.0/24
maximum-paths 64
exit-address-family
bgpd.conf
announce the server prefixes

## Slide 35: data plane
root@spine_1_1_1:/# ip route
10.0.0.0/30 dev eth0 proto kernel scope link src 10.0.0.2
10.0.0.8/30 dev eth1 proto kernel scope link src 10.0.0.10
10.0.0.16/30 dev eth2 proto kernel scope link src 10.0.0.17
10.0.0.20/30 dev eth3 proto kernel scope link src 10.0.0.21
201.1.1.0/24 nhid 12 via 10.0.0.1 dev eth0 proto bgp metric 20
201.1.2.0/24 nhid 12 via 10.0.0.1 dev eth0 proto bgp metric 20
201.2.1.0/24 nhid 11 via 10.0.0.9 dev eth1 proto bgp metric 20
201.2.2.0/24 nhid 11 via 10.0.0.9 dev eth1 proto bgp metric 20
202.1.1.0/24 nhid 16 proto bgp metric 20
nexthop via 10.0.0.18 dev eth2 weight 1
nexthop via 10.0.0.22 dev eth3 weight 1
202.1.2.0/24 nhid 16 proto bgp metric 20
nexthop via 10.0.0.18 dev eth2 weight 1
nexthop via 10.0.0.22 dev eth3 weight 1
202.2.1.0/24 nhid 16 proto bgp metric 20
nexthop via 10.0.0.18 dev eth2 weight 1
nexthop via 10.0.0.22 dev eth3 weight 1
202.2.2.0/24 nhid 16 proto bgp metric 20
nexthop via 10.0.0.18 dev eth2 weight 1
nexthop via 10.0.0.22 dev eth3 weight 1
multiple next-hop for the same prefix

## Slide 36: control plane
spine_1_1_1# show ip bgp
BGP table version is 8, local router ID is 192.168.0.6, vrf id 0
Default local pref 100, local AS 64514
Status codes: s suppressed, d damped, h history, * valid, > best, = multipath,
i internal, r RIB-failure, S Stale, R Removed
Nexthop codes: @NNN nexthop's vrf id, < announce-nh-self
Origin codes: i - IGP, e - EGP, ? - incomplete
Network Next Hop Metric LocPrf Weight Path
*> 201.1.1.0/24 10.0.0.5 0 0 64512 i
*> 201.1.2.0/24 10.0.0.5 0 0 64512 i
*> 201.2.1.0/24 10.0.0.13 0 0 64513 i
*> 201.2.2.0/24 10.0.0.13 0 0 64513 i
*> 202.1.1.0/24 10.0.0.26 0 64518 64517 64515 i
*= 10.0.0.30 0 64518 64517 64515 i
*> 202.1.2.0/24 10.0.0.26 0 64518 64517 64515 i
*= 10.0.0.30 0 64518 64517 64515 i
*> 202.2.1.0/24 10.0.0.26 0 64518 64517 64516 i
*= 10.0.0.30 0 64518 64517 64516 i
*> 202.2.2.0/24 10.0.0.26 0 64518 64517 64516 i
*= 10.0.0.30 0 64518 64517 64516 i
Displayed 8 routes and 12 total paths

## Slide 37: Multi-Path traceroute
traditional traceroute may provide hard-to-interpret or even misleading results when used in presence of ECMP
Multi-Path traceroute tools generate packet header contents to obtain a more precise picture of the actual routes of packets
  allow all probes towards a destination to follow the same path in the presence of per-flow load balancing
  allow a user to distinguish between the presence of per-flow load balancing and per-packet load balancing

## Slide 38: Multi-Path traceroute
two different tools:
  paris-traceroute
    traceroute designed to work in presence of Multi-Path and load balancers
  dublin-traceroute
    based on the paris-traceroute
    adds a NAT detection technique
    introduces visualization and analysis tools

## Slide 39: dublin-traceroute example output

## Slide 40: bibliography and further readings
[Caiazzi ‘22] Caiazzi, Scazzariello, Alberro, Ariemma, Castro, Grampin, Di Battista, “Sibyl: a Framework for Evaluating the Implementation of Routing Protocols in Fat-Trees“, NOMS 2022
[Caiazzi ‘21] Caiazzi, Scazzariello, Ariemma, “VFTGen: a Tool to Perform Experiments in Virtual Fat Tree Topologies“, IM 2021
[Caiazzi ‘19] Caiazzi, “Software Defined Data Centers: methods and tools for routing protocol verification and comparison”, Ms. Thesis, Roma Tre University, 2019
[Dutt ‘17] Dutt, “BGP in the Data Center”, O’Reilly, 2017
[RFC-7938] Lapukhov, Premji, “Use of BGP for Routing in Large-Scale Data Centers” Internet Engineering Task Force (IETF) Request for Comments: 7938