## Slide 1: kathara lab
rip with FRRouting
Version | 1.1
Author(s) | G. Di Battista, M. Patrignani, M. Pizzonia, L. Ariemma, M. Scazzariello, T. Caiazzi
E-mail | contact@kathara.org
Web | http://www.kathara.org/
Description | experiences with the ripv2 distance vector routing protocol – derives from kathara rip lab ver. 1.2 which, in turns, derives from netkit rip lab ver. 2.4

## Slide 2: copyright notice
All the pages/slides in this presentation, including but not limited to, images, photos, animations, videos, sounds, music, and text (hereby referred to as “material”) are protected by copyright.
This material, with the exception of some multimedia elements licensed by other organizations, is property of the authors and/or organizations appearing in the first slide.
This material, or its parts, can be reproduced and used for didactical purposes within universities and schools, provided that this happens for non-profit purposes.
Information contained in this material cannot be used within network design projects or other products of any kind.
Any other use is prohibited, unless explicitly authorized by the authors on the basis of an explicit agreement.
The authors assume no responsibility about this material and provide this material “as is”, with no implicit or explicit warranty about the correctness and completeness of its contents, which may be subject to changes.
This copyright notice must always be redistributed together with the material, or its portions.

## Slide 3: the RIP protocol
RIP is a routing protocol
RIPS is a distance-vector routing protocol
  approach: send all your information to a few
  update your routing information based on what you hear
in this lab we will see an example of RIPv2 protocol on the FRRouting Suite

## Slide 4: sample frr.conf configuration file
root@pc1:~$ cat /etc/frr/frr.conf
!
! FRRouting configuration file
!
!
! RIP CONFIGURATION
!
router rip
network 100.1.0.0/16
!
log file /var/log/frr/frr.log
talk rip on some interface
send rip multicast packets to interfaces falling into this prefix

## Slide 5: small network connected to Internet
r5
r4
r1
r3
r2

## Slide 6: the involved ip subnets
each circle represents a subnet
r5
r4
r1
r3
r2
L
B
A
H
E
C
D
G
F
I
legend

## Slide 7: assigning ip numbers to subnets
100.1.4.0/24
r5
L
r4
r1
r3
B
100.1.2.0/24
A
100.1.1.0/24
H
100.1.0.12/30
E
100.1.0.0/30
100.2.0.0/30
r2
C
100.1.3.0/24
D
G
F
I
100.1.0.4/30
100.1.0.16/30
100.1.0.8/30
legend
ip subnet
assigned prefix
L
100.2.0.0/30

## Slide 8: assigning ip numbers to interfaces
r5
eth0
1
eth0
2
L
eth2
18
r4
eth3
14
eth1
9
eth2
1
eth0
6
eth1
10
r1
r3
eth3
1
eth2
1
B
100.1.2.0/24
A
100.1.1.0/24
H
100.1.0.12/30
E
100.1.0.0/30
100.2.0.0/30
r2
eth2
17
C
100.1.3.0/24
eth0
13
D
100.1.4.0/24
eth1
1
G
F
I
eth3
1
eth0
2
eth1
5
100.1.0.4/30
100.1.0.16/30
100.1.0.8/30
dev
ip
legend
last byte of ip address
network interface

## Slide 9: launching the lab
the lab configuration is such that the frr routing daemon is not automatically started
root@localhost:~$ cd kathara-lab_rip
root@localhost:~/kathara-lab_rip$ kathara lstart

## Slide 10: checking connectivity
towards a directly connected destination
root@r4:~$ ping 100.1.0.13
PING 100.1.0.13 (100.1.0.13) 56(84) bytes of data.
64 bytes from 100.1.0.13: icmp_seq=1 ttl=64 time=1.23 ms
64 bytes from 100.1.0.13: icmp_seq=2 ttl=64 time=0.592 ms
64 bytes from 100.1.0.13: icmp_seq=3 ttl=64 time=0.393 ms
--- 100.1.0.13 ping statistics ---
3 packets transmitted, 3 received, 0% packet loss, time 2032ms
rtt min/avg/max/mdev = 0.393/0.741/1.238/0.360 ms

## Slide 11: checking connectivity
towards a remote destination
what’s going on?
root@r4:~$ ping 100.1.2.1
connect: Network is unreachable

## Slide 12: examining the kernel routing table
since no routing daemon is currently running, only directly connected destinations are known to the router
root@r4:~$ ip route
100.1.0.12/30 dev eth3 proto kernel scope link src 100.1.0.14
100.1.0.16/30 dev eth2 proto kernel scope link src 100.1.0.18
100.1.4.0/24 dev eth1 proto kernel scope link src 100.1.4.1
100.2.0.0/30 dev eth0 proto kernel scope link src 100.2.0.1

## Slide 13: starting the routing daemons
on each router (but r5) issue the following command:
root@r4:~$ systemctl start frr

## Slide 14: checking connectivity (again)
towards a remote destination
after a while, all remote destinations are reachable
root@r4:~$ ping 100.1.2.1
PING 100.1.2.1 (100.1.2.1) 56(84) bytes of data.
64 bytes from 100.1.2.1: icmp_seq=1 ttl=63 time=0.743 ms
64 bytes from 100.1.2.1: icmp_seq=2 ttl=63 time=0.875 ms
64 bytes from 100.1.2.1: icmp_seq=3 ttl=63 time=0.685 ms
--- 100.1.2.1 ping statistics ---
3 packets transmitted, 3 received, 0% packet loss, time 2005ms
rtt min/avg/max/mdev = 0.685/0.767/0.875/0.085 ms

## Slide 15: checking the routing table
the routing table is now updated
root@r4:~$ ip route
100.1.0.0/30 nhid 12 via 100.1.0.13 dev eth3 proto rip metric 20
100.1.0.4/30 nhid 10 via 100.1.0.17 dev eth2 proto rip metric 20
100.1.0.8/30 nhid 10 via 100.1.0.17 dev eth2 proto rip metric 20
100.1.0.12/30 dev eth3 proto kernel scope link src 100.1.0.14
100.1.0.16/30 dev eth2 proto kernel scope link src 100.1.0.18
100.1.1.0/24 nhid 12 via 100.1.0.13 dev eth3 proto rip metric 20
100.1.2.0/24 nhid 12 via 100.1.0.13 dev eth3 proto rip metric 20
100.1.3.0/24 nhid 10 via 100.1.0.17 dev eth2 proto rip metric 20
100.1.4.0/24 dev eth1 proto kernel scope link src 100.1.4.1
100.2.0.0/30 dev eth0 proto kernel scope link src 100.2.0.1

## Slide 16: a look at ripv2 packets
root@r4:~$ tcpdump –tenni eth2 -v
let’s sniff ripv2 packets
display packet details
(enable full protocol decoding)

## Slide 17: a look at ripv2 packets
root@r4:~$ tcpdump –tenni eth2 –v
76:b9:c2:6b:d7:d8 > 01:00:5e:00:00:09, ethertype IPv4 (0x0800), length 166: (tos 0xc0, ttl 1, id 62062, offset 0, flags [DF], proto UDP (17), length 152)
100.1.0.17.520 > 224.0.0.9.520:
RIPv2, Response, length: 124, routes: 6 or less
AFI IPv4, 100.1.0.0/30, tag 0x0000, metric: 2, next-hop: self
AFI IPv4, 100.1.0.4/30, tag 0x0000, metric: 1, next-hop: self
AFI IPv4, 100.1.0.8/30, tag 0x0000, metric: 1, next-hop: self
AFI IPv4, 100.1.1.0/24, tag 0x0000, metric: 2, next-hop: self
AFI IPv4, 100.1.2.0/24, tag 0x0000, metric: 2, next-hop: self
AFI IPv4, 100.1.3.0/24, tag 0x0000, metric: 1, next-hop: self
let’s sniff ripv2 packets

## Slide 18: inspecting the rip routing table
kathara – [ lab: rip ]
root@r4:~$ vtysh
r4# show ip rip
Codes: R - RIP, C - connected, S - Static, O - OSPF, B - BGP
Sub-codes:
(n) - normal, (s) - static, (d) - default, (r) - redistribute,
(i) - interface
Network Next Hop Metric From Tag Time
R(n) 100.1.0.0/30 100.1.0.13 2 100.1.0.13 0 02:55
R(n) 100.1.0.4/30 100.1.0.17 2 100.1.0.17 0 02:27
R(n) 100.1.0.8/30 100.1.0.17 2 100.1.0.17 0 02:27
C(i) 100.1.0.12/30 0.0.0.0 1 self 0
C(i) 100.1.0.16/30 0.0.0.0 1 self 0
R(n) 100.1.1.0/24 100.1.0.13 2 100.1.0.13 0 02:55
R(n) 100.1.2.0/24 100.1.0.13 3 100.1.0.13 0 02:55
R(n) 100.1.3.0/24 100.1.0.17 2 100.1.0.17 0 02:27
C(r) 100.1.4.0/24 0.0.0.0 1 self 0
C(r) 100.2.0.0/30 0.0.0.0 1 self 0

## Slide 19: static routing
our network is a stub network (i.e., it has just one connection to an external router, r5); hence, static routes are enough for connecting it to the internet
r4
r1
r3
r2
inbound traffic
(to 100.1.0.0/16)
r5
outbound traffic
(to 0.0.0.0/0)

## Slide 20: adding a static route to r5
root@r5:~$ ip route add 100.1.0.0/16 via 100.2.0.1
root@r5:~$ ping 100.1.2.1
PING 100.1.2.1 (100.1.2.1) 56(84) bytes of data.
64 bytes from 100.1.2.1: icmp_seq=1 ttl=62 time=24.1 ms
64 bytes from 100.1.2.1: icmp_seq=2 ttl=62 time=1.11 ms
--- 100.1.2.1 ping statistics ---
2 packets transmitted, 2 received, 0% packet loss, time 1023ms
rtt min/avg/max/mdev = 1.117/12.634/24.151/11.517 ms

## Slide 21: configuring r4
step 1: configuring the default route
root@r4:~$ ip route add default via 100.2.0.2
root@r4:~$ ip route
default via 100.2.0.2 dev eth0
100.1.0.0/30 nhid 12 via 100.1.0.13 dev eth3 proto rip metric 20
100.1.0.4/30 nhid 10 via 100.1.0.17 dev eth2 proto rip metric 20
100.1.0.8/30 nhid 10 via 100.1.0.17 dev eth2 proto rip metric 20
100.1.0.12/30 dev eth3 proto kernel scope link src 100.1.0.14
100.1.0.16/30 dev eth2 proto kernel scope link src 100.1.0.18
100.1.1.0/24 nhid 12 via 100.1.0.13 dev eth3 proto rip metric 20
100.1.2.0/24 nhid 12 via 100.1.0.13 dev eth3 proto rip metric 20
100.1.3.0/24 nhid 10 via 100.1.0.17 dev eth2 proto rip metric 20
100.1.4.0/24 dev eth1 proto kernel scope link src 100.1.4.1
100.2.0.0/30 dev eth0 proto kernel scope link src 100.2.0.1

## Slide 22: configuring r4
root@r4:~$ vtysh
Hello, this is FRRouting (version 8.0.1).
Copyright 1996-2005 Kunihiro Ishiguro, et al.
r4# configure
r4(config)# router rip
r4(config-router)# route 0.0.0.0/0
r4(config-router)# quit
r4(config)# quit
r4# exit
step 2: propagating the default route into rip
begin configuration
configure the rip protocol
statically configure the default route
end of rip configuration
end configuration

## Slide 23: the default route
root@r1:~$ ip route
default nhid 12 via 100.1.0.14 dev eth0 proto rip metric 20
100.1.0.0/30 dev eth2 proto kernel scope link src 100.1.0.1
100.1.0.4/30 nhid 11 via 100.1.0.10 dev eth1 proto rip metric 20
100.1.0.8/30 dev eth1 proto kernel scope link src 100.1.0.9
100.1.0.12/30 dev eth0 proto kernel scope link src 100.1.0.13
100.1.0.16/30 nhid 12 via 100.1.0.14 dev eth0 proto rip metric 20
100.1.1.0/24 dev eth3 proto kernel scope link src 100.1.1.1
100.1.2.0/24 nhid 14 via 100.1.0.2 dev eth2 proto rip metric 20
100.1.3.0/24 nhid 11 via 100.1.0.10 dev eth1 proto rip metric 20
100.1.4.0/24 nhid 12 via 100.1.0.14 dev eth0 proto rip metric 20
100.2.0.0/30 nhid 12 via 100.1.0.14 dev eth0 proto rip metric 20
after a while, the default route has been injected (via rip) into the network

## Slide 24: checking connectivity
r5
eth0
1
eth0
2
L
r4
eth3
14
r1
H
100.1.0.12/30
100.2.0.0/30
eth0
13
root@r1:~$ ping 193.204.161.1
PING 193.204.161.1 (193.204.161.1) 56(84) bytes of data.
From 100.2.0.2 icmp_seq=1 Destination Net Unreachable
From 100.2.0.2 icmp_seq=2 Destination Net Unreachable
--- 193.204.161.1 ping statistics ---
2 packets transmitted, 0 received, +2 errors, 100% packet loss, time 999ms
any (even non-existing) destination

## Slide 25: checking connectivity
r5 is actually receiving echo request packets
root@r5:~$ tcpdump –tenni eth0
tcpdump: verbose output suppressed, use -v or -vv for full protocol decode
listening on eth0, link-type EN10MB (Ethernet), capture size 1518 bytes
11:38:43.822503 arp who-has 100.2.0.2 tell 100.2.0.1
11:38:43.824221 arp reply 100.2.0.2 is-at fe:fd:64:02:00:02
11:38:43.825890 IP 100.1.0.13 > 193.204.161.1: icmp 64: echo request seq 1
11:38:43.827139 IP 100.2.0.2 > 100.1.0.13: icmp 92: net 193.204.161.1 unreachable
11:38:44.841566 IP 100.1.0.13 > 193.204.161.1: icmp 64: echo request seq 2
11:38:44.841651 IP 100.2.0.2 > 100.1.0.13: icmp 92: net 193.204.161.1 unreachable
6 packets captured
6 packets received by filter
0 packets dropped by kernel

## Slide 26: shutting down an interface
kathara – [ lab: rip ]
r5
r4
eth1
9
eth1
10
r1
r3
r2
G
100.1.0.8/30
root@r1:~$ traceroute 100.1.0.10
traceroute to 100.1.0.10 (100.1.0.10), 64 hops max, 40 byte packets
1 100.1.0.10 (100.1.0.10) 24 ms 1 ms 1 ms
root@r1:~$ ip link set eth1 down

## Slide 27: shutting down an interface
kathara – [ lab: rip ]
r5
eth2
18
r4
eth3
14
eth1
9
eth2
1
eth1
10
r1
r3
H
100.1.0.12/30
r2
eth2
17
eth0
13
G
I
100.1.0.16/30
100.1.0.8/30
r1 attempts forwarding the packet using the default route
?
root@r1:~$ traceroute 100.1.0.10
traceroute to 100.1.0.10 (100.1.0.10), 64 hops max, 40 byte packets
1 100.1.0.14 (100.1.0.10) 1 ms 1 ms 1 ms
2 * * *
3 * * *

## Slide 28: shutting down an interface
kathara – [ lab: rip ]
r5
eth2
18
r4
eth3
14
eth1
9
eth2
1
eth1
10
r1
r3
H
100.1.0.12/30
r2
eth2
17
eth0
13
G
I
100.1.0.16/30
100.1.0.8/30
after a while, routing information has been updated
root@r1:~$ traceroute 100.1.0.10
traceroute to 100.1.0.10 (100.1.0.10), 64 hops max, 40 byte packets
1 100.1.0.14 (100.1.0.14) 1 ms 1 ms 1 ms
2 100.1.0.10 (100.1.0.10) 5 ms 2 ms 1 ms

## Slide 29: about redistribute connected
by default (i.e., without further configuration) RIP already propagates information about all directly connected subnets attached to RIP-speaking interfaces
redistribute connected forces RIP to propagate information about all connected subnets
the semantic of redistribute connected applies to all routing protocols
the default behavior does not
  some protocols (e.g., bgp) are lazier, and do not propagate anything unless explicitly told to do so