## Slide 1: Kathará lab
one bridge
Version | 3.0
Author(s) | L. Ariemma, T. Caiazzi, G. Di Battista
E-mail | contact@kathara.org
Web | http://www.kathara.org/
Description | One bridge and four computers are connected; the learning features of the bridge are experienced

## Slide 2: copyright notice
All the pages/slides in this presentation, including but not limited to, images, photos, animations, videos, sounds, music, and text (hereby referred to as “material”) are protected by copyright.
This material, with the exception of some multimedia elements licensed by other organizations, is property of the authors and/or organizations appearing in the first slide.
This material, or its parts, can be reproduced and used for didactical purposes within universities and schools, provided that this happens for non-profit purposes.
Information contained in this material cannot be used within network design projects or other products of any kind.
Any other use is prohibited, unless explicitly authorized by the authors on the basis of an explicit agreement.
The authors assume no responsibility about this material and provide this material “as is”, with no implicit or explicit warranty about the correctness and completeness of its contents, which may be subject to changes.
This copyright notice must always be redistributed together with the material, or its portions.

## Slide 3: network topology
eth3
eth0
eth1
eth2
eth0
eth0
eth0
eth0
A
B
C
D
b1
pc1
pc2
pc4
pc3
0:1
0:2
0:3
0:4
0:b4
0:b3
0:b2
0:b1

## Slide 4: the lab.conf
pc1[0]="A/00:00:00:00:00:01"
pc1[image]="kathara/core"
pc1[ipv6]="false"
pc2[0]="B/00:00:00:00:00:02"
pc2[image]="kathara/core"
pc2[ipv6]="false"
pc3[0]="C/00:00:00:00:00:03"
pc3[image]="kathara/core"
pc3[ipv6]="false"
pc4[0]="D/00:00:00:00:00:04"
pc4[image]="kathara/core"
pc4[ipv6]="false"
lab.conf – part 1
b1[0]="A/00:00:00:00:00:b1"
b1[1]="B/00:00:00:00:00:b2"
b1[2]="C/00:00:00:00:00:b3"
b1[3]="D/00:00:00:00:00:b4"
b1[image]="kathara/core"
b1[ipv6]="false"
lab.conf – part 2

## Slide 5: how to create a bridge
we want device b1 to be a bridge
Linux has an already available software bridge
  we will use it
  there are different utilities that manages different parts of the bridge
    ip link
    brctl
    bridge
    …

## Slide 6: how to create a bridge
the command that lets b1 to be a bridge follows
  the name of the device remains b1, the internal name we give to the bridge is mainbridge
root@b1:~$ ip link add name mainbridge type bridge
the type of the newly created object
the internal name of the bridge

## Slide 7: remarks
b1 is a name of the Kathará device
mainbridge is the name of a bridge inside b1

## Slide 8: connect interfaces to a bridge
the bridge needs then to be connected to some network interfaces
connecting an interface to a bridge is called "enslaving"
  it is done setting the bridge as the master of that interface
root@b1:~$ ip link set dev eth0 master mainbridge
the name of the bridge to connect the interface
the name of the interface to be connected

## Slide 9: bringing up the bridge
the bridge is born with its state DOWN
  this means that it is switched off
the following command allows to switch up/down a bridge (or even a network interface)
  it can be also used for ethX interfaces
root@b1:~$ ip link set up dev mainbridge
the desired state
the name of the bridge to be brought on

## Slide 10: bridge ageing time
the ageing time is the number of seconds that a MAC address will be kept in the FDB (Filtering Data Base)
by default, it is set to 300 (5 minutes)
to change the ageing time:
root@b1:~$ brctl setageing mainbridge 600
utility to control bridges
name of the bridge
new ageing time, set in seconds

## Slide 11: b1.startup
ip link add name mainbridge type bridge
ip link set dev eth0 master mainbridge
ip link set dev eth1 master mainbridge
ip link set dev eth2 master mainbridge
ip link set dev eth3 master mainbridge
ip link set up dev mainbridge
brctl setageing mainbridge 600
b1.startup

## Slide 12: let's start the lab

## Slide 13: show the FDB of a bridge
to show the FDB of a bridge, the brctl command can be used
root@b1:~$ brctl showmacs mainbridge
port no mac addr is local? ageing timer
1 00:00:00:00:00:b1 yes 0.00
1 00:00:00:00:00:b1 yes 0.00
2 00:00:00:00:00:b2 yes 0.00
2 00:00:00:00:00:b2 yes 0.00
3 00:00:00:00:00:b3 yes 0.00
3 00:00:00:00:00:b3 yes 0.00
4 00:00:00:00:00:b4 yes 0.00
4 00:00:00:00:00:b4 yes 0.00

## Slide 14: auto-learning local interfaces
the Linux bridge automatically learns the MAC addresses of all its local interfaces
  he already knows them because they are hosted on the same device
the ageing timer is shown as 0.00 because those entries never expire

## Slide 15: the port column
in the brctl showmacs <bridge_name> command, the first column of the output is called port
the port indicates the number of the virtual port of the bridge
a linux bridge has a hard limit (hardcoded in the Kernel) of 1024 ports
the ports are assigned starting from 1 in the order they are connected to interfaces
  the order of the commands that enslave the interfaces

## Slide 16: learn dynamic FDB entries – part 1
if a packet is sent from a PC, the bridge will automatically learn its MAC address
try to send a packet from pc1 to pc2 using scapy
root@pc1:~$ scapy
>>> p=Ether(dst='00:00:00:00:00:02', src='00:00:00:00:00:01')
>>> sendp(p, iface='eth0')
Sent 1 packets.

## Slide 17: learn dynamic FDB entries – part 2
now, take a look at the FDB of mainbridge again
root@b1:~$ brctl showmacs mainbridge
port no mac addr is local? ageing timer
1 00:00:00:00:00:01 no 18.54
1 00:00:00:00:00:b1 yes 0.00
1 00:00:00:00:00:b1 yes 0.00
2 00:00:00:00:00:b2 yes 0.00
2 00:00:00:00:00:b2 yes 0.00
3 00:00:00:00:00:b3 yes 0.00
3 00:00:00:00:00:b3 yes 0.00
4 00:00:00:00:00:b4 yes 0.00
4 00:00:00:00:00:b4 yes 0.00
the MAC address of pc1 has been learnt
this timer always increases, showing how long the entry has been in the FDB

## Slide 18: bridge ageing time
the "ageing timer" of the previous slide always increases, showing how long the entry has been in the FDB
eventually, the entry expires and simply disappears

## Slide 19: exercises
why, after the above experiment, in the FDB there is no entry for pc2?
try to sniff from pc3 while sending the packet from pc1 to pc2, what happens?
send a "reply" packet from pc2, how the FDB changes?
try again to sniff from pc3 while sending the packet from pc1 to pc2, is the result the same?
try to send packets with the wrong source address