## Slide 1: data centers’ architecture and routing
Version | 3.0
Author(s) | L. Ariemma, G. Di Battista, M. Patrignani, M. Scazzariello, T. Caiazzi
E-mail | contact@kathara.org
Web | http://www.kathara.org/
Description | Basics of Data Centers’ Routing

## Slide 2: copyright notice
all the pages/slides in this presentation, including but not limited to, images, photos, animations, videos, sounds, music, and text (hereby referred to as “material”) are protected by copyright
this material, with the exception of some multimedia elements licensed by other organizations, is property of the authors and/or organizations appearing in the first slide
this material, or its parts, can be reproduced and used for didactical purposes within universities and schools, provided that this happens for non-profit purposes
any other use is prohibited, unless explicitly authorized by the authors on the basis of an explicit agreement
this copyright notice must always be redistributed together with the material, or its portions

## Slide 3: Multi-Path
in a nutshell

## Slide 4: Multi-Path
data center architectures allow to establish several paths between pairs of nodes
Multi-Path routing is used to
  distribute and balance the traffic among different paths
  increase the fault tolerance

## Slide 5: Multi-Path
allows to have more than one next-hop for the same prefix in the FIB (Forwarding Information Base)
needs kernel support
  the main OSes and routers support it
different usage policies can be applied
packets of the same flow should use the same path
  reordering packets is computationally heavy

## Slide 6: Equal-Cost Multi-Path (ECMP)
a specific approach to Multi-Path
exploits paths to the same destination that have the same “cost”
  e.g., same IGP cost, same number of hops
allows to choose among the available paths in a uniform way
often used in Fat-Tree data centers
  we’ll get there in a couple of slides

## Slide 7: how packets are forwarded
for each packet, the kernel decides the FIB entry to be used
different policies are allowed
  hash-based policy
    Layer-3 hash (src IP, dst IP)
    Layer-4 hash (src IP, dst IP, src port, dst port, protocol)
  round-robin

## Slide 8: Hyper-scale Data Centers
main concepts

## Slide 9: a high-level architecture
Internet connections
  multiple redundant high-speed fiber optic links
fabric
  infrastructure designed to transport packets between servers and between servers and Internet
server farm
  host applications and services

## Slide 10: a high-level architecture
server farm
Internet
data center fabric

## Slide 11: fabric architecture
why Fat-Trees?

## Slide 12: overview – fabric architecture
real-life data centers
service model
data center network
  traffic flow directions
  requirements
  components
  topologies

## Slide 13: real data center information – figures
links are fiber optic links
each link in the fabric is at least at 100Gb/s
each switch is at least of 64 ports
about 5,000 switches/routers
about 60,000 servers

## Slide 15: data center failures – yearly report
statistics by Google (2008) in a portion of data center composed of 1,800 servers:
1,000 individual machine (switch/router or server) failures
thousands of hard drive failure
1 power distribution unit failure
  down for 500/1000 machines for 6 hours
1 cluster complete rewire (not simultaneously)

## Slide 16: data center service models
three different service models
  on-premise data centers
    built, owned and operated by a company
    often housed in a building of the organization
  colocation data centers
    built and owned by a company that rents space within the data center to other companies
      the hosting company manages the infrastructure (building, cooling, bandwidth, security etc.)
      the hosted companies provides the components, including servers, storage, and firewalls
  cloud data centers
    applications and data are hosted by a cloud service provider such as Amazon Web Services (AWS), Microsoft Azure, and Google Cloud Platform (GCP)

## Slide 17: traffic flows inside a data center
two types of flows can be identified
  traffic exiting or entering the data center
    also called “north-south traffic”
    data sent/received via Internet
  server-to-server communications
    also called “east-west traffic”: in data center schemata servers are typically drawn side-by-side
    primarily, supports micro-services and distributed architectures

## Slide 18: traffic flows inside a data center
server farm
Internet
data center fabric
north-south traffic
east-west traffic

## Slide 19: data center network requirements
support high-bandwidth server-to-server communication
  applications that rely on cluster computations, such as Hadoop or Spark, can involve hundreds or thousands of servers
  customer’s containers/virtual machines (VMs) are distributed across multiple servers but need to communicate seamlessly
  microservice architectures heavily rely on server-to-server communication
scale
  data centers range from a few hundred to a hundred thousand servers in a single physical location
resilience
  data center applications are designed to work in presence of failures

## Slide 20: data center network components
data center nodes can be connected by using two network component types
  specialized hardware
    proprietary hardware that can scale to clusters of thousands of nodes with high bandwidth
      e.g., Google Jupiter and InfiniBand switches
    expensive option
  commodity switches and routers
    cheap option
    widely adopted, this is the option we consider in the following

## Slide 21: topology requirements
scalability
  it should be possible to expand the data center
  in other words, it must be possible to buy and deploy hardware similar to the one already deployed
bandwidth
  hosts in the fabric should communicate with each other using the full bandwidth of their NICs

## Slide 22: data center network topologies
several topologies have been proposed
  Clos
  Fat-Tree
  VL2
  Jellyfish
  Xpander
  DCell
  ...

## Slide 23: Clos topology
invented by Edson Erwin in 1938 to address scalability issues in telephone networking
  formalized by Charles Clos in 1953
the original problem was allowing N contemporary connections from N input lines to N output lines without using a single crossbar switch

## Slide 24: Fat-Tree topology
Fat-Trees were originally introduced by Charles Leiserson in 1985
the Fat-Tree is a special case of a Clos
typical Fat-Tree architectures today consist of three level of nodes (switches/routers)
high redundancy
constant bisection of the available bandwidth
typically, nodes have the same characteristics
  easier to stock spare equipments

## Slide 25: Fat-Tree parameters
the Fat-Tree is a modular topology
two parameters define a Fat-Tree
  radix of the nodes (even number, denoted by 2K)
    number of available ports
  redundancy factor (denoted by R)
usually, if the radix of a node is 2K it has K connections towards the north and K connections towards the south
  different choices are possible, but not considered here

## Slide 26: Fat-Tree nodes
Leaf
  node connected to the server farm
Spine
  node north of Leaves and south of ToF nodes
Point of Delivery (PoD)
  set of fully interconnected Leaves and Spines
Top of Fabric (ToF)
  set of top nodes that provide inter-PoD communication

## Slide 27: an example of Fat-Tree: FT(K=2,R=2)
ToF (Top of Fabric)
Leaf
Spine
aggregation layer
PoD (Point of Delivery)
Server Farm

## Slide 28: redundancy factor (R)
number of links between a ToF node and a PoD
allow to connect more PoDs reducing the redundancy
Server Farm
R = 2
Server Farm
R = 1

## Slide 29: multi-plane Fat-Tree
when KR the Fat-Tree is called multi-plane
the ToF nodes are partitioned in sets called planes
Server Farm
Plane A
Plane B

## Slide 30: example of a multi-plane Fat-Tree
diagram from the IETF RIFT Draft

## Slide 31: connecting a Fat-Tree to the Internet
two strategies
  usage of a dedicated PoD
  usage of ToFs
Internet
Internet

## Slide 32: routing in Fat-Trees
why BGP?

## Slide 33: overview – routing
why routing and not switching?
the choice of the routing protocols
why using BGP in Fat-Tree data centers?
inter-domain routing VS data center routing
BGP in the data center

## Slide 34: why routing and not switching?
 | Pros | Cons
Switching (L2) | No configuration needed | STP protocol has no multipath support Using VLANs for load balancing is tricky Broadcast traffic flooding the network
Routing (L3) | Multipath support | Need of routing protocols Complex configuration Need of automating the configuration

## Slide 35: choosing a routing protocol
there are many possibilities, among them
  a classical IGP protocol (e.g., OSPF, IS-IS)
  BGP (most used in Hyperscale data centers)
  RIFT (Routing In Fat-Trees)
    Under standardization at IETF
    Designed for Fat-Trees topologies
  OpenFabric
    IS-IS variant created for Clos topologies
  SDN Protocols

## Slide 36: why using BGP in Fat-Tree data centers?
BGP has several stable and robust implementations, even open-source
  e.g., FRRouting, Quagga
BGP generates less flooding than common IGPs (IS-IS, OSPF, etc.)
  if a received update does not change the best route, a BGP speaker does not propagate the update
BGP natively supports ECMP (Equal-Cost Multi-Path)
  Fat-Trees have many paths with the same length

## Slide 37: why using eBGP? (and not iBGP)
the most obvious choice would be to use iBGP since the data center networks is under the same administration
however, eBGP is always used because
  eBGP is easier to setup, no need for IGP
    with iBGP, the IGP would compute routes
  iBGP multipath support has some limitations
    can be overcame, but it is complex

## Slide 38: inter-domain routing VS DC routing
inter-domain routing | data centers’ routing
the internet has relatively sparse connectivity | data centers’ networks have very dense connectivity
stability is preferred over quick convergence | quick convergence is preferred over stability
the aim is computing a single best path for each destination | the aim is computing multiple paths to each destination

## Slide 39: BGP in the data center
BGP was primarily devised for inter-domain routing
  default configurations are not suitable in a data center
needs some tweaks described in RFC-7938
  AS numbers assignment
  ECMP policy relax
  timer adjustment

## Slide 40: AS numbers assignment
global ASNs are not used in the data center
  they can be misleading
    because operators associate them with names
  they are dangerous
    an accidental leakage of the internal BGP notifications to the internet may be disruptive
private ASNs are generally used
  the 2-byte ASNs allow only 1,023 private ASes in the range 64512–65534
  the 4-byte ASNs support almost 95 million private ASes in the range 4,200,000,000–4,294,967,294

## Slide 41: ASes and routers
the most obvious choice would be assigning a different ASN to each node
however, this approach would lead to BGP path exploration issues

## Slide 42: BGP path exploration
immediately after a fault there is a transient period when inconsistent AS-paths are propagated in the network
  routers have plenty of alternatives and jump from one to another before all alternatives are withdrawn
  each best route change is propagated again by the routers
  lots of useless BGP updates are transmitted
since data centers’ topologies are dense and hence have a lot of cycles this problem has to be addressed

## Slide 43: the problem of BGP path exploration
*>193.204.0.0/15 [L2]
[L1,S1,L2]
*>193.204.0.0/15 [L2]
S2
S1
L2
L1
because of the adopted AS scheme several fake routes could be possible during path exploration
193.204.0.0/15
[L2]
[L2]
[S1,L2]
[S2,L2]
*>193.204.0.0/15 [S1,L2]
*= [S2,L2]
X
[L1,S1,L2]
*>193.204.0.0/15 [L2]

## Slide 44: the ASes scheme of choice
each Leaf is a different AS
the Spine nodes of each PoD belong to the same AS
the ToF nodes of the same plane belong to the same AS
BEWARE: there are NO iBGP peerings

## Slide 45: the ASes scheme of choice – multi-plane
Server Farm
Plane A
Plane B

## Slide 46: multiple paths between Leaves
the adopted AS scheme allows for multiple paths between pairs of Leaves
  in a FT(K=2,R=2) only two paths are possible between two Leaves of the same PoD
    they don’t leave the PoD

## Slide 47: multiple paths between Leaves
the adopted AS scheme allows for multiple paths between pairs of Leaves
  in a FT(K=2,R=2) eight paths are possible between two Leaves of different PoDs

## Slide 48: BGP and ECMP
BGP natively supports ECMP
by default, BGP considers two announcement of the same prefix “equal” if they are equal in each best-path selection criterion except for the last one
  lowest router-id of the announcing peer
to enable multi-path, BGP requires that the AS-paths selected for multi-path match exactly
  not just they have equal-length but equal AS numbers inside

## Slide 49: BGP multi-path relax
when the AS_PATH lengths of different announcements for the same prefix are the same, the best-path algorithm skips checking for exact match of the AS numbers
this modification is often called “as-path multipath-relax”
  different vendors may use different names
really needed for using dual attached servers and multi-plane Fat-Trees

## Slide 50: tuning BGP timers
there are four main timers that are responsible for BGP behaviour
  advertisement interval timer
  keepalive timer
  hold timer
  connect timer

## Slide 51: advertisement interval timer
announcements that need to be sent to a neighbor are bunched together and sent together only when the interval expires
  then the timer is reset for that neighbor
the default value for eBGP is 30s
  in interdomain routing this improves stability and reduces the number of multiple updates for the same prefix
in data centers is set to 0s
  it is required for fast convergence

## Slide 52: keepalive and hold timers
each BGP peer sends periodic keepalive messages to its neighbors according to the keepalive timer
when a peer doesn’t receive a keepalive for a period greater than the hold timer
  the connection is dropped
  all the announcements received are considered invalid
  the peer tries to re-establish the connection
by default, the keepalive timer is 60s and the hold timer is 180s
in data centers timers of 3s and 9s are used, respectively

## Slide 53: connect timer
when a connection to a peer fails, BGP waits for the connect timer expiration before attempting to reconnect
  the connect timer by default is 60s
  this can delay session re-establishment when a link recovers from a failure or a node powers up
in data centers it is set to 10s

## Slide 54: automating the configuration
unnumbered interfaces
  used to establish peerings specifying the interface name rather than the IP address and the remote AS number
peer groups
  used to specify policies for groups of peers

## Slide 55: connecting the servers
Servers
Containers or VMs
IPs are assigned directly to the servers
each Leaf announces its server’s prefix

## Slide 56: disadvantages
containers/VMs share the same IP prefix of the server
  no possibility to move containers between servers without IP remapping
tenants must follow the IP plan of the data center
  cannot expose containers with custom IPs
there is no isolation between
  the data center traffic and the tenants traffic
  different tenants

## Slide 57: basic Fat-Tree lab
hands on Kathará

## Slide 58: lab pre-conditions
Linux and macOS
  no specific requirement
Windows
  WSL 2 does not support Multi-Path
  need to fallback to Hyper-V Docker backend
    open Docker Desktop and go to Settings (cog in the top-right corner)
    unselect the “Use the WSL 2 based engine” checkbox
    click “Apply & restart”
  or create a VM with a Linux distribution

## Slide 59: naming convention
tof_x_y_z
  x: plane number
  y: level, always 2
  z: ToF number
spine_x_y_z
  x: PoD number
  y: level, always 1
  z: Spine number
leaf_x_y_z
  x: PoD number
  y: level, always 0
  z: Leaf number
server_x_y_z
  x: PoD number
  y: corresponding Leaf number
  z: server number

## Slide 60: lab topology
spine_1_1_2
spine_1_1_1
leaf_1_0_1
leaf_1_0_2
spine_2_1_1
spine_2_1_2
tof_1_2_1
tof_1_2_2
server_1_1_1
server_1_1_2
server_1_2_1
server_1_2_2
server_2_1_1
server_2_1_2
server_2_2_1
server_2_2_2
leaf_2_0_1
leaf_2_0_2
A
C
U
V
Z
M
F
P
W
O
L
N
K
E
B
D
Q
R
S
T
10.0.0.16/30
10.0.0.0/30
10.0.0.12/30
10.0.0.8/30
10.0.0.4/30
10.0.0.44/30
10.0.0.32/30
10.0.0.40/30
10.0.0.36/30
10.0.0.24/30
10.0.0.20/30
10.0.0.28/30
10.0.0.60/30
10.0.0.52/30
10.0.0.56/30
10.0.0.48/30
201.1.1.0/24
201.1.2.0/24
201.2.2.0/24
201.2.1.0/24
202.2.2.0/24
202.2.1.0/24
I
G
H
J
202.1.1.0/24
202.1.2.0/24
AS64512
AS64514
AS64513
AS64515
AS64516
AS64517
AS64518

## Slide 61: ToF configuration example
router bgp 64518
timers bgp 3 9
bgp router-id 192.168.0.14
no bgp ebgp-requires-policy
bgp bestpath as-path multipath-relax
neighbor fabric peer-group
neighbor fabric remote-as external
neighbor fabric advertisement-interval 0
neighbor fabric timers connect 10
neighbor eth0 interface peer-group fabric
neighbor eth1 interface peer-group fabric
neighbor eth2 interface peer-group fabric
neighbor eth3 interface peer-group fabric
address-family ipv4 unicast
neighbor fabric activate
maximum-paths 64
exit-address-family
bgpd.conf
set keepalive and hold timers
BGP multi-path relax
create a peer-group
all peers of the group are eBGP. The remote ASN is inferred
set advertisement interval timer
set connect timer
add interfaces to peer-group for unnumbered peering
enable A.F. to peer-group
maximum Multi-Path possibilities

## Slide 62: Spine configuration example
router bgp 64514
timers bgp 3 9
bgp router-id 192.168.0.5
no bgp ebgp-requires-policy
bgp bestpath as-path multipath-relax
neighbor TOR peer-group
neighbor TOR remote-as external
neighbor TOR advertisement-interval 0
neighbor TOR timers connect 10
neighbor eth0 interface peer-group TOR
neighbor eth1 interface peer-group TOR
neighbor fabric peer-group
neighbor fabric remote-as external
neighbor fabric advertisement-interval 0
neighbor fabric timers connect 10
neighbor eth2 interface peer-group fabric
neighbor eth3 interface peer-group fabric
bgpd.conf – part 1
address-family ipv4 unicast
neighbor fabric activate
neighbor TOR activate
maximum-paths 64
exit-address-family
bgpd.conf – part 2

## Slide 63: Leaf configuration example
router bgp 64512
timers bgp 3 9
bgp router-id 192.168.0.1
no bgp ebgp-requires-policy
bgp bestpath as-path multipath-relax
neighbor TOR peer-group
neighbor TOR remote-as external
neighbor TOR advertisement-interval 0
neighbor TOR timers connect 10
neighbor eth0 interface peer-group TOR
neighbor eth1 interface peer-group TOR
address-family ipv4 unicast
neighbor TOR activate
network 201.1.1.0/24 network 201.1.2.0/24
maximum-paths 64
exit-address-family
bgpd.conf
announce the server prefixes

## Slide 64: data plane
root@spine_1_1_1:/# route -n
Kernel IP routing table
Destination Gateway Genmask Flags Metric Ref Use Iface
10.0.0.4 0.0.0.0 255.255.255.252 U 0 0 0 eth0
10.0.0.12 0.0.0.0 255.255.255.252 U 0 0 0 eth1
10.0.0.24 0.0.0.0 255.255.255.252 U 0 0 0 eth2
10.0.0.28 0.0.0.0 255.255.255.252 U 0 0 0 eth3
201.1.1.0 10.0.0.5 255.255.255.0 UG 20 0 0 eth0
201.1.2.0 10.0.0.5 255.255.255.0 UG 20 0 0 eth0
201.2.1.0 10.0.0.13 255.255.255.0 UG 20 0 0 eth1
201.2.2.0 10.0.0.13 255.255.255.0 UG 20 0 0 eth1
202.1.1.0 10.0.0.26 255.255.255.0 UG 20 0 0 eth2
202.1.2.0 10.0.0.26 255.255.255.0 UG 20 0 0 eth2
202.2.1.0 10.0.0.26 255.255.255.0 UG 20 0 0 eth2
202.2.2.0 10.0.0.26 255.255.255.0 UG 20 0 0 eth2
unable to view multi-path routes

## Slide 65: data plane
root@spine_1_1_1:/# ip route
10.0.0.0/30 dev eth0 proto kernel scope link src 10.0.0.2
10.0.0.8/30 dev eth1 proto kernel scope link src 10.0.0.10
10.0.0.16/30 dev eth2 proto kernel scope link src 10.0.0.17
10.0.0.20/30 dev eth3 proto kernel scope link src 10.0.0.21
201.1.1.0/24 nhid 12 via 10.0.0.1 dev eth0 proto bgp metric 20
201.1.2.0/24 nhid 12 via 10.0.0.1 dev eth0 proto bgp metric 20
201.2.1.0/24 nhid 11 via 10.0.0.9 dev eth1 proto bgp metric 20
201.2.2.0/24 nhid 11 via 10.0.0.9 dev eth1 proto bgp metric 20
202.1.1.0/24 nhid 16 proto bgp metric 20
nexthop via 10.0.0.18 dev eth2 weight 1
nexthop via 10.0.0.22 dev eth3 weight 1
202.1.2.0/24 nhid 16 proto bgp metric 20
nexthop via 10.0.0.18 dev eth2 weight 1
nexthop via 10.0.0.22 dev eth3 weight 1
202.2.1.0/24 nhid 16 proto bgp metric 20
nexthop via 10.0.0.18 dev eth2 weight 1
nexthop via 10.0.0.22 dev eth3 weight 1
202.2.2.0/24 nhid 16 proto bgp metric 20
nexthop via 10.0.0.18 dev eth2 weight 1
nexthop via 10.0.0.22 dev eth3 weight 1
command to manage routing tables
multiple next-hop for the same prefix

## Slide 66: control plane
spine_1_1_1# show ip bgp
BGP table version is 8, local router ID is 192.168.0.6, vrf id 0
Default local pref 100, local AS 64514
Status codes: s suppressed, d damped, h history, * valid, > best, = multipath,
i internal, r RIB-failure, S Stale, R Removed
Nexthop codes: @NNN nexthop's vrf id, < announce-nh-self
Origin codes: i - IGP, e - EGP, ? - incomplete
Network Next Hop Metric LocPrf Weight Path
*> 201.1.1.0/24 10.0.0.5 0 0 64512 i
*> 201.1.2.0/24 10.0.0.5 0 0 64512 i
*> 201.2.1.0/24 10.0.0.13 0 0 64513 i
*> 201.2.2.0/24 10.0.0.13 0 0 64513 i
*> 202.1.1.0/24 10.0.0.26 0 64518 64517 64515 i
*= 10.0.0.30 0 64518 64517 64515 i
*> 202.1.2.0/24 10.0.0.26 0 64518 64517 64515 i
*= 10.0.0.30 0 64518 64517 64515 i
*> 202.2.1.0/24 10.0.0.26 0 64518 64517 64516 i
*= 10.0.0.30 0 64518 64517 64516 i
*> 202.2.2.0/24 10.0.0.26 0 64518 64517 64516 i
*= 10.0.0.30 0 64518 64517 64516 i
Displayed 8 routes and 12 total paths

## Slide 67: Multi-Path traceroute
traditional traceroute may provide hard-to-interpret or even misleading results when used in presence of ECMP
Multi-Path traceroute tools generate packet header contents to obtain a more precise picture of the actual routes of packets
  allow all probes towards a destination to follow the same path in the presence of per-flow load balancing
  allow a user to distinguish between the presence of per-flow load balancing and per-packet load balancing

## Slide 68: Multi-Path traceroute
two different tools:
  paris-traceroute
    traceroute designed to work in presence of Multi-Path and load balancers
  dublin-traceroute
    based on the paris-traceroute
    adds a NAT detection technique
    introduces visualization and analysis tools

## Slide 69: dublin-traceroute example output

## Slide 70: bibliography and further readings
[Caiazzi ‘22] Caiazzi, Scazzariello, Alberro, Ariemma, Castro, Grampin, Di Battista, “Sibyl: a Framework for Evaluating the Implementation of Routing Protocols in Fat-Trees“, NOMS 2022
[Caiazzi ‘21] Caiazzi, Scazzariello, Ariemma, “VFTGen: a Tool to Perform Experiments in Virtual Fat Tree Topologies“, IM 2021
[Caiazzi ‘19] Caiazzi, “Software Defined Data Centers: methods and tools for routing protocol verification and comparison”, Ms. Thesis, Roma Tre University, 2019
[Dutt ‘17] Dutt, “BGP in the Data Center”, O’Reilly, 2017
[RFC-7938] Lapukhov, Premji, “Use of BGP for Routing in Large-Scale Data Centers” Internet Engineering Task Force (IETF) Request for Comments: 7938

## Slide 71: how to handle multiple tenants?
again, why BGP?

## Slide 72: overview – multiple tenants
requirements
  servers’ architecture requirements
  orchestration requirements
  tenant requirements
tunneling protocols
VXLAN
EVPN-BGP

## Slide 73: servers' architecture requirements
having services directly on bare metal is not used
  too many physical servers needed
  no way to scale if more resources are requested
  no isolation between different services on the same server
support a virtual layer of containers or VMs
  high-availability guaranteed via orchestration
  useful for resource-slicing
  complete isolation between different containers or VMs on the same server
    possibility to assign containers or VMs to different tenants

## Slide 74: orchestration requirements
an orchestrator is a software that manages the lifecycle of containers/VMs
  creates, moves, and destroys containers/VMs
needed for
  optimal resource allocation, handling failures, management
when moving a container/VM
  possibility to keep network configurations (MAC/IP)
  minimal downtime

## Slide 75: tenant requirements
each tenant wants to independently manage its own private IP address space
  containers/VMs traffic must be segregated between tenants and between the data center traffic

## Slide 76: consequence of requirements
server, orchestration, and tenant requirements have a consequence
  usage of tunnels

## Slide 77: tunneling protocol requirements
minimal configuration
encapsulate the traffic of each tenant
  an identifier of the tenant is needed
encapsulation in Layer-4
  to fully exploit IP Multi-Path
  to traverse routers
    data center fabric is Layer-3
  to traverse Internet
    different data centers must interconnect via Internet transparently (to create the so called regions)

## Slide 78: possible choices for tunneling
VLAN
  can be used only in L2, the data center is L3
MPLS
  each router must be configured for each new tenant
  traversing Internet requires ISP to configure intermediate routers
VXLAN
  created ad-hoc 

## Slide 79: VXLAN
Virtual eXtensible Local Area Network (RFC-7348)
designed to address the need for overlay networks within virtualized data centers accommodating multiple tenants
encapsulates Layer-2 frames into UDP packets

## Slide 80: VXLAN terminology
VNI: VXLAN Network Identifier
  identifier of a specific VXLAN tunnel
  similar to the VLAN ID
  24 bit address space, more than 16M possible VNIs
VTEP: VXLAN Tunnel End Point
  device (physical or virtual) that encapsulates and decapsulates VXLAN packets

## Slide 81: VXLAN encapsulation
overhead of 50 bytes
random Source Port to fully exploit Multi-Path

## Slide 82: MAC-to-VTEP Table
hosted in each VTEP
similar to the switch forwarding table
for each VNI the VTEP keeps a table of pairs <mac,ip>, that associates MAC Addresses and destination VTEP IPs
each physical (or VLAN) L2 interface of a VTEP is assigned to a VNI
  the MAC addresses learned on such interfaces are local, and the IPs of their pairs is replaced by the word local

## Slide 83: MAC-to-VTEP Table
when a VTEP receives a frame destinated to a MAC Address m from a local interface belonging to a certain VNI, it checks for the existence (in the VNI) of a pair <m,i> containing m
  if the pair exists
    if i is local, then the frame is forwarded to the L2 port where m is located
    otherwise, the VTEP encapsulates the frame, and sends the resulting packet to the destination VTEP IP i
  if not, the frame is sent to all the other VTEPs (encapsulated) and to all the local ports of that VNI

## Slide 84: VXLAN transport
VTEP
VTEP
Host 1
Host 2
193.204.0.0/15
10.0.0.0/24
10.0.0.0/24
.1
0:A
.2
0:B
L2 Packets
VXLAN Packets, VNI 100
L2 Packets
0:A 100 local
0:B 100 193.204.0.2
0:B 100 local
0:A 100 193.204.0.1
.1
.2

## Slide 85: how to handle broadcast traffic
two types of broadcast must be handled
  traffic directed to the MAC broadcast address
    e.g., ARP traffic
  traffic directed to a MAC address that has not been learned
IP multicast groups are used by default
  each VNI is assigned to an IP multicast group of the underlay network and each VTEP subscribes itself to each group of its VNIs
  the multicast group of a VNI is used only to send the broadcast traffic

## Slide 86: disadvantages of multicast and alternatives
multicast must be enabled in the underlay network
  it may require to deploy several protocols
    e.g., IGMP, IGMP Snooping, PIM, ….
  complex configuration
if multicast is not enabled, broadcast frames are duplicated and sent unicast to all the VTEPs of the VNI
proxy ARP techniques can be used to mitigate broadcast traffic

## Slide 87: EVPN-BGP
Ethernet VPN (RFC-7432 and RFC-8365)
uses MP-BGP with specific AFI/SAFI
  Address Family Identifier/Subsequent AFI
  AFI=25 (L2VPN) – SAFI=70 (EVPN)
advertises MAC Addresses of VNIs using BGP updates
a VTEP automatically learns local MAC Addresses and advertises them to all other VTEPs (of the same VNI)
VTEP proxies ARP requests to limit broadcast traffic

## Slide 88: VXLAN and EVPN-BGP transport
VTEP
VTEP
Host 1
Host 2
193.204.0.0/15
.1
.2
10.0.0.0/24
10.0.0.0/24
.1
0:A
.2
0:B
0:A 100 local
0:B 100 193.204.0.2
0:B 100 local
0:A 100 193.204.0.1
eBGP multihop peering
0:A 100 local
0:A 100 193.204.0.1
0:A 100 193.204.0.1
0:B 100 193.204.0.2
0:B
0:A
(+ BGP Router)
(+ BGP Router)

## Slide 89: VXLAN and EVPN-BGP Lab
time to use Kathará

## Slide 90: topology
.1
.2
s1
A
vtep1
vtep2
B
C
10.0.0.0/24
193.204.0.0/15
10.0.0.0/24
s2
.1
.2

## Slide 91: lab base config
ifconfig eth0 10.0.0.1/24 up
ip link set dev eth0 mtu 1450
/etc/init.d/apache2 start
s1.startup
ifconfig eth0 10.0.0.2/24 up
ip link set dev eth0 mtu 1450
/etc/init.d/apache2 start
s2.startup
s1[0]=A
vtep1[0]=A
vtep1[1]=B
vtep2[0]=C
vtep2[1]=B
s2[0]=C
lab.conf
ifconfig eth1 193.204.0.1/30 up
vtep1.startup
ifconfig eth1 193.204.0.2/30 up
vtep2.startup

## Slide 92: MTU
need to set manual MTU of each device’s interface associated to a VNI
when a frame is encapsulated by a VTEP, if its size is greater than 1450 (LAN MTU – VXLAN overhead)
  the frame is dropped
  an ICMP “packet too big” message is sent back

## Slide 93: configuring a bridge/router with VTEPs
we need to configure a Kathara device that is able to:
  act as a bridge on L2 ports
    able to perform L2 learning
  act as a router on the ports on the underlay networks
    able to establish BGP peerings
    able to encapsulate/decapsulate VXLAN traffic

## Slide 94: VTEP configuration
create bridge facilities (aka companion bridges)
  one virtual bridge for each VNI
    ideally, one could have just one bridge with ports assigned to VLANs corresponding to VNIs; hard to do with Linux bridges
attach the collision domains associated to a VNI to the companion bridge of that VNI
configure the base BGP peerings
  enable the AFI/SAFI of EVPN
configure VXLAN

## Slide 95: vtep e-BGP configuration
router bgp 1
neighbor 193.204.0.2 remote-as 2
address-family l2vpn evpn
neighbor 193.204.0.2 activate
advertise-all-vni
exit-address-family
vtep1/etc/frr/bgpd.conf
router bgp 2
neighbor 193.204.0.1 remote-as 1
address-family l2vpn evpn
neighbor 193.204.0.1 activate
advertise-all-vni
exit-address-family
vtep2/etc/frr/bgpd.conf
activate the address-family on the peering with specific neighbor
announce on the peerings all the VNIs configured in the VTEP

## Slide 96: companion bridge
the bridge connected to the VTEP interface
used by the VTEP to perform source address learning of local interfaces
when in combination with EVPN-BGP
  its forwarding table is also populated via updates received from BGP
  the FRR control plane watch to updates of the bridge forwarding table to send updates via BGP

## Slide 97: vtep1 bridge configuration
# Setting up VXLAN interfaces
ip link add vtep100 type vxlan id 100 dev eth1 dstport 4789 local 193.204.0.1 nolearning
ip link set up dev vtep100
# Creating the companion bridge
brctl addbr br100 type bridge
brctl addif br100 vtep100
brctl addif br100 eth0
brctl stp br100 off
ip link set up dev br100
# Enabling FRR
/etc/init.d/frr start
vtep1.startup
create the interface
name of the interface
VNI
VXLAN dst port
VXLAN src IP
enable the VXLAN interface
create the companion bridge and name it
attach the VXLAN interface to the bridge
disable STP protocol
enable the bridge
disable the mcast learning
interface used to send VXLAN packets into the underlay network
attach eth0 (the server s1 collision domain) to the bridge

## Slide 98: vtep2 bridge configuration
# Setting up VXLAN interfaces
ip link add vtep100 type vxlan id 100 dev eth1 dstport 4789 local 193.204.0.2 nolearning
ip link set up dev vtep100
# Creating the companion bridge
brctl addbr br100 type bridge
brctl addif br100 vtep100
brctl addif br100 eth0
brctl stp br100 off
ip link set up dev br100
# Enabling FRR
/etc/init.d/frr start
vtep2.startup

## Slide 99: the EVPN-BGP control-plane
vtep1# show evpn mac vni all
VNI 100 #MACs (local and remote) 2
Flags: N=sync-neighs, I=local-inactive, P=peer-active, X=peer-proxy
MAC Type Flags Intf/Remote ES/VTEP VLAN Seq #'s
a2:6d:75:c7:06:6f remote 193.204.0.2 0/0
c2:93:31:36:31:b6 local eth0 0/0

## Slide 100: a BGP update
AFI/SAFI of l2vpn/EVPN
announcement
from vtep2 to vtep1
MAC address of s1
VNI of s1
VTEP destination

## Slide 101: VXLAN encapsulation
overhead of 50 bytes
random Source Port to fully exploit Multi-Path

## Slide 102: a PING packet encapsulated in VXLAN
IPs of servers
MAC addresses of s1 and s2
MAC addresses of vtep1 and vtep2
Outer Layer 1
Outer UDP Header
VXLAN Header
Original Layer 2
Original Layer 3
Original ICMP Packet
IPs of VTEPs
Outer MAC Header
Outer IP Layer

## Slide 103: putting together
(EVPN-)BGP

## Slide 104: overview
containers or VMs of different tenants
where is the VTEP?
the Leaf-server links
inside the servers
dual attached servers
one week later

## Slide 105: servers in the fabric – recap
Servers
Containers or VMs

## Slide 106: containers or VMs of different tenants
different colours represent different tenants

## Slide 107: EVPN-BGP – where is the VTEP?
containers must be unaware of the tunneling
different choices for the positioning of the VTEP
  in each server
    the server should have a BGP peering for enabling EVPN-BGP
    the server CPU would be used to route packets
  in each Leaf
    the Leaf already has a BGP peering
    the Leaf is a router, so it has dedicated routing hardware
    additional encapsulation is required between Leaves and servers

## Slide 108: inside the Leaves
VLAN is used
mapping between VNIs and VLAN IDs
  tenants are unaware of the mapping
Leaves decapsulate VXLAN packets and encapsulate them into VLAN frames, according to the mapping

## Slide 109: inside the servers
the server uses the VLAN IDs to forward packets to the correct containers/VMs
the server untags the packets so that the containers/VMs are unaware of the VLANs
  containers/VMs of the same tenant shares the same virtual Layer-2 network

## Slide 110: deploying VXLAN
VLAN ID VNI
10 5010
20 5020
… …
VXLAN
VLAN
no encapsulation

## Slide 111: the last problem to overcome
if a Leaf-server link breaks down, the server is severed off the data center
if a Leaf breaks, all the servers connected to that Leaf are severed off the data center
if a maintenance needs to be done on a Leaf, all the servers connected to that Leaf are temporarily severed off the data center

## Slide 112: dual attached servers – bonding
aggregates multiple NICs into a single virtual interface
Layer-2 technology
different policies are possible
  active-backup
  active-active
    round-robin
    broadcase
    balance-xor
    and more…

## Slide 113: one week later
VLAN ID VNI
10 5010
20 5020
… …
VXLAN
VLAN
no encapsulation

## Slide 114: bibliography and further readings
[Dutt ‘18] Dutt, “EVPN in the Data Center”, O’Reilly, 2018
[Bernat ‘17] Bernat, “VXLAN: BGP EVPN with FRR“, https://vincent.bernat.ch/en/blog/2017-vxlan-bgp-evpn
[Bernat ‘17] Bernat, “VXLAN & Linux”, https://vincent.bernat.ch/en/blog/2017-vxlan-linux
[RFC-7432] Sajassi, Aggarwal, Bitar, Isaac, Uttaro, Drake, Henderickx, “BGP MPLS-Based Ethernet VPN ” Internet Engineering Task Force (IETF) Request for Comments: 7432
[RFC-8365] Sajassi, Drake, Bitar, Shekhar, Uttaro, Henderickx, “A Network Virtualization Overlay Solution Using Ethernet VPN (EVPN)” Internet Engineering Task Force (IETF) Request for Comments: 8365