## Slide 1: data centers’ architecture
Version | 3.1
Author(s) | L. Ariemma, G. Di Battista, M. Patrignani, M. Scazzariello, T. Caiazzi
E-mail | contact@kathara.org
Web | http://www.kathara.org/
Description | Data Centers’ Routing: Multipath, Fat-Trees

## Slide 2: copyright notice
all the pages/slides in this presentation, including but not limited to, images, photos, animations, videos, sounds, music, and text (hereby referred to as “material”) are protected by copyright
this material, with the exception of some multimedia elements licensed by other organizations, is property of the authors and/or organizations appearing in the first slide
this material, or its parts, can be reproduced and used for didactical purposes within universities and schools, provided that this happens for non-profit purposes
any other use is prohibited, unless explicitly authorized by the authors on the basis of an explicit agreement
this copyright notice must always be redistributed together with the material, or its portions

## Slide 3: Multi-Path
in a nutshell

## Slide 4: Multi-Path
data center architectures allow to establish several paths between pairs of nodes
Multi-Path routing is used to
  distribute and balance the traffic among different paths
  increase the fault tolerance

## Slide 5: Multi-Path
allows to have more than one next-hop for the same prefix in the FIB (Forwarding Information Base)
needs kernel support
  the main OSes and routers support it
different usage policies can be applied
packets of the same flow should use the same path
  reordering packets is computationally heavy

## Slide 6: Equal-Cost Multi-Path (ECMP)
a specific approach to Multi-Path
exploits paths to the same destination that have the same “cost”
  e.g., same IGP cost, same number of hops
allows to choose among the available paths in a uniform way
often used in Fat-Tree data centers
  we’ll get there in a couple of slides

## Slide 7: how packets are forwarded
for each packet, the kernel decides the FIB entry to be used
different policies are allowed
  hash-based policy
    Layer-3 hash (src IP, dst IP)
    Layer-4 hash (src IP, dst IP, src port, dst port, protocol)
  round-robin

## Slide 8: Hyper-scale Data Centers
main concepts

## Slide 9: a high-level architecture
Internet connections
  multiple redundant high-speed fiber optic links
fabric
  infrastructure designed to transport packets between servers and between servers and Internet
server farm
  host applications and services

## Slide 10: a high-level architecture
server farm
Internet
data center fabric

## Slide 11: fabric architecture
why Fat-Trees?

## Slide 12: overview – fabric architecture
real-life data centers
service model
data center network
  traffic flow directions
  requirements
  components
  topologies

## Slide 13: real data center information – figures
links are fiber optic links
each link in the fabric is at least at 100Gb/s
each switch is at least of 64 ports
about 5,000 switches/routers
about 60,000 servers

## Slide 15: data center failures – yearly report
statistics by Google (2008) in a portion of data center composed of 1,800 servers:
1,000 individual machine (switch/router or server) failures
thousands of hard drive failure
1 power distribution unit failure
  down for 500/1000 machines for 6 hours
1 cluster complete rewire (not simultaneously)

## Slide 16: data center service models
three different service models
  on-premise data centers
    built, owned and operated by a company
    often housed in a building of the organization
  colocation data centers
    built and owned by a company that rents space within the data center to other companies
      the hosting company manages the infrastructure (building, cooling, bandwidth, security etc.)
      the hosted companies provides the components, including servers, storage, and firewalls
  cloud data centers
    applications and data are hosted by a cloud service provider such as Amazon Web Services (AWS), Microsoft Azure, and Google Cloud Platform (GCP)

## Slide 17: traffic flows inside a data center
two types of flows can be identified
  traffic exiting or entering the data center
    also called “north-south traffic”
    data sent/received via Internet
  server-to-server communications
    also called “east-west traffic”: in data center schemata servers are typically drawn side-by-side
    primarily, supports micro-services and distributed architectures

## Slide 18: traffic flows inside a data center
server farm
Internet
data center fabric
north-south traffic
east-west traffic

## Slide 19: data center network requirements
support high-bandwidth server-to-server communication
  applications that rely on cluster computations, such as Hadoop or Spark, can involve hundreds or thousands of servers
  customer’s containers/virtual machines (VMs) are distributed across multiple servers but need to communicate seamlessly
  microservice architectures heavily rely on server-to-server communication
scale
  data centers range from a few hundred to a hundred thousand servers in a single physical location
resilience
  data center applications are designed to work in presence of failures

## Slide 20: data center network components
data center nodes can be connected by using two network component types
  specialized hardware
    proprietary hardware that can scale to clusters of thousands of nodes with high bandwidth
      e.g., Google Jupiter and InfiniBand switches
    expensive option
  commodity switches and routers
    cheap option
    widely adopted, this is the option we consider in the following

## Slide 21: topology requirements
scalability
  it should be possible to expand the data center
  in other words, it must be possible to buy and deploy hardware similar to the one already deployed
bandwidth
  hosts in the fabric should communicate with each other using the full bandwidth of their NICs

## Slide 22: data center network topologies
several topologies have been proposed
  Clos
  Fat-Tree
  VL2
  Jellyfish
  Xpander
  DCell
  ...

## Slide 23: Clos topology
invented by Edson Erwin in 1938 to address scalability issues in telephone networking
  formalized by Charles Clos in 1953
the original problem was allowing N contemporary connections from N input lines to N output lines without using a single crossbar switch

## Slide 24: Fat-Tree topology
Fat-Trees were originally introduced by Charles Leiserson in 1985
the Fat-Tree is a special case of a Clos
typical Fat-Tree architectures today consist of three level of nodes (switches/routers)
high redundancy
constant bisection of the available bandwidth
typically, nodes have the same characteristics
  easier to stock spare equipments

## Slide 25: Fat-Tree parameters
the Fat-Tree is a modular topology
two parameters define a Fat-Tree
  radix of the nodes (even number, denoted by 2K)
    number of available ports
  redundancy factor (denoted by R)
usually, if the radix of a node is 2K it has K connections towards the north and K connections towards the south
  different choices are possible, but not considered here

## Slide 26: Fat-Tree nodes
Leaf
  node connected to the server farm
Spine
  node north of Leaves and south of ToF nodes
Point of Delivery (PoD)
  set of fully interconnected Leaves and Spines
Top of Fabric (ToF)
  set of top nodes that provide inter-PoD communication

## Slide 27: an example of Fat-Tree: FT(K=2,R=2)
ToF (Top of Fabric)
Leaf
Spine
aggregation layer
PoD (Point of Delivery)
Server Farm

## Slide 28: redundancy factor (R)
number of links between a ToF node and a PoD
allow to connect more PoDs reducing the redundancy
Server Farm
R = 2
Server Farm
R = 1

## Slide 29: multi-plane Fat-Tree
when KR the Fat-Tree is called multi-plane
the ToF nodes are partitioned in sets called planes
Server Farm
Plane A
Plane B

## Slide 30: example of a multi-plane Fat-Tree
diagram from the IETF RIFT Draft

## Slide 31: connecting a Fat-Tree to the Internet
two strategies
  usage of a dedicated PoD
  usage of ToFs
Internet
Internet

## Slide 32: bibliography and further readings
[Caiazzi ‘22] Caiazzi, Scazzariello, Alberro, Ariemma, Castro, Grampin, Di Battista, “Sibyl: a Framework for Evaluating the Implementation of Routing Protocols in Fat-Trees“, NOMS 2022
[Caiazzi ‘21] Caiazzi, Scazzariello, Ariemma, “VFTGen: a Tool to Perform Experiments in Virtual Fat Tree Topologies“, IM 2021
[Caiazzi ‘19] Caiazzi, “Software Defined Data Centers: methods and tools for routing protocol verification and comparison”, Ms. Thesis, Roma Tre University, 2019
[Dutt ‘17] Dutt, “BGP in the Data Center”, O’Reilly, 2017
[RFC-7938] Lapukhov, Premji, “Use of BGP for Routing in Large-Scale Data Centers” Internet Engineering Task Force (IETF) Request for Comments: 7938