## Slide 1: kathara lab
DNS
Version | 2.0
Author(s) | L. Ariemma, T. Caiazzi, G. Di Battista, M. Patrignani, M. Pizzonia, F. Ricci, M. Rimondini
E-mail | contact@kathara.org
Web | http://www.kathara.org/
Description | using the domain name system – kathara version of an existing netkit lab

## Slide 2: copyright notice
All the pages/slides in this presentation, including but not limited to, images, photos, animations, videos, sounds, music, and text (hereby referred to as “material”) are protected by copyright.
This material, with the exception of some multimedia elements licensed by other organizations, is property of the authors and/or organizations appearing in the first slide.
This material, or its parts, can be reproduced and used for didactical purposes within universities and schools, provided that this happens for non-profit purposes.
Information contained in this material cannot be used within network design projects or other products of any kind.
Any other use is prohibited, unless explicitly authorized by the authors on the basis of an explicit agreement.
The authors assume no responsibility about this material and provide this material “as is”, with no implicit or explicit warranty about the correctness and completeness of its contents, which may be subject to changes.
This copyright notice must always be redistributed together with the material, or its portions.

## Slide 3: purpose of this lab
get familiar with DNS
observe the behavior of name servers and their interactions
learn simple DNS configurations

## Slide 4: lab limitations
DNS security issues and protocols are not covered
  we use a version of Bind, which currently is the most widely used domain name server software, that allows ignoring security aspects
all IP addresses are IPv4

## Slide 5: about the DNS
takes care of associating names with IP addresses
the name system is distributed over several nodes (hosts) that are hierarchically organized to form a tree
each node in the hierarchy corresponds to a name
a domain in the name system is a subtree
a node in the hierarchy may be delegated to handle names for a particular zone
  such a node is an authoritative server for that zone
a zone is a domain which is devoid of those nodes having a different authoritative server (i.e., a tree without subtrees)

## Slide 6: the DNS name hierarchy
each node corresponds
to a name
pc1
uniroma3
startup
it
net
“”
dnsroot
dnsit
dnsuni
dnsnet
this node is startup.net
this node is pc1.uniroma3.it
localuni
pc2
dnsstart
localstart

## Slide 7: the DNS name hierarchy
dnsuni
uniroma3
startup
org
net
“”
pc1
pc2
dnsit
dnsroot
dnsnet
dnsstart
localuni
localstart
net domain
startup.net domain
domains are subtrees
  their name is the name of the root node
  every node (including leaves) defines a domain
  domains do overlap

## Slide 8: the DNS name hierarchy
leaves always correspond to real hosts
dnsuni
uniroma3
startup
it
net
“”
pc1
pc2
intermediate nodes may correspond to real hosts (in this example they do not)
dnsit
dnsroot
dnsnet
dnsstart
localuni
localstart

## Slide 9: zones
a zone is a domain without the delegated subdomains
dnsuni
uniroma3
startup
it
net
“”
pc1
pc2
zones cannot overlap
  each node falls into a single zone
dnsit
dnsroot
dnsnet
dnsstart
localuni
localstart

## Slide 10: zones
zones have name servers
  they are not constrained to be inside the zone they serve
dnsuni
uniroma3
startup
net
“”
pc1
pc2
dnsit
dnsroot
dnsnet
dnsstart
localuni
localstart
served by dnsroot
served by
dnsit.it
served by
dnsnet.net
served by dnsuni.uniroma3.it
served by dnsstart.startup.net
it

## Slide 11: more about the DNS
the dns hierarchy is largely orthogonal with respect to the actual network topology
in order to focus on the behavior of the dns we choose a flat topology, consisting of a single collision domain

## Slide 12: step 1 – network topology
192.168.0.0/24
pc1
pc2
.2
dnsuni
startup
dnsit
dnsnet
dnsroot
.5
.22
.222
.1
.11
.111
abc
machine name
localstart
.220
localuni
.110

## Slide 13: step 1 – DNS (zone) hierarchy
pc1
pc2
uniroma3
it
net
“”
served by
dnsroot
served by
dnsit.it
served by
dnsnet.net
served by
dnsuni.uniroma3.it
served by
dnsstart.startup.net
domain name
abc
startup

## Slide 14: step 2 – starting the lab
the lab is configured to
  start all the 9 devices
  automatically configure network interfaces (IPv4 only)
  automatically configure the authoritative name servers
  automatically configure name servers offering a recursive resolution service
  automatically start the name server software (bind) on each name server
    the daemon corresponding to bind is called named

## Slide 15: step 2 – exploring the configuration
root@pc1:~$ cat /etc/resolv.conf
nameserver 192.168.0.110
search uniroma3.it
options single-request
root@pc2:~$ cat /etc/resolv.conf
nameserver 192.168.0.220
search startup.net
options single-request
configuration on the PCs consists of the specification of the default name server
localuni.uniroma3.it
suffix to append to unqualified names (e.g., asking to resolve dummy results in querying for dummy.uniroma3.it)
localstart.startup.net
perform first IPv4 and then IPv6 queries

## Slide 16: step 2 – exploring the configuration
configuration on the name servers specifies
  associations between zones and name servers
  information about the root name servers
  authoritative information
    associations between names and IP addresses
  authorization to resolve recursive queries

## Slide 17: step 2 – exploring the configuration
root@dnsuni:~$ cat /etc/bind/named.conf
include "/etc/bind/named.conf.options";
zone "." {
type hint;
file "/etc/bind/db.root";
};
zone "uniroma3.it" {
type master;
file "/etc/bind/db.it.uniroma3";
};
configuration on the name servers specifies
  associations between zones and name servers
kathara – [ lab: dns ]
where to find information about the root name server
we are the primary master for zone uniroma3.it
where to find data about the names in this zone
include some additional configuration

## Slide 18: step 2 – exploring the configuration
configuration on the name servers specifies
  additional configuration
root@dnsuni:~$ cat /etc/bind/named.conf.options
options {
directory "/var/cache/bind";
};
use this folder to store the cache.
COMPULSORY, otherwise, named wont ‘t start

## Slide 19: format of a resource record
<domain> <class> <type> <rdata>
domain: the record owner (=domain to which the record refers)
class: usually IN (=Internet system); may be HS (=hesiod) or CH (=chaos)
type: see next slide...
rdata: record data (depends on the record type)

## Slide 20: step 2 – exploring the configuration
last update: Nov 2018
kathara – [ lab: dns ]
available record types
A a host address.
A6 Obsolete format of IPv6 address.
AAAA an IPv6 address.
AFSDB (x) location of AFS database servers. Experimental.
CERT holds a digital certificate.
CNAME identifies the canonical name of an alias.
DNAME for delegation of reverse addresses. Replaces the domain name specified with
another name to be looked up. Described in RFC 2672.
GPOS Specifies the global position. Superseded by LOC.
HINFO identifies the CPU and OS used by a host.
ISDN (x) representation of ISDN addresses. Experimental.
KEY stores a public key associated with a DNS name.
KX identifies a key exchanger for this DNS name.
LOC (x) for storing GPS info. See RFC 1876. Experimental.
MX identifies a mail exchange for the domain. See RFC 974 for details.
NAPTR name authority pointer.
NSAP a network service access point.
NS the authoritative nameserver for the domain.
NXT used in DNSSEC to securely indicate that RRs with an owner name in a certain
name interval do not exist in a zone and indicate what R
PTR a pointer to another part of the domain name space.
PX provides mappings between RFC 822 and X.400 addresses.
RP (x) information on persons responsible for the domain. Experimental.
RT (x) route-through binding for hosts that do not have their own direct wide area
network addresses. Experimental.
SIG ("signature") contains data authenticated in the secure DNS. See RFC 2535 for
details.
SOA identifies the start of a zone of authority.
SRV information about well known network services (replaces WKS).
TXT text records.
WKS (h) information about which well known network services, such as SMTP, that a
domain supports. Historical, replaced by newer RR SRV.
X25 (x) representation of X.25 network addresses. Experimental

## Slide 21: step 2 – exploring the configuration
configuration on the name servers specifies
  information about the root name servers
kathara – [ lab: dns ]
root@dnsuni:~$ cat /etc/bind/db.root
. IN NS ROOT-SERVER.
ROOT-SERVER. IN A 192.168.0.5
a resource record

## Slide 22: step 2 – exploring the configuration
configuration on the name servers specifies
  authoritative information
root@dnsuni:~$ cat /etc/bind/db.it.uniroma3
$TTL 60000
time to live, in seconds (determines how long a resource record should be cached)

## Slide 23: step 2 – exploring the configuration
configuration on the name servers specifies
  authoritative information
root@dnsuni:~$ cat /etc/bind/db.it.uniroma3
$TTL 60000
@ IN SOA dnsuni.uniroma3.it. root.dnsuni.uniroma3.it. (
2006031201 ; serial
28 ; refresh
14 ; retry
3600000 ; expire
0 ; negative cache ttl
)
Start of Authority record
must be all on a single line; line breaks can only be introduced when using parentheses
a zone data file can contain only one SOA record

## Slide 24: step 2 – exploring the configuration
configuration on the name servers specifies
  authoritative information
root@dnsuni:~$ cat /etc/bind/db.it.uniroma3
$TTL 60000
@ IN SOA dnsuni.uniroma3.it. root.dnsuni.uniroma3.it. (
2006031201 ; serial
28 ; refresh
14 ; retry
3600000 ; expire
0 ; negative cache ttl
)
this record is referred to the current origin (uniroma3.it)
all domain names in this data file that are not fully qualified (do not end with a ‘.’) are relative to the origin
the origin is the domain name in the zone statement of the server configuration file:
  zone "uniroma3.it" {
  type master;
  file "/etc/bind/db.it.uniroma3";
  };

## Slide 25: step 2 – exploring the configuration
configuration on the name servers specifies
  authoritative information
root@dnsuni:~$ cat /etc/bind/db.it.uniroma3
$TTL 60000
@ IN SOA dnsuni.uniroma3.it. root.dnsuni.uniroma3.it. (
2006031201 ; serial
28 ; refresh
14 ; retry
3600000 ; expire
0 ; negative cache ttl
)
primary master (=authority) server for this zone (dnsuni.uniroma3.it);
don’t forget the trailing dot, or the origin name (uniroma3.it) would be appended!

## Slide 26: step 2 – exploring the configuration
configuration on the name servers specifies
  authoritative information
root@dnsuni:~$ cat /etc/bind/db.it.uniroma3
$TTL 60000
@ IN SOA dnsuni.uniroma3.it. root.dnsuni.uniroma3.it. (
2006031201 ; serial
28 ; refresh
14 ; retry
3600000 ; expire
0 ; negative cache ttl
)
mail address of the person that is responsible for the zone
(root@dnsuni.uniroma3.it)
the first ‘.’ must be replaced by a ‘@’
only meant to be used by humans; has no use within the dns service

## Slide 27: step 2 – exploring the configuration
configuration on the name servers specifies
  authoritative information
root@dnsuni:~$ cat /etc/bind/db.it.uniroma3
$TTL 60000
@ IN SOA dnsuni.uniroma3.it. root.dnsuni.uniroma3.it. (
2006031201 ; serial
28 ; refresh
14 ; retry
3600000 ; expire
0 ; negative cache ttl
)
makes sense for master/slave server configurations

## Slide 28: step 2 – exploring the configuration
configuration on the name servers specifies
  authoritative information
root@dnsuni:~$ cat /etc/bind/db.it.uniroma3
$TTL 60000
@ IN SOA dnsuni.uniroma3.it. root.dnsuni.uniroma3.it. (
2006031201 ; serial
28 ; refresh
14 ; retry
3600000 ; expire
0 ; negative cache ttl
)
serial number
determines how recent the information is
influences all data within the zone
conventional format: YYYYMMDDNN (year, month, day, # of changes within that day)

## Slide 29: step 2 – exploring the configuration
configuration on the name servers specifies
  authoritative information
root@dnsuni:~$ cat /etc/bind/db.it.uniroma3
$TTL 60000
@ IN SOA dnsuni.uniroma3.it. root.dnsuni.uniroma3.it. (
2006031201 ; serial
28 ; refresh
14 ; retry
3600000 ; expire
0 ; negative cache ttl
)
refresh interval
(seconds)
tells a slave how often to check that the data for this zone is up to date

## Slide 30: step 2 – exploring the configuration
configuration on the name servers specifies
  authoritative information
root@dnsuni:~$ cat /etc/bind/db.it.uniroma3
$TTL 60000
@ IN SOA dnsuni.uniroma3.it. root.dnsuni.uniroma3.it. (
2006031201 ; serial
28 ; refresh
14 ; retry
3600000 ; expire
0 ; negative cache ttl
)
interval (seconds) between subsequent attempts to contact the master

## Slide 31: step 2 – exploring the configuration
configuration on the name servers specifies
  authoritative information
root@dnsuni:~$ cat /etc/bind/db.it.uniroma3
$TTL 60000
@ IN SOA dnsuni.uniroma3.it. root.dnsuni.uniroma3.it. (
2006031201 ; serial
28 ; refresh
14 ; retry
3600000 ; expire
0 ; negative cache ttl
)
slave expire time
(seconds)
if the slave fails to contact the master for this amount of time, it considers the zone data too old and stops giving answers about it

## Slide 32: step 2 – exploring the configuration
configuration on the name servers specifies
  authoritative information
root@dnsuni:~$ cat /etc/bind/db.it.uniroma3
$TTL 60000
@ IN SOA dnsuni.uniroma3.it. root.dnsuni.uniroma3.it. (
2006031201 ; serial
28 ; refresh
14 ; retry
3600000 ; expire
0 ; negative cache ttl
)
ttl for negative responses from authoritative name servers

## Slide 33: step 2 – exploring the configuration
configuration on the name servers specifies
  associations between names and ip addresses
root@dnsuni:~$ cat /etc/bind/db.it.uniroma3
$TTL 60000
@ IN SOA dnsuni.uniroma3.it. root.dnsuni.uniroma3.it. (
2006031201 ; serial
28 ; refresh
14 ; retry
3600000 ; expire
0 ; negative cache ttl
)
@ IN NS dnsuni.uniroma3.it.
dnsuni.uniroma3.it. IN A 192.168.0.11
pc1.uniroma3.it. IN A 192.168.0.111
record type NS
(name server)
the authoritative name server for this zone (uniroma3.it) is dnsuni.uniroma3.it

## Slide 34: step 2 – exploring the configuration
configuration on the name servers specifies
  associations between names and ip addresses
root@dnsuni:~$ cat /etc/bind/db.it.uniroma3
$TTL 60000
@ IN SOA dnsuni.uniroma3.it. root.dnsuni.uniroma3.it. (
2006031201 ; serial
28 ; refresh
14 ; retry
3600000 ; expire
0 ; negative cache ttl
)
@ IN NS dnsuni.uniroma3.it.
dnsuni.uniroma3.it. IN A 192.168.0.11
pc1.uniroma3.it. IN A 192.168.0.111
two machines in this zone:
dnsuni.uniroma3.it
pc1.uniroma3.it
record type A
(address)

## Slide 35: step 2 – exploring the configuration
configuration on the name servers specifies
  associations between names and ip addresses
root@dnsit:~$ tail –n 5 /etc/bind/db.it
@ IN NS dnsit.it.
dnsit.it. IN A 192.168.0.1
uniroma3.it. IN NS dnsuni.uniroma3.it.
dnsuni.uniroma3.it. IN A 192.168.0.11
dnsit.it is the authority for this zone (it)
dnsuni.uniroma3.it is the authority for zone uniroma3(.it)

## Slide 36: step 2 – exploring the configuration
configuration on the name servers specifies
  allowing recursive queries and disabling dnssec
root@localuni:~$ cat /etc/bind/named.conf.options
options {
directory "/var/cache/bind";
allow-recursion { 192.168.0.0/24; };
auto-dnssec off;
dnssec-validation no;
dnssec-enable no;
dnssec-lookaside no;
filter-aaaa-on-v4 yes;
send-cookie no;
};
allow recursive queries from 192.168.0.0/24
disable dnssec
filter AAAA addresses on IPv4 only
Do not send DNS cookies

## Slide 37: let’s start the lab

## Slide 38: step 3 – experiment setting
192.168.0.0/24
pc1
pc2
.2
dnsuni
startup
dnsit
dnsnet
dnsroot
.5
.22
.222
.1
.11
.111
localstart
.220
localuni
.110

## Slide 39: sniff the traffic
connect the wireshark device to collision domain A
open any browser on the host machine
  on localhost:3000
  sniff eth1
user@localhost:~/kathara-lab_dns$ kathara lconfig -n wireshark --add A

## Slide 40: step 3 – ping from pc1
execute a ping command towards pc2
root@pc1:/# ping -n pc2.startup.net
PING pc2.startup.net (192.168.0.222) 56(84) bytes of data.
64 bytes from 192.168.0.222: icmp_seq=1 ttl=64 time=1.50 ms
64 bytes from 192.168.0.222: icmp_seq=2 ttl=64 time=0.580 ms
64 bytes from 192.168.0.222: icmp_seq=3 ttl=64 time=0.525 ms
--- pc2.startup.net ping statistics ---
3 packets transmitted, 3 received, 0% packet loss, time 2010ms
rtt min/avg/max/mdev = 0.525/0.867/1.496/0.445 ms
pc1
Numeric output only. No attempt will be made to lookup symbolic names for host addresses.

## Slide 41: step 3 – the sniffer output

## Slide 42: step 3 – the sniffer output
filter to only show DNS packets

## Slide 43: step 3 – the sniffer output
query id
query type
(address)
query value
pc1 asks to localuni
the address of pc2

## Slide 44: step 3 – the sniffer output
request root name servers
answer with all the authoritative root name servers

## Slide 45: step 3 – the sniffer output
localuni asks dnsroot who is the name server for the net domain
dnsnet.net address is 192.168.0.2

## Slide 46: step 3 – the sniffer output
localuni asks dnsnet who is the name server for the startup.net domain
dnsstart.startup.net address is 192.168.0.22

## Slide 47: step 3 – the sniffer output
localuni asks dnsstart what is the address of pc2.startup.net
pc2.startup.net address is 192.168.0.222

## Slide 48: step 3 – the sniffer output
localuni reports to pc1 the addres of pc2.startup.net

## Slide 49: step 3 – the sniffer output
pc1 asks localuni for AAAA records of pc2.startup.net
localuni directly asks dnsstart (it already knows it) for AAAA records of pc2.startup.net
dnsstart returns a SOA record, indicating that it does not have any AAAA record for pc2.startup.net
localuni reports dnsstart answer to pc1

## Slide 50: step 3 – exchanged messages
192.168.0.0/24
pc1
pc2
.2
dnsuni
dnsstart
dnsit
dnsnet
dnsroot
.5
.22
.222
.1
.11
.111
abc
machine name

## Slide 51: step 3 – exchanged messages
192.168.0.0/24
pc1
pc2
.2
dnsuni
dnsstart
dnsit
dnsnet
dnsroot
.5
.22
.222
.1
.11
.111
abc
machine name

## Slide 52: step 3 – exchanged messages
192.168.0.0/24
pc1
pc2
.2
dnsuni
dnsstart
dnsit
dnsnet
dnsroot
.5
.22
.222
.1
.11
.111
abc
machine name

## Slide 53: step 3 – exchanged messages
192.168.0.0/24
pc1
pc2
.2
dnsuni
dnsstart
dnsit
dnsnet
dnsroot
.5
.22
.222
.1
.11
.111
abc
machine name

## Slide 54: step 3 – exchanged messages
192.168.0.0/24
pc1
pc2
.2
dnsuni
dnsstart
dnsit
dnsnet
dnsroot
.5
.22
.222
.1
.11
.111
abc
machine name

## Slide 55: step 3 – exchanged messages
192.168.0.0/24
pc1
pc2
.2
dnsuni
dnsstart
dnsit
dnsnet
dnsroot
.5
.22
.222
.1
.11
.111
abc
machine name

## Slide 56: step 3 – exchanged messages
192.168.0.0/24
pc1
pc2
.2
dnsuni
dnsstart
dnsit
dnsnet
dnsroot
.5
.22
.222
.1
.11
.111
abc
machine name

## Slide 57: step 3 – exchanged messages
192.168.0.0/24
pc1
pc2
.2
dnsuni
dnsstart
dnsit
dnsnet
dnsroot
.5
.22
.222
.1
.11
.111
abc
machine name
recursive behavior

## Slide 58: step 4 – repeating the experiment
execute a ping command towards pc2
root@pc1:/# ping -n pc2.startup.net
PING pc2.startup.net (192.168.0.222) 56(84) bytes of data.
64 bytes from 192.168.0.222: icmp_seq=1 ttl=64 time=1.50 ms
64 bytes from 192.168.0.222: icmp_seq=2 ttl=64 time=0.580 ms
64 bytes from 192.168.0.222: icmp_seq=3 ttl=64 time=0.525 ms
--- pc2.startup.net ping statistics ---
3 packets transmitted, 3 received, 0% packet loss, time 2010ms
rtt min/avg/max/mdev = 0.525/0.867/1.496/0.445 ms
pc1

## Slide 59: step 4 – repeating the experiment
the name server cache helps reducing traffic

## Slide 60: step 4 – repeating the experiment
192.168.0.0/24
pc1
pc2
.2
dnsuni
dnsstart
dnsit
dnsnet
dnsroot
.5
.22
.222
.1
.11
.111
abc
machine name

## Slide 61: step 5 – cleaning the cache
rndc controls the operation of a name server
the flush command cleans up caches
  a new client query triggers the complete sequence of iterative queries
root@localuni:/# rndc flush
localuni

## Slide 62: step 6 – ping non-existent target
execute a ping command towards a non-existent target
root@pc1:/# ping pluto.startup.net
ping: pluto.startup.net: Name or service not known
pc1

## Slide 63: step 6 – non-existent target
kathara – [ lab: dns ]
all the iterative queries are performed again because of the cache flush

## Slide 64: step 6 – non-existent target
kathara – [ lab: dns ]
the requested domain (pluto.startup.net) does not exist

## Slide 65: step 6 – non-existent target
kathara – [ lab: dns ]
since the query has failed, pc1 tries once more with the domain search path configured inside its /etc/resolv.conf:
nameserver 192.168.0.11
search uniroma3.it

## Slide 66: step 6 – ping non-existent target
repeat the ping command towards the non-existent target
root@pc1:/# ping pluto.startup.net
ping: pluto.startup.net: Name or service not known
pc1

## Slide 67: step 6 – ping non-existent target
kathara – [ lab: dns ]
the name server negative cache has stored the negative answer
as before, pc1 tries once more with the domain search path configured inside its /etc/resolv.conf

## Slide 68: step 7 – advanced queries
resource records can be searched by using dig
  highly customizable queries
  detailed responses
root@pc1:/# dig pc2.startup.net
pc1

## Slide 69: step 7 – advanced queries
root@pc1:/# dig pc2.startup.net
; <<>> DiG 9.18.19-1~deb12u1-Debian <<>> pc2.startup.net
;; global options: +cmd
;; Got answer:
;; ->>HEADER<<- opcode: QUERY, status: NOERROR, id: 22137
;; flags: qr rd ra; QUERY: 1, ANSWER: 1, AUTHORITY: 1, ADDITIONAL: 2
;; OPT PSEUDOSECTION:
; EDNS: version: 0, flags:; udp: 4096
; COOKIE: b4c95f2012cf8905d705a97c657b10f314be1a5abe3ec74d (good)
;; QUESTION SECTION:
;pc2.startup.net. IN A
;; ANSWER SECTION:
pc2.startup.net. 60000 IN A 192.168.0.222
;; AUTHORITY SECTION:
startup.net. 59173 IN NS dnsstart.startup.net.
;; ADDITIONAL SECTION:
dnsstart.startup.net. 59173 IN A 192.168.0.22
;; Query time: 0 msec
;; SERVER: 192.168.0.110#53(192.168.0.110) (UDP)
;; WHEN: Thu Dec 14 14:28:03 UTC 2023
;; MSG SIZE rcvd: 127
pc1
answer flags:
qr: query response
rd: recursion desired (the user asked for a recursive lookup)
ra: recursion available (the server allows recursive lookups)

## Slide 70: step 7 – advanced queries
root@pc1:/# dig pc2.startup.net
; <<>> DiG 9.18.19-1~deb12u1-Debian <<>> pc2.startup.net
;; global options: +cmd
;; Got answer:
;; ->>HEADER<<- opcode: QUERY, status: NOERROR, id: 22137
;; flags: qr rd ra; QUERY: 1, ANSWER: 1, AUTHORITY: 1, ADDITIONAL: 2
;; OPT PSEUDOSECTION:
; EDNS: version: 0, flags:; udp: 4096
; COOKIE: b4c95f2012cf8905d705a97c657b10f314be1a5abe3ec74d (good)
;; QUESTION SECTION:
;pc2.startup.net. IN A
;; ANSWER SECTION:
pc2.startup.net. 60000 IN A 192.168.0.222
;; AUTHORITY SECTION:
startup.net. 59173 IN NS dnsstart.startup.net.
;; ADDITIONAL SECTION:
dnsstart.startup.net. 59173 IN A 192.168.0.22
;; Query time: 0 msec
;; SERVER: 192.168.0.110#53(192.168.0.110) (UDP)
;; WHEN: Thu Dec 14 14:28:03 UTC 2023
;; MSG SIZE rcvd: 127
pc1
these sections correspond to those contained in DNS packets

## Slide 71: step 7 – advanced queries
root@pc1:/# dig pc2.startup.net
; <<>> DiG 9.18.19-1~deb12u1-Debian <<>> pc2.startup.net
;; global options: +cmd
;; Got answer:
;; ->>HEADER<<- opcode: QUERY, status: NOERROR, id: 22137
;; flags: qr rd ra; QUERY: 1, ANSWER: 1, AUTHORITY: 1, ADDITIONAL: 2
;; OPT PSEUDOSECTION:
; EDNS: version: 0, flags:; udp: 4096
; COOKIE: b4c95f2012cf8905d705a97c657b10f314be1a5abe3ec74d (good)
;; QUESTION SECTION:
;pc2.startup.net. IN A
;; ANSWER SECTION:
pc2.startup.net. 60000 IN A 192.168.0.222
;; AUTHORITY SECTION:
startup.net. 59173 IN NS dnsstart.startup.net.
;; ADDITIONAL SECTION:
dnsstart.startup.net. 59173 IN A 192.168.0.22
;; Query time: 0 msec
;; SERVER: 192.168.0.110#53(192.168.0.110) (UDP)
;; WHEN: Thu Dec 14 14:28:03 UTC 2023
;; MSG SIZE rcvd: 127
pc1
records being searched
(class: IN, type: A  address records)
a dns message never contains more than one question section

## Slide 72: step 7 – advanced queries
root@pc1:/# dig pc2.startup.net
; <<>> DiG 9.18.19-1~deb12u1-Debian <<>> pc2.startup.net
;; global options: +cmd
;; Got answer:
;; ->>HEADER<<- opcode: QUERY, status: NOERROR, id: 22137
;; flags: qr rd ra; QUERY: 1, ANSWER: 1, AUTHORITY: 1, ADDITIONAL: 2
;; OPT PSEUDOSECTION:
; EDNS: version: 0, flags:; udp: 4096
; COOKIE: b4c95f2012cf8905d705a97c657b10f314be1a5abe3ec74d (good)
;; QUESTION SECTION:
;pc2.startup.net. IN A
;; ANSWER SECTION:
pc2.startup.net. 60000 IN A 192.168.0.222
;; AUTHORITY SECTION:
startup.net. 59173 IN NS dnsstart.startup.net.
;; ADDITIONAL SECTION:
dnsstart.startup.net. 59173 IN A 192.168.0.22
;; Query time: 0 msec
;; SERVER: 192.168.0.110#53(192.168.0.110) (UDP)
;; WHEN: Thu Dec 14 14:28:03 UTC 2023
;; MSG SIZE rcvd: 127
pc1
records that form the answer to the question
may be more than one
time to live of a resource record that is cached on the server
try invoking dig once more to see it decreasing
constant if the record is not cached (i.e., it is stored on the name server being queried – by default the one configured in /etc/resolv.conf)

## Slide 73: step 7 – advanced queries
root@pc1:/# dig pc2.startup.net
; <<>> DiG 9.18.19-1~deb12u1-Debian <<>> pc2.startup.net
;; global options: +cmd
;; Got answer:
;; ->>HEADER<<- opcode: QUERY, status: NOERROR, id: 22137
;; flags: qr rd ra; QUERY: 1, ANSWER: 1, AUTHORITY: 1, ADDITIONAL: 2
;; OPT PSEUDOSECTION:
; EDNS: version: 0, flags:; udp: 4096
; COOKIE: b4c95f2012cf8905d705a97c657b10f314be1a5abe3ec74d (good)
;; QUESTION SECTION:
;pc2.startup.net. IN A
;; ANSWER SECTION:
pc2.startup.net. 60000 IN A 192.168.0.222
;; AUTHORITY SECTION:
startup.net. 59173 IN NS dnsstart.startup.net.
;; ADDITIONAL SECTION:
dnsstart.startup.net. 59173 IN A 192.168.0.22
;; Query time: 0 msec
;; SERVER: 192.168.0.110#53(192.168.0.110) (UDP)
;; WHEN: Thu Dec 14 14:28:03 UTC 2023
;; MSG SIZE rcvd: 127
pc1
records describing authoritative name servers are returned here
additional records are returned here

## Slide 74: step 8 – an iterative query
root@pc1:/# dig +noquestion +noadditional +norecurse pc2.startup.net
pc1
disable recursion
avoid displaying question and additional sections
restart bind on the name server
perform an iterative query using dig
root@localuni:/# systemctl restart bind9
localuni

## Slide 75: step 8 – an iterative query
root@pc1:/# dig +noquestion +noadditional +norecurse pc2.startup.net
; <<>> DiG 9.18.19-1~deb12u1-Debian <<>> +noquestion +noadditional +norecurse pc2.startup.net
;; global options: +cmd
;; Got answer:
;; ->>HEADER<<- opcode: QUERY, status: NOERROR, id: 15543
;; flags: qr ra; QUERY: 1, ANSWER: 0, AUTHORITY: 1, ADDITIONAL: 1
;; OPT PSEUDOSECTION:
; EDNS: version: 0, flags:; udp: 4096
; COOKIE: 5ea4ced6cdaf30599571a9e0657b15c2381005312bcc21e9 (good)
;; AUTHORITY SECTION:
. 0 IN NS ROOT-SERVER.
;; Query time: 0 msec
;; SERVER: 192.168.0.110#53(192.168.0.110) (UDP)
;; WHEN: Thu Dec 14 14:48:34 UTC 2023
;; MSG SIZE rcvd: 96
pc1
the server answers by specifying the authoritative name server to be contacted to get the desired information

## Slide 76: step 8 – an iterative query
root@pc1:/# dig +noquestion +noadditional +norecurse @192.168.0.5 pc2.startup.net
; <<>> DiG 9.18.19-1~deb12u1-Debian <<>> +noquestion +noadditional +norecurse @192.168.0.5 pc2.startup.net
; (1 server found)
;; global options: +cmd
;; Got answer:
;; ->>HEADER<<- opcode: QUERY, status: NOERROR, id: 24163
;; flags: qr ra; QUERY: 1, ANSWER: 0, AUTHORITY: 1, ADDITIONAL: 2
;; OPT PSEUDOSECTION:
; EDNS: version: 0, flags:; udp: 4096
; COOKIE: 301c8e7f8267ad01ed2cc63e657b1736676e072f5ecd90bf (good)
;; AUTHORITY SECTION:
net. 60000 IN NS dnsnet.net.
;; Query time: 0 msec
;; SERVER: 192.168.0.5#53(192.168.0.5) (UDP)
;; WHEN: Thu Dec 14 14:54:46 UTC 2023
;; MSG SIZE rcvd: 109
pc1
dnsnet.net is the authoritative name server for zone net
query a specific name server (dnsroot)

## Slide 77: step 8 – an iterative query
root@pc1:/# dig +noquestion +noadditional +norecurse @192.168.0.2 pc2.startup.net
; <<>> DiG 9.18.19-1~deb12u1-Debian <<>> +noquestion +noadditional +norecurse @192.168.0.2 pc2.startup.net
; (1 server found)
;; global options: +cmd
;; Got answer:
;; ->>HEADER<<- opcode: QUERY, status: NOERROR, id: 42339
;; flags: qr ra; QUERY: 1, ANSWER: 0, AUTHORITY: 1, ADDITIONAL: 2
;; OPT PSEUDOSECTION:
; EDNS: version: 0, flags:; udp: 4096
; COOKIE: d96ea5b92e6860aeed2cc63e657b1878e06d204302aa8149 (good)
;; AUTHORITY SECTION:
startup.net. 60000 IN NS dnsstart.startup.net.
;; Query time: 9 msec
;; SERVER: 192.168.0.2#53(192.168.0.2) (UDP)
;; WHEN: Thu Dec 14 15:00:08 UTC 2023
;; MSG SIZE rcvd: 111
pc1
dnsstart.startup.net is the authoritative name server for zone startup.net
query a specific name server (dnsnet.net)

## Slide 78: step 8 – an iterative query
root@pc1:/# dig +noquestion +noadditional +norecurse @192.168.0.22 pc2.startup.net
; <<>> DiG 9.18.19-1~deb12u1-Debian <<>> +noquestion +noadditional +norecurse @192.168.0.22 pc2.startup.net
; (1 server found)
;; global options: +cmd
;; Got answer:
;; ->>HEADER<<- opcode: QUERY, status: NOERROR, id: 49113
;; flags: qr aa ra; QUERY: 1, ANSWER: 1, AUTHORITY: 1, ADDITIONAL: 2
;; OPT PSEUDOSECTION:
; EDNS: version: 0, flags:; udp: 4096
; COOKIE: b119e8f8b644792eb3bafbd6657b17989cd95e340adb2072 (good)
;; ANSWER SECTION:
pc2.startup.net. 60000 IN A 192.168.0.222
;; AUTHORITY SECTION:
startup.net. 60000 IN NS dnsstart.startup.net.
;; Query time: 0 msec
;; SERVER: 192.168.0.22#53(192.168.0.22) (UDP)
;; WHEN: Thu Dec 14 14:56:24 UTC 2023
;; MSG SIZE rcvd: 127
pc1
the address of pc2.startup.net
query a specific name server (dnsstart.startup.net )