## Slide 1: kathara lab(s)
ospf with FRRouting
Version | 1.0
Author(s) | Giuseppe Di Battista, Massimo Rimondini, Maurizio Patrignani
E-mail | contact@kathara.org
Web | http://www.kathara.org/
Description | A set of labs showing the operation of the ospf routing protocol in different scenarios – kathara version of an existing netkit lab

## Slide 2: copyright notice
All the pages/slides in this presentation, including but not limited to, images, photos, animations, videos, sounds, music, and text (hereby referred to as “material”) are protected by copyright.
This material, with the exception of some multimedia elements licensed by other organizations, is property of the authors and/or organizations appearing in the first slide.
This material, or its parts, can be reproduced and used for didactical purposes within universities and schools, provided that this happens for non-profit purposes.
Information contained in this material cannot be used within network design projects or other products of any kind.
Any other use is prohibited, unless explicitly authorized by the authors on the basis of an explicit agreement.
The authors assume no responsibility about this material and provide this material “as is”, with no implicit or explicit warranty about the correctness and completeness of its contents, which may be subject to changes.
This copyright notice must always be redistributed together with the material, or its portions.

## Slide 3: about ospf
open shortest path first
an interior gateway protocol
 | specification | authentication confidentiality
version 2 | rfc 2328 | rfc 5709
version 3 (with ipv6 support) | rfc 5340 | rfc 4552

## Slide 4: ospf: overview
each router floods its local state (usable interfaces, reachable neighbors) through the network, using link state advertisements (lsa)
based on this information, each router builds and maintains a link state database (lsdb) describing the whole network topology
  identical for (almost) all routers
  each entry is a router’s local state
each router uses the lsdb to compute a shortest path tree rooted at itself
  interfaces may be assigned costs
note: designed to operate on broadcast networks, but has modes to operate on non-broadcast ones

## Slide 5: a simple ospf lab
single-area

## Slide 6: lab topology
Area ID
10.0.3.0/24
10.0.1.0/24
10.0.2.0/24
bb0
eth0
3
eth1
3
D
B
C
0.0.0.0
10.0.0.0/24
A
bb1
eth0
1
eth1
1
45
10
eth0
2
eth1
1
bb2
10
10
eth1
2
eth0
2
bb3
7
10
bb4
eth1
2
eth0
1
10
10
36
21
ospf cost for exiting the interface

## Slide 7: lab description
single (backbone) area (0.0.0.0)
each interface is assigned an ospf cost
  default: 10
  we have tweaked the costs to force paths taken by traffic
to set interface costs:
  interface eth1 ospf cost 45

## Slide 8: (some) shortest paths
10.0.3.0/24
10.0.1.0/24
10.0.2.0/24
bb0
eth0
3
eth1
3
D
B
C
0.0.0.0
10.0.0.0/24
A
bb1
eth0
1
eth1
1
45
10
eth0
2
eth1
1
bb2
10
10
eth1
2
eth0
2
bb3
7
10
bb4
eth1
2
eth0
1
10
10
36
21
Area ID
ospf cost for exiting the interface
shortest path to reach:
10.0.2.0/24
shortest path to reach:
10.0.3.0/24

## Slide 9: experiments
perform traceroutes from/to different interfaces
perform a traceroute –I from bb1 to 10.0.2.1
  what path is the traceroute expected to take?
  what path are ICMP replies expected to take?
perform a traceroute –I from bb1 to 10.0.3.2
  what path is the traceroute expected to take?
  observe the interplay between ospf routes and directly connected networks (i.e., perform a show ip route in frr)
try to alter the costs and observe the effect of the changes

## Slide 10: experiments
access the ospfd cli (or the vtysh cli) on the various routers and issue the following commands:
  show ip ospf database
  show ip ospf neighbor
  show ip ospf route
check that the lsdb is exactly the same for all routers

## Slide 11: designated routers (router interfaces designated for each network)
for each network, one of the interfaces attached to that network is elected as designated (dr)
priority-based election, using hello packets
  the router (interface) sending hello packets with highest piority wins the election
  break ties on highest router id
    by default, a router id is the address of one of its interfaces
  priority[0,255] default priority: 1 priority=0  never become a dr
a backup dr (i.e., the one with second highest priority) is also elected, to quickly recover from dr failures

## Slide 12: designated routers (router interfaces designated for each network)
a change of the dr is a change in ospf’s topology model (new lsas are sent)
for this reason, the dr is changed infrequently
  if a router with high priority wakes up and finds that a dr already exists, it accepts that dr

## Slide 13: designated routers (router interfaces designated for each network)
10.0.3.0/24
10.0.1.0/24
10.0.2.0/24
bb0
eth0
3
eth1
3
D
B
C
0.0.0.0
10.0.0.0/24
A
bb1
eth0
1
eth1
1
eth0
2
eth1
1
bb2
eth1
2
eth0
2
bb3
bb4
eth1
2
eth0
1
Area ID
designated
10.0.3.1
10.0.3.2
router id
10.0.2.2
10.0.1.1
10.0.2.3

## Slide 14: designated routers (router interfaces designated for each network)
bb1
eth0
1
eth1
1
designated
10.0.3.1
router id
bb1-frr# show ip ospf interface
eth0 is up
ifindex 106, MTU 1500 bytes, BW 10000 Mbit <UP,BROADCAST,RUNNING,MULTICAST>
Internet Address 10.0.0.1/24, Broadcast 10.0.0.255, Area 0.0.0.0
MTU mismatch detection: enabled
Router ID 10.0.3.1, Network Type BROADCAST, Cost: 10
Transmit Delay is 1 sec, State DR, Priority 1
Designated Router (ID) 10.0.3.1 Interface Address 10.0.0.1/24
Backup Designated Router (ID) 10.0.2.3, Interface Address 10.0.0.3
Saved Network-LSA sequence number 0x80000002
Multicast group memberships: OSPFAllRouters OSPFDesignatedRouters
Timer intervals configured, Hello 10s, Dead 40s, Wait 40s, Retransmit 5
Hello due in 8.859s
Neighbor Count is 2, Adjacent neighbor count is 2
eth1 is up
ifindex 116, MTU 1500 bytes, BW 10000 Mbit <UP,BROADCAST,RUNNING,MULTICAST>
Internet Address 10.0.3.1/24, Broadcast 10.0.3.255, Area 0.0.0.0
MTU mismatch detection: enabled
Router ID 10.0.3.1, Network Type BROADCAST, Cost: 45
Transmit Delay is 1 sec, State Backup, Priority 1
Designated Router (ID) 10.0.3.2 Interface Address 10.0.3.2/24
Backup Designated Router (ID) 10.0.3.1, Interface Address 10.0.3.1
Multicast group memberships: OSPFAllRouters OSPFDesignatedRouters
Timer intervals configured, Hello 10s, Dead 40s, Wait 40s, Retransmit 5
Hello due in 8.859s
Neighbor Count is 1, Adjacent neighbor count is 1
bb1

## Slide 15: ospf’s view of the network
by exchanging link state update packets, every router learns about the complete network topology, that is:
  routers
  subnets
  adjacencies between routers and networks

## Slide 16: ospf’s view of the network
kathara – [ labs: ospf ]
bb0-frr# show ip ospf database █
bb0

## Slide 17: ospf’s view of the network
kathara – [ labs: ospf ]
bb0
0.0.0.0
bb1
bb2
bb3
bb4
10.0.3.1
10.0.3.2
10.0.2.2
10.0.1.1
10.0.2.3
OSPF Router with ID (10.0.2.3)
Router Link States (Area 0.0.0.0)
Link ID ADV Router Age Seq# CkSum Link count
10.0.1.1 10.0.1.1 553 0x80000003 0xe9fa 2
10.0.2.2 10.0.2.2 552 0x80000003 0xe3fa 2
10.0.2.3 10.0.2.3 552 0x80000003 0xe7cd 2
10.0.3.1 10.0.3.1 552 0x80000003 0x3288 2
10.0.3.2 10.0.3.2 548 0x80000004 0x488d 2
█
bb0
for router lsas, the Link ID is the router’s id

## Slide 18: ospf’s view of the network
kathara – [ labs: ospf ]
bb0
0.0.0.0
bb1
bb2
bb3
bb4
10.0.3.1
10.0.3.2
10.0.2.2
10.0.1.1
10.0.2.3
Net Link States (Area 0.0.0.0)
Link ID ADV Router Age Seq# CkSum
10.0.0.1 10.0.3.1 557 0x80000001 0x6ba8
10.0.1.2 10.0.2.2 559 0x80000001 0x69bb
10.0.2.1 10.0.3.2 553 0x80000002 0x729a
10.0.3.2 10.0.3.2 553 0x80000001 0x6bb3
█
bb0
for network lsas, the Link ID is the dr’s address
10.0.3.2
10.0.1.2
10.0.2.1
10.0.0.1
D
B
C
A

## Slide 19: ospf’s view of the network
kathara – [ labs: ospf ]
bb0
0.0.0.0
bb1
bb3
bb4
10.0.3.1
10.0.3.2
10.0.2.2
10.0.1.1
10.0.2.3
bb0-frr# show ip ospf database router
Link State ID: 10.0.1.1
Number of Links: 2
Link connected to: a Transit Network
(Link ID) Designated Router address: 10.0.0.1
(Link Data) Router Interface address: 10.0.0.2
Link connected to: a Transit Network
(Link ID) Designated Router address: 10.0.1.2
(Link Data) Router Interface address: 10.0.1.1 █
bb0
note: the output of show ip ospf database router has been summarized
bb2
10.0.3.2
10.0.1.2
10.0.2.1
10.0.0.1
D
C
A
B

## Slide 20: ospf’s view of the network
kathara – [ labs: ospf ]
bb0
0.0.0.0
bb1
bb3
bb4
10.0.3.1
10.0.3.2
10.0.2.2
10.0.1.1
10.0.2.3
bb0-frr# show ip ospf database router
Link State ID: 10.0.1.1
Number of Links: 2
Link connected to: a Transit Network
(Link ID) Designated Router address: 10.0.0.1
(Link Data) Router Interface address: 10.0.0.2
Link connected to: a Transit Network
(Link ID) Designated Router address: 10.0.1.2
(Link Data) Router Interface address: 10.0.1.1 █
bb0
note: the output of show ip ospf database router has been summarized
bb2
10.0.3.2
10.0.1.2
10.0.2.1
10.0.0.1
D
C
A
B
we consider this router (bb2)

## Slide 21: ospf’s view of the network
kathara – [ labs: ospf ]
bb0
0.0.0.0
bb1
bb3
bb4
10.0.3.1
10.0.3.2
10.0.2.2
10.0.1.1
10.0.2.3
bb0-frr# show ip ospf database router
Link State ID: 10.0.1.1
Number of Links: 2
Link connected to: a Transit Network
(Link ID) Designated Router address: 10.0.0.1
(Link Data) Router Interface address: 10.0.0.2
Link connected to: a Transit Network
(Link ID) Designated Router address: 10.0.1.2
(Link Data) Router Interface address: 10.0.1.1 █
bb0
note: the output of show ip ospf database router has been summarized
this router interface...
10.0.3.2
10.0.1.2
10.0.2.1
10.0.0.1
D
C
A
B
bb2
...is connected to the subnet represented by this dr
eth0
2
eth1
1

## Slide 22: ospf’s view of the network
kathara – [ labs: ospf ]
bb0
0.0.0.0
bb1
bb4
10.0.3.1
10.0.3.2
10.0.2.2
10.0.1.1
10.0.2.3
Link State ID: 10.0.2.2
Number of Links: 2
Link connected to: a Transit Network
(Link ID) Designated Router address: 10.0.1.2
(Link Data) Router Interface address: 10.0.1.2
Link connected to: a Transit Network
(Link ID) Designated Router address: 10.0.2.1
(Link Data) Router Interface address: 10.0.2.2 █
bb0
note: the output of show ip ospf database router has been summarized
10.0.3.2
10.0.1.2
10.0.2.1
10.0.0.1
D
A
eth0
2
eth1
1
bb2
B
C
bb3
eth0
2
eth1
2

## Slide 23: ospf’s view of the network
kathara – [ labs: ospf ]
bb0
0.0.0.0
bb1
bb4
10.0.3.1
10.0.3.2
10.0.2.2
10.0.1.1
10.0.2.3
Link State ID: 10.0.2.2
Number of Links: 2
Link connected to: a Transit Network
(Link ID) Designated Router address: 10.0.1.2
(Link Data) Router Interface address: 10.0.1.2
Link connected to: a Transit Network
(Link ID) Designated Router address: 10.0.2.1
(Link Data) Router Interface address: 10.0.2.2 █
bb0
note: the output of show ip ospf database router has been summarized
10.0.3.2
10.0.2.1
10.0.0.1
D
A
eth0
2
eth1
1
bb2
B
C
bb3
eth0
2
eth1
2

## Slide 24: ospf’s view of the network
kathara – [ labs: ospf ]
Link State ID: 10.0.2.3
Number of Links: 2
Link connected to: a Transit Network
(Link ID) Designated Router address: 10.0.0.1
(Link Data) Router Interface address: 10.0.0.3
Link connected to: a Transit Network
(Link ID) Designated Router address: 10.0.2.1
(Link Data) Router Interface address: 10.0.2.3 █
bb0
10.0.3.2
10.0.2.1
10.0.0.1
D
0.0.0.0
bb1
bb4
10.0.3.1
10.0.3.2
10.0.2.2
10.0.1.1
note: the output of show ip ospf database router has been summarized
eth0
2
eth1
1
bb2
B
eth0
2
eth1
2
bb3
A
C
bb0
10.0.2.3
eth0
3
eth1
3

## Slide 25: ospf’s view of the network
kathara – [ labs: ospf ]
0.0.0.0
bb4
10.0.3.1
10.0.3.2
10.0.2.2
10.0.1.1
10.0.2.3
Link State ID: 10.0.3.1
Number of Links: 2
Link connected to: a Transit Network
(Link ID) Designated Router address: 10.0.0.1
(Link Data) Router Interface address: 10.0.0.1
Link connected to: a Transit Network
(Link ID) Designated Router address: 10.0.3.2
(Link Data) Router Interface address: 10.0.3.1 █
bb0
note: the output of show ip ospf database router has been summarized
eth1
1
eth0
2
eth0
3
bb0
eth1
3
bb1
10.0.3.2
10.0.2.1
10.0.0.1
B
C
D
A
bb3
eth0
1
eth1
1
eth1
2
eth0
2
bb2

## Slide 26: ospf’s view of the network
kathara – [ labs: ospf ]
0.0.0.0
bb4
10.0.3.1
10.0.3.2
10.0.2.2
10.0.1.1
10.0.2.3
Link State ID: 10.0.3.1
Number of Links: 2
Link connected to: a Transit Network
(Link ID) Designated Router address: 10.0.0.1
(Link Data) Router Interface address: 10.0.0.1
Link connected to: a Transit Network
(Link ID) Designated Router address: 10.0.3.2
(Link Data) Router Interface address: 10.0.3.1 █
bb0
note: the output of show ip ospf database router has been summarized
eth1
1
eth0
2
eth0
3
bb0
eth1
3
bb1
10.0.3.2
10.0.2.1
B
C
D
A
eth0
2
bb2
eth0
1
eth1
1
eth1
2
bb3

## Slide 27: ospf’s view of the network
kathara – [ labs: ospf ]
0.0.0.0
10.0.3.1
10.0.3.2
10.0.2.2
10.0.1.1
10.0.2.3
Link State ID: 10.0.3.2
Number of Links: 2
Link connected to: a Transit Network
(Link ID) Designated Router address: 10.0.2.1
(Link Data) Router Interface address: 10.0.2.1
Link connected to: a Transit Network
(Link ID) Designated Router address: 10.0.3.2
(Link Data) Router Interface address: 10.0.3.2 █
bb0
note: the output of show ip ospf database router has been summarized
eth0
2
eth1
1
bb2
B
eth0
2
eth1
2
bb3
eth0
3
bb0
eth1
3
bb1
eth0
1
A
bb4
eth1
1
10.0.3.2
10.0.2.1
C
D
eth1
2
eth0
1

## Slide 28: ospf’s view of the network
kathara – [ labs: ospf ]
0.0.0.0
10.0.3.1
10.0.3.2
10.0.2.2
10.0.1.1
10.0.2.3
Link State ID: 10.0.3.2
Number of Links: 2
Link connected to: a Transit Network
(Link ID) Designated Router address: 10.0.2.1
(Link Data) Router Interface address: 10.0.2.1
Link connected to: a Transit Network
(Link ID) Designated Router address: 10.0.3.2
(Link Data) Router Interface address: 10.0.3.2 █
bb0
note: the output of show ip ospf database router has been summarized
eth0
2
eth1
1
bb2
B
eth0
2
eth1
2
bb3
eth0
3
bb0
eth1
3
bb1
eth0
1
A
bb4
C
D
eth1
1
eth1
2
eth0
1

## Slide 29: ospf’s view of the network
kathara – [ labs: ospf ]
0.0.0.0
10.0.3.1
10.0.3.2
10.0.2.2
10.0.1.1
10.0.2.3
bb0-frr# show ip ospf database network █
bb0
eth0
2
eth1
1
bb2
B
eth0
2
eth1
2
bb3
eth0
3
bb0
eth1
3
bb1
eth0
1
A
bb4
eth1
2
eth0
1
C
D
eth1
1

## Slide 30: ospf’s view of the network
kathara – [ labs: ospf ]
0.0.0.0
10.0.3.1
10.0.3.2
10.0.2.2
10.0.1.1
10.0.2.3
Link State ID: 10.0.0.1 (address of Designated Router)
Advertising Router: 10.0.3.1
Network Mask: /24
Attached Router: 10.0.3.1
Attached Router: 10.0.1.1
Attached Router: 10.0.2.3 █
bb0
eth0
2
eth1
1
bb2
B
eth0
2
eth1
2
bb3
eth0
3
bb0
eth1
3
bb1
eth0
1
bb4
eth1
2
eth0
1
C
D
note: the output of show ip ospf database network has been summarized
10.0.0.0/24
A
eth1
1

## Slide 31: ospf’s view of the network
kathara – [ labs: ospf ]
0.0.0.0
10.0.3.1
10.0.3.2
10.0.2.2
10.0.1.1
10.0.2.3
Link State ID: 10.0.1.2 (address of Designated Router)
Advertising Router: 10.0.2.2
Network Mask: /24
Attached Router: 10.0.1.1
Attached Router: 10.0.2.2 █
bb0
eth0
2
eth1
1
bb2
eth0
2
eth1
2
bb3
eth0
3
bb0
eth1
3
bb1
eth0
1
bb4
eth1
2
eth0
1
C
D
note: the output of show ip ospf database network has been summarized
10.0.0.0/24
A
B
10.0.1.0/24
eth1
1

## Slide 32: ospf’s view of the network
kathara – [ labs: ospf ]
0.0.0.0
10.0.3.1
10.0.3.2
10.0.2.2
10.0.1.1
10.0.2.3
Link State ID: 10.0.2.1 (address of Designated Router)
Advertising Router: 10.0.3.2
Network Mask: /24
Attached Router: 10.0.3.2
Attached Router: 10.0.2.2
Attached Router: 10.0.2.3 █
bb0
eth0
2
eth1
1
bb2
eth0
2
eth1
2
bb3
eth0
3
bb0
eth1
3
bb1
eth0
1
bb4
eth1
2
eth0
1
note: the output of show ip ospf database network has been summarized
10.0.0.0/24
A
B
10.0.1.0/24
D
10.0.2.0/24
C
eth1
1

## Slide 33: ospf’s view of the network
kathara – [ labs: ospf ]
0.0.0.0
10.0.3.1
10.0.3.2
10.0.2.2
10.0.1.1
10.0.2.3
Link State ID: 10.0.3.2 (address of Designated Router)
Advertising Router: 10.0.3.2
Network Mask: /24
Attached Router: 10.0.3.1
Attached Router: 10.0.3.2 █
bb0
eth0
2
eth1
1
bb2
eth0
2
eth1
2
bb3
eth0
3
bb0
eth1
3
bb1
eth0
1
bb4
eth1
2
eth0
1
note: the output of show ip ospf database network has been summarized
10.0.0.0/24
A
B
10.0.1.0/24
10.0.2.0/24
C
10.0.3.0/24
D
eth1
1

## Slide 34: ospf’s view of the network
kathara – [ labs: ospf ]
10.0.3.0/24
10.0.1.0/24
10.0.2.0/24
bb0
eth0
3
eth1
3
D
B
C
0.0.0.0
10.0.0.0/24
A
bb1
eth0
1
eth1
1
eth0
2
eth1
1
bb2
eth1
2
eth0
2
bb3
bb4
eth1
2
eth0
1
10.0.3.1
10.0.3.2
10.0.2.2
10.0.1.1
10.0.2.3
bb0:~# vtysh -e "show ip ospf interface" | egrep "eth|Cost"
eth0 is up
Router ID 10.0.2.3, Network Type BROADCAST, Cost: 21
eth1 is up
Router ID 10.0.2.3, Network Type BROADCAST, Cost: 36
█
bb0
ospf interface costs can be queried on all routers
36
21
a shortcut to quickly get the cost

## Slide 35: neighborhood
router neighbors can be shown by using the show ip ospf neighbor command
note: lsas are only sent between neighbors in Full state (i.e., capable of a bidirectional exchange of information); reaching the Full state requires that:
  neighbors have been discovered (using hello packets)
  bidirectional communication is possible
  a designated router has been elected
once reached, routers immediately synchronize their lsdbs
bb0-frr# show ip ospf neighbor
Neighbor ID Pri State Dead Time Address Interface RXmtL RqstL DBsmL
10.0.3.1 1 Full/DR 30.462s 10.0.0.1 eth0:10.0.0.3 0 0 0
10.0.1.1 1 Full/DROther 30.462s 10.0.0.2 eth0:10.0.0.3 0 0 0
10.0.3.2 1 Full/DR 31.587s 10.0.2.1 eth1:10.0.2.3 0 0 0
10.0.2.2 1 Full/DROther 31.586s 10.0.2.2 eth1:10.0.2.3 0 0 0
bb0-frr# █
bb0

## Slide 36: ospf routing table
the ospf routing table can be dumped by using show ip ospf route
bb0-frr# show ip ospf route
============ OSPF network routing table ============
N 10.0.0.0/24 [21] area: 0.0.0.0
directly attached to eth0
N 10.0.1.0/24 [31] area: 0.0.0.0
via 10.0.0.2, eth0
N 10.0.2.0/24 [36] area: 0.0.0.0
directly attached to eth1
N 10.0.3.0/24 [46] area: 0.0.0.0
via 10.0.2.1, eth1
============ OSPF router routing table =============
R 10.0.1.1 [21] area: 0.0.0.0, ASBR
via 10.0.0.2, eth0
R 10.0.2.2 [31] area: 0.0.0.0, ASBR
via 10.0.0.2, eth0
R 10.0.3.1 [21] area: 0.0.0.0, ASBR
via 10.0.0.1, eth0
R 10.0.3.2 [36] area: 0.0.0.0, ASBR
via 10.0.2.1, eth1
============ OSPF external routing table ===========
bb0-frr# █
bb0
route cost

## Slide 37: experiments
issue the show ip ospf database and show ip ospf neighbor commands on different routers
capture and look at exchanged ospf packets using tcpdump

## Slide 38: ospf is fast at detecting topology changes
case #1: link fault
  bring down a single network interface using ifconfig
    the change is immediately propagated by the router inside lsa packets
    routing tables are immediately updated (show ip ospf route)

## Slide 39: ospf is fast at detecting topology changes
case #1: link fault
  bring down a single network interface using ifconfig
    the change is immediately propagated by the router inside lsa packets
    routing tables are immediately updated (show ip ospf route)
    the lsdb is handled a little differently...

## Slide 40: ospf is fast at detecting topology changes
last update: Nov 2018
kathara – [ labs: ospf ]
case #1: link fault
  bring down a single network interface using ifconfig
    if this brings down a dr, the information is immediately flushed from the lsdb(s)...
      ...and eventually reannounced when a dr is re-elected
    otherwise, ospf waits expiry of the RouterDeadInterval timer (default: 40s) before removing the adjacency from the lsdb (show ip ospf database network)
      note: networks that are connected to one router only, called stub networks, are only visible using show ip ospf database router

## Slide 41: ospf is fast at detecting topology changes
case #1: link fault
  bring down a single network interface using ifconfig
overall reaction time (estimated)
min
max
0
RouterDeadInterval

## Slide 42: ospf is (often) fast at detecting topology changes
last update: Nov 2018
kathara – [ labs: ospf ]
case #2: router fault
  bring down a router (by crashing it or by shutting down all its interfaces simultaneously)
  the router has no chance to propagate lsas
    the change cannot be immediately propagated
    neighboring routers can only realize it (and update routing tables) after expiry of the RouterDeadInterval timer

## Slide 43: ospf is (often) fast at detecting topology changes
last update: Nov 2018
kathara – [ labs: ospf ]
case #2: router fault
  bring down a router (by crashing it or by shutting down all its interfaces simultaneously)
  after the change has been propagated...
    ...lsdb information about networks for which the failed router was not dr is immediately flushed from other routers’ lsdbs
      the dr takes care of sending appropriate lsas
    ...lsdb information about networks for which the failed router was dr (including those where a dr will be re-elected) and about routers is more “tough”
      ospf waits for the lsa to expire (expiration happens when the age of the lsa reaches the MaxAge value of 1 hour) before taking any actions

## Slide 44: ospf is (often) fast at detecting topology changes
case #2: router fault
  bring down a router (by crashing it or by shutting down all its interfaces simultaneously)
overall reaction time (estimated)
min
max
RouterDeadInterval
MaxAge

## Slide 45: lab: ospf-multiarea

## Slide 46: ospf areas
an abstraction that simplifies administration and improves scalability
  the topology of an area is invisible from the outside
  routers internal to a given area don’t see the detailed external topology
each area runs a separate instance of the link state routing algorithm
  all routers in an area construct the same lsdb
  each router keeps a distinct lsdb for each area it belongs to

## Slide 47: ospf areas
identified by a 32-bit number, often in dotted decimal notation (1.2.3.4)
  different interfaces of the same router can be assigned to different areas
  each
    router interface...
    network...
    router adjacency...
  ...is associated with a single area

## Slide 48: area types
backbone (0.0.0.0)
  must be (virtually) connected
  all other areas are connected to it
  contains all the area border routers
stub
  does not receive advertisements of external routes
  internal nodes are offered a default route
  cannot contain autonomous system boundary routers
  the backbone can’t be a stub area
transit
  used to pass traffic from one adjacent area to another, via virtual links

## Slide 49
last update: Nov 2018
kathara – [ labs: ospf ]
0.0.0.0
1.1.1.1
2.2.2.2
3.3.3.3
backbone
stub
stub
stub

## Slide 50: router types
internal router
  all interfaces belong to the same area
area border router (abr)
  connects one or more areas to the backbone
  keeps multiple lsdbs, one for each area
backbone router
  has at least one interface connected to the backbone
  an abr is always a backbone router
autonomous system boundary router (asbr)
  imports and floods routing information from other routing protocols (typically, bgp)
note: a router can be of more than one type

## Slide 51
kathara – [ labs: ospf ]
bb4
bb0
0.0.0.0
1.1.1.1
2.2.2.2
3.3.3.3
r1
r2
r6
bb3
r5
bb2
r4
r3
bb1

## Slide 52
kathara – [ labs: ospf ]
bb4
bb0
0.0.0.0
1.1.1.1
2.2.2.2
3.3.3.3
r1
r2
r6
bb3
r5
bb2
r4
r3
bb1
backbone
routers

## Slide 53
kathara – [ labs: ospf ]
bb4
bb0
0.0.0.0
1.1.1.1
2.2.2.2
3.3.3.3
r1
r2
r6
bb3
r5
bb2
r4
r3
bb1
area border
routers

## Slide 54
kathara – [ labs: ospf ]
bb4
bb0
0.0.0.0
1.1.1.1
2.2.2.2
3.3.3.3
r1
r2
r6
bb3
r5
bb2
r4
r3
bb1
internal
routers

## Slide 55
kathara – [ labs: ospf ]
10.0.3.0/24
10.0.1.0/24
bb4
10.0.2.0/24
10.0.0.0/24
bb0
eth0
3
eth1
3
D
A
B
C
0.0.0.0
eth0
2
eth2
1
E
100.0.0.0/30
1.1.1.1
2.2.2.2
3.3.3.3
r1
eth0
2
eth1
1
I
200.0.0.0/30
r2
J
200.0.1.0/24
r6
L
220.0.0.0/30
N
220.0.1.0/30
M
220.0.2.0/30
eth0
1
eth1
1
eth0
2
eth1
2
eth1
1
eth1
1
eth0
1
eth0
2
eth1
2
eth1
1
eth0
1
eth1
2
eth1
1
eth0
2
eth0
2
bb3
210.0.0.0/24
r5
eth2
2
eth2
1
H
130.0.0.0/30
bb2
eth3
1
r4
G
120.0.0.0/30
eth0
2
K
eth3
1
110.0.0.0/30
F
eth1
2
eth2
1
r3
bb1
90
100
default cost (10) is assumed where unspecified

## Slide 56: area configuration
area information is found in two places
  when enabling ospf on router interfaces network 200.0.0.0/16 area 1.1.1.1
  when specifying the area type (not required for the backbone) area 1.1.1.1 stub

## Slide 57: ospf path types
there are 4 path types
  intra-area
  inter-area
  external type 1
  external type 2
types can coexist in the same network
each type is preferred over the following ones

## Slide 58: ospf path types
intra-area paths
  calculated using the shortest-path tree

## Slide 59: ospf path types
inter-area paths
  abrs inject summary information inside each area, to make it aware of available destinations in other areas
    such information includes the cost of the shortest path from the abr to the destination
    if multiple subnets are summarized into a single network, the route cost will be the maximum cost to any of the component subnets
  an inter-area path is always composed of:
    an intra-area path from the source to the abr
    a backbone path between the source and destination areas
    an intra-area path to the destination

## Slide 60: ospf path types
last update: Nov 2018
kathara – [ labs: ospf ]
* cost used when redistributing the protocol (bgp) into ospf; default for bgp=20; configurable by using redistribute bgp metric value
external paths are learned from other routing protocols (e.g., bgp)
type 1: the cost is expressed in terms of
  the external (bgp) route cost* +
  the ospf cost to the asbr
  example with bgp cost=495, ospf cost=10: N E1 50.0.0.0/16 [505] tag: 0 via 10.0.1.2, eth1

## Slide 61: ospf path types
last update: Nov 2018
kathara – [ labs: ospf ]
external paths are learned from other routing protocols (e.g., bgp)
type 1: the cost is expressed in terms of
  the external (bgp) route cost* +
  the ospf cost to the asbr
type 2: the cost is expressed in terms of
  the external (bgp) route cost* only (distance to the asbr is only used to break ties)
  example with bgp cost=495, ospf cost=10: N E2 50.0.0.0/16 [10/495] tag: 0
  via 10.0.1.2, eth1

## Slide 62: ospf path types
last update: Nov 2018
external paths are learned from other routing protocols (e.g., bgp)
type 1: the cost is expressed in terms of
  the external (bgp) route cost* +
  the ospf cost to the asbr
type 2: the cost is expressed in terms of
  the external (bgp) route cost* only (distance to the asbr is only used to break ties)
metric type is user-configurable redistribute bgp metric-type 2 metric 495

## Slide 63: experiments
last update: Nov 2018
kathara – [ labs: ospf ]
check that routers know detailed topology information only about their own area
r2-frr# show ip ospf neighbor
Neighbor ID Pri State Dead Time Address Interface RXmtL RqstL DBsmL
200.0.0.1 1 Full/Backup 34.184s 200.0.0.1 eth0:200.0.0.2 0 0 0
r2-frr# show ip ospf database router
OSPF Router with ID (200.0.1.1)
Router Link States (Area 1.1.1.1 [Stub])
Link State ID: 110.0.0.1
Number of Links: 1
Link connected to: a Transit Network
(Link ID) Designated Router address: 100.0.0.2
(Link Data) Router Interface address: 100.0.0.1
Link State ID: 200.0.0.1
Number of Links: 2
Link connected to: a Transit Network
(Link ID) Designated Router address: 100.0.0.2
(Link Data) Router Interface address: 100.0.0.2
Link connected to: a Transit Network
(Link ID) Designated Router address: 200.0.0.2
(Link Data) Router Interface address: 200.0.0.1
Link State ID: 200.0.1.1
Number of Links: 2
Link connected to: a Transit Network
(Link ID) Designated Router address: 200.0.0.2
(Link Data) Router Interface address: 200.0.0.2
Link connected to: Stub Network
(Link ID) Net: 200.0.1.0
(Link Data) Network Mask: 255.255.255.0 █
r2
note: the output has been summarized

## Slide 64: experiments
last update: Nov 2018
kathara – [ labs: ospf ]
check that routers know detailed topology information only about their own area
r2-frr# show ip ospf database network
OSPF Router with ID (200.0.1.1)
Net Link States (Area 1.1.1.1 [Stub])
LS age: 448
Options: 0x0 : *|-|-|-|-|-|-|*
LS Flags: 0x6
LS Type: network-LSA
Link State ID: 100.0.0.2 (address of Designated Router)
Advertising Router: 200.0.0.1
LS Seq Number: 80000002
Checksum: 0x07ed
Length: 32
Network Mask: /30
Attached Router: 110.0.0.1
Attached Router: 200.0.0.1
LS age: 452
Options: 0x0 : *|-|-|-|-|-|-|*
LS Flags: 0x1
LS Type: network-LSA
Link State ID: 200.0.0.2 (address of Designated Router)
Advertising Router: 200.0.1.1
LS Seq Number: 80000002
Checksum: 0x6cc7
Length: 32
Network Mask: /30
Attached Router: 200.0.0.1
Attached Router: 200.0.1.1
r2-frr# █
r2

## Slide 65: experiments
check what routers know about the outside of the area, using the show ip ospf database summary command
  in particular, check the Metric values, that show how far away the destination is from the advertising abr
check that routers in stub areas are offered a default route, whereas routers in the backbone are not
  also check what Metric is assigned to the default route

## Slide 66: experiments
experiment ospf’s recovery capabilities
  when multiple equal cost routes are available, ospf keeps all of them
  check it by verifying what r3 knows about the default route
r3-frr# show ip ospf route
============ OSPF network routing table ============
N IA 0.0.0.0/0 [11] area: 2.2.2.2
via 110.0.0.1, eth1
via 120.0.0.1, eth0
█
r3
inter-area path
equal cost routes

## Slide 67: experiments
last update: Nov 2018
kathara – [ labs: ospf ]
experiment ospf’s recovery capabilities
  when multiple equal cost routes are available, ospf keeps all of them
  check it by verifying what r3 knows about the default route
  zebra performs the actual selection
r3-frr# show ip route
Codes: K - kernel route, C - connected, S – static, R - RIP, O - OSPF,
I - ISIS, B - BGP, > - selected route, * - FIB route
O>* 0.0.0.0/0 [110/11] via 110.0.0.1, eth1, 00:04:56
* via 120.0.0.1, eth0, 00:04:56
█
r3

## Slide 68: experiments
experiment ospf’s recovery capabilities
  when multiple equal cost routes are available, ospf keeps all of them
  check it by verifying what r3 knows about the default route
  zebra performs the actual selection
    now bring bb1’s eth3 down using ifconfig, wait a few seconds and check how the routing is changed
    bring bb1’s eth3 back up and check again how the routing is changed

## Slide 69: lab: ospf-complex

## Slide 70
last update: Nov 2018
kathara – [ labs: ospf ]
10.0.3.0/24
10.0.1.0/24
bb4
10.0.2.0/24
10.0.0.0/24
bb0
eth0
3
eth1
3
D
A
B
C
0.0.0.0
eth0
2
eth2
1
E
100.0.0.0/30
1.1.1.1
2.2.2.2
3.3.3.3
r1
eth0
2
eth1
1
I
200.0.0.0/30
r2
J
200.0.1.0/24
r6
L
220.0.0.0/30
N
220.0.1.0/30
M
220.0.2.0/30
eth0
1
eth1
1
eth0
2
eth1
2
eth1
1
eth1
1
eth0
1
eth0
2
eth1
2
eth1
1
eth0
1
eth1
2
eth1
1
eth0
2
eth0
2
bb3
as100r1
210.0.0.0/24
eth2
1
eth0
2
O
140.0.0.0/30
r5
50.0.0.0/16
AS10
AS100
eth2
2
eth2
1
H
130.0.0.0/30
bb2
eth3
1
r4
G
120.0.0.0/30
eth0
2
K
eth3
1
110.0.0.0/30
F
eth1
2
eth2
1
r3
bb1
90
100
default cost (10) is assumed where unspecified

## Slide 71: lab description
same as multiarea + some information is injected via bgp from an external as
  also, abrs are configured to just inject the default route area 1.1.1.1 stub no-summary
perform the same experiments as for the multiarea lab
  in addition, check asbr information using show ip ospf database asbr-summary
  also check that such information is not propagated inside stub areas

## Slide 72: a quick note about stub networks
kathara – [ labs: ospf ]
“stub” = not used for transit
three possible situations:
r2
J
200.0.1.0/24
eth1
1
ospf is enabled also on the stub network’s interface
the stub network is advertised in the entire ospf domain
interface uselessly sends hello packets
ospf is not enabled on the stub network’s interface
the stub network is advertised
the stub network is advertised as an AS-external route (hence, only through the backbone)
ospf is enabled on the stub network’s interface, which is configured as passive-interface
the stub network is advertised in the entire ospf domain
N/A
then
but
then
but
then
but