## Slide 1: data centers and VXLAN
Version | 3.1
Author(s) | L. Ariemma, G. Di Battista, M. Patrignani, M. Scazzariello, T. Caiazzi
E-mail | contact@kathara.org
Web | http://www.kathara.org/
Description | Data Centers’ Routing: BGP and VXLAN

## Slide 2: copyright notice
all the pages/slides in this presentation, including but not limited to, images, photos, animations, videos, sounds, music, and text (hereby referred to as “material”) are protected by copyright
this material, with the exception of some multimedia elements licensed by other organizations, is property of the authors and/or organizations appearing in the first slide
this material, or its parts, can be reproduced and used for didactical purposes within universities and schools, provided that this happens for non-profit purposes
any other use is prohibited, unless explicitly authorized by the authors on the basis of an explicit agreement
this copyright notice must always be redistributed together with the material, or its portions

## Slide 3: a Fat-Tree with BGP routing
Servers
Containers or VMs
Prefixes are assigned directly to the servers
each Leaf announces its server’s prefix

## Slide 4: drawbacks of using just BGP
containers/VMs share the same IP prefix of the server
  no possibility to move containers between servers without IP remapping
tenants must follow the IP plan of the data center
  cannot expose containers with custom IPs
there is no isolation between
  the data center traffic and the tenant's traffic
  different tenants

## Slide 5: how to handle multiple tenants?
again, why (EVPN) BGP?

## Slide 6: overview – multiple tenants
requirements
  servers’ architecture requirements
  orchestration requirements
  tenant requirements
tunneling protocols
VXLAN
EVPN-BGP

## Slide 7: servers' architecture requirements
having services directly on bare metal is not used
  too many physical servers needed
  no way to scale if more resources are requested
  no isolation between different services on the same server
support a virtual layer of containers or VMs
  high-availability guaranteed via orchestration
  useful for resource-slicing
  complete isolation between different containers or VMs on the same server
    possibility to assign containers or VMs to different tenants

## Slide 8: orchestration requirements
an orchestrator is a software that manages the lifecycle of containers/VMs
  creates, moves, and destroys containers/VMs
needed for
  optimal resource allocation, handling failures, management
when moving a container/VM
  possibility to keep network configurations (MAC/IP)
  minimal downtime

## Slide 9: tenant requirements
each tenant wants to independently manage its own private IP address space
  containers/VMs traffic must be segregated between tenants and between the data center traffic

## Slide 10: consequence of requirements
server, orchestration, and tenant requirements have a consequence
  usage of tunnels

## Slide 11: tunneling protocol requirements
minimal configuration
encapsulate the traffic of each tenant
  an identifier of the tenant is needed
encapsulation in Layer-4
  to fully exploit IP Multi-Path
  to traverse routers
    data center fabric is Layer-3
  to traverse Internet
    different data centers must interconnect via Internet transparently (to create the so called regions)

## Slide 12: possible choices for tunneling
VLAN
  can be used only in L2, the data center is L3
MPLS
  each router must be configured for each new tenant
  traversing Internet requires ISP to configure intermediate routers
VXLAN
  created ad-hoc 

## Slide 13: VXLAN
Virtual eXtensible Local Area Network (RFC-7348)
designed to address the need for overlay networks within virtualized data centers accommodating multiple tenants
encapsulates Layer-2 frames into UDP packets

## Slide 14: VXLAN terminology
VNI: VXLAN Network Identifier
  identifier of a specific VXLAN tunnel
  similar to the VLAN ID
  24 bit address space, more than 16M possible VNIs
VTEP: VXLAN Tunnel End Point
  device (physical or virtual) that encapsulates and decapsulates VXLAN packets

## Slide 15: VXLAN encapsulation
overhead of 50 bytes
random Source Port to fully exploit Multi-Path

## Slide 16: MAC-to-VTEP Table
hosted in each VTEP
similar to the switch forwarding table
for each VNI the VTEP keeps a table of pairs <mac,ip>, that associates MAC Addresses and destination VTEP IPs
each physical (or VLAN) L2 interface of a VTEP is assigned to a VNI
  the MAC addresses learned on such interfaces are local, and the IPs of their pairs is replaced by the word local

## Slide 17: MAC-to-VTEP Table
when a VTEP receives a frame destinated to a MAC Address m from a local interface belonging to a certain VNI, it checks for the existence (in the VNI) of a pair <m,i> containing m
  if the pair exists, the VTEP encapsulates the frame, and sends the resulting packet to the destination VTEP IP i
  if not, the frame is sent to all the other VTEPs (encapsulated) and to all the local ports of that VNI

## Slide 18: VXLAN transport
VTEP
VTEP
Host 1
Host 2
193.204.0.0/15
10.0.0.0/24
10.0.0.0/24
.1
0:A
.2
0:B
L2 Packets
VXLAN Packets, VNI 100
L2 Packets
0:A 100 local
0:B 100 193.204.0.2
0:B 100 local
0:A 100 193.204.0.1
.1
.2

## Slide 19: how to handle broadcast traffic
two types of broadcast must be handled
  traffic directed to the MAC broadcast address
    e.g., ARP traffic
  traffic directed to a MAC address that has not been learned
IP multicast groups are used by default
  each VNI is assigned to an IP multicast group of the underlay network and each VTEP subscribes itself to each group of its VNIs
  the multicast group of a VNI is used only to send the broadcast traffic

## Slide 20: disadvantages of multicast
multicast must be enabled in the underlay network
  it may require to deploy several protocols
    e.g., IGMP, IGMP Snooping, PIM, ….
  complex configuration
if multicast is not enabled, broadcast frames are duplicated and sent unicast to all the VTEPs of the VNI
proxy ARP techniques can be used to mitigate broadcast traffic

## Slide 21: EVPN-BGP
Ethernet VPN (RFC-7432 and RFC-8365)
uses MP-BGP with specific AFI/SAFI
  Address Family Identifier/Subsequent AFI
  AFI=25 (L2VPN) – SAFI=70 (EVPN)
advertises MAC Addresses of VNIs using BGP updates
a VTEP automatically learns local MAC Addresses and advertises them to all other VTEPs (of the same VNI)
VTEP proxies ARP requests to limit broadcast traffic

## Slide 22: VXLAN and EVPN-BGP transport
VTEP
VTEP
Host 1
Host 2
193.204.0.0/15
.1
.2
10.0.0.0/24
10.0.0.0/24
.1
0:A
.2
0:B
0:A 100 local
0:B 100 193.204.0.2
0:B 100 local
0:A 100 193.204.0.1
eBGP multihop peering
0:A 100 local
0:A 100 193.204.0.1
0:A 100 193.204.0.1
0:B 100 193.204.0.2
0:B
0:A
(+ BGP Router)
(+ BGP Router)

## Slide 23: VXLAN and EVPN-BGP Lab
time to use Kathará

## Slide 24: topology
.1
.2
s1
A
vtep1
vtep2
B
C
10.0.0.0/24
193.204.0.0/30
10.0.0.0/24
s2
.1
.2

## Slide 25: lab base config – topology, s1, and s2
ip address add 10.0.0.1/24 dev eth0
ip link set dev eth0 mtu 1450
systemctl start apache2
s1.startup
ip address add 10.0.0.2/24 dev eth0
ip link set dev eth0 mtu 1450
systemctl start apache2
s2.startup
s1[0]=A
vtep1[0]=A
vtep1[1]=B
vtep2[0]=C
vtep2[1]=B
s2[0]=C
lab.conf

## Slide 26: MTU
need to set manual MTU of each device’s interface associated to a VNI
when a frame is encapsulated by a VTEP, if its size is greater than 1450 (LAN MTU – VXLAN overhead)
  the frame is dropped
  an ICMP “packet too big” message is sent back

## Slide 27: configuring a bridge/router with VTEPs
we need to configure a Kathara device that is able to:
  act as a bridge on L2 ports
    able to perform L2 learning
  act as a router on the ports on the underlay networks
    able to establish BGP peerings
    able to encapsulate/decapsulate VXLAN traffic

## Slide 28: VTEP configuration
create bridge facilities (aka companion bridges)
  one virtual bridge with ports assigned to VLANs corresponding to VNIs
attach the collision domains associated to a VNI to the companion bridge of that VNI
configure the base BGP peerings
  enable the AFI/SAFI of EVPN
configure VXLAN

## Slide 29: vtep e-BGP configuration
router bgp 1
neighbor 193.204.0.2 remote-as 2
address-family l2vpn evpn
neighbor 193.204.0.2 activate
advertise-all-vni
exit-address-family
vtep1/etc/frr/bgpd.conf
router bgp 2
neighbor 193.204.0.1 remote-as 1
address-family l2vpn evpn
neighbor 193.204.0.1 activate
advertise-all-vni
exit-address-family
vtep2/etc/frr/bgpd.conf
activate the address-family on the peering with specific neighbor
announce on the peerings all the VNIs configured in the VTEP

## Slide 30: companion bridge
the bridge connected to VTEP interfaces
used by the VTEP to perform source address learning of local interfaces
when in combination with EVPN-BGP
  its forwarding table is also populated via updates received from BGP
  the FRR control plane watch to updates of the bridge forwarding table to send updates via BGP

## Slide 31: vtep1 bridge configuration
ip address add 193.204.0.1/30 dev eth1
# Setting up VXLAN interfaces
ip link add vtep100 type vxlan id 100 dev eth1 dstport 4789 local 193.204.0.1 nolearning
# Creating the companion bridge
ip link add br100 type bridge
ip link set br100 addrgenmode none
# Attach interfaces to the bridge
ip link set dev vtep100 master br100 addrgenmode none
ip link set vtep100 type bridge_slave neigh_suppress on learning off
ip link set dev eth0 master br100
# Enable interfaces
ip link set up dev vtep100
ip link set up dev br100
# Enabling FRR
systemctl start frr
vtep1.startup
create the interface
name of the interface
VNI
VXLAN dst port
VXLAN src IP
disable the mcast learning
attach eth0 (the server s1 collision domain) to the bridge

## Slide 32: vtep1 bridge configuration
ip address add 193.204.0.1/30 dev eth1
# Setting up VXLAN interfaces
ip link add vtep100 type vxlan id 100 dev eth1 dstport 4789 local 193.204.0.1 nolearning
# Creating the companion bridge
ip link add br100 type bridge
ip link set br100 addrgenmode none
# Attach interfaces to the bridge
ip link set dev vtep100 master br100 addrgenmode none
ip link set vtep100 type bridge_slave neigh_suppress on learning off
ip link set dev eth0 master br100
# Enable interfaces
ip link set up dev vtep100
ip link set up dev br100
# Enabling FRR
systemctl start frr
vtep1.startup
create the companion bridge and name it

## Slide 33: vtep1 bridge configuration
ip address add 193.204.0.1/30 dev eth1
# Setting up VXLAN interfaces
ip link add vtep100 type vxlan id 100 dev eth1 dstport 4789 local 193.204.0.1 nolearning
# Creating the companion bridge
ip link add br100 type bridge
ip link set br100 addrgenmode none
# Attach interfaces to the bridge
ip link set dev vtep100 master br100 addrgenmode none
ip link set vtep100 type bridge_slave neigh_suppress on learning off
ip link set dev eth0 master br100
# Enable interfaces
ip link set up dev vtep100
ip link set up dev br100
# Enabling FRR
systemctl start frr
vtep1.startup
disable IPv6 link-local generation on the bridge

## Slide 34: vtep1 bridge configuration
ip address add 193.204.0.1/30 dev eth1
# Setting up VXLAN interfaces
ip link add vtep100 type vxlan id 100 dev eth1 dstport 4789 local 193.204.0.1 nolearning
# Creating the companion bridge
ip link add br100 type bridge
ip link set br100 addrgenmode none
# Attach interfaces to the bridge
ip link set dev vtep100 master br100 addrgenmode none
ip link set vtep100 type bridge_slave neigh_suppress on learning off
ip link set dev eth0 master br100
# Enable interfaces
ip link set up dev vtep100
ip link set up dev br100
# Enabling FRR
systemctl start frr
vtep1.startup
attach the VXLAN interface to the bridge
do not generate IPv6 link-local addresses

## Slide 35: vtep1 bridge configuration
ip address add 193.204.0.1/30 dev eth1
# Setting up VXLAN interfaces
ip link add vtep100 type vxlan id 100 dev eth1 dstport 4789 local 193.204.0.1 nolearning
# Creating the companion bridge
ip link add br100 type bridge
ip link set br100 addrgenmode none
# Attach interfaces to the bridge
ip link set dev vtep100 master br100 addrgenmode none
ip link set vtep100 type bridge_slave neigh_suppress on learning off
ip link set dev eth0 master br100
# Enable interfaces
ip link set up dev vtep100
ip link set up dev br100
# Enabling FRR
systemctl start frr
vtep1.startup
set the type of vtep100 to bridge_slave
suppress neighbor discovery (ARP and ND)
do not learn MAC addresses

## Slide 36: vtep1 bridge configuration
ip address add 193.204.0.1/30 dev eth1
# Setting up VXLAN interfaces
ip link add vtep100 type vxlan id 100 dev eth1 dstport 4789 local 193.204.0.1 nolearning
# Creating the companion bridge
ip link add br100 type bridge
ip link set br100 addrgenmode none
# Attach interfaces to the bridge
ip link set dev vtep100 master br100 addrgenmode none
ip link set vtep100 type bridge_slave neigh_suppress on learning off
ip link set dev eth0 master br100
# Enable interfaces
ip link set up dev vtep100
ip link set up dev br100
# Enabling FRR
systemctl start frr
vtep1.startup
attach eth0 (the server s1 collision domain) to the bridge

## Slide 37: vtep1 bridge configuration
ip address add 193.204.0.1/30 dev eth1
# Setting up VXLAN interfaces
ip link add vtep100 type vxlan id 100 dev eth1 dstport 4789 local 193.204.0.1 nolearning
# Creating the companion bridge
ip link add br100 type bridge
ip link set br100 addrgenmode none
# Attach interfaces to the bridge
ip link set dev vtep100 master br100 addrgenmode none
ip link set vtep100 type bridge_slave neigh_suppress on learning off
ip link set dev eth0 master br100
# Enable interfaces
ip link set up dev vtep100
ip link set up dev br100
# Enabling FRR
systemctl start frr
vtep1.startup
enable the VXLAN interface

## Slide 38: vtep1 bridge configuration
ip address add 193.204.0.1/30 dev eth1
# Setting up VXLAN interfaces
ip link add vtep100 type vxlan id 100 dev eth1 dstport 4789 local 193.204.0.1 nolearning
# Creating the companion bridge
ip link add br100 type bridge
ip link set br100 addrgenmode none
# Attach interfaces to the bridge
ip link set dev vtep100 master br100 addrgenmode none
ip link set vtep100 type bridge_slave neigh_suppress on learning off
ip link set dev eth0 master br100
# Enable interfaces
ip link set up dev vtep100
ip link set up dev br100
# Enabling FRR
systemctl start frr
vtep1.startup
enable the bridge

## Slide 39: vtep2 bridge configuration
ip address add 193.204.0.2/30 dev eth1
# Setting up VXLAN interfaces
ip link add vtep100 type vxlan id 100 dev eth1 dstport 4789 local 193.204.0.2 nolearning
# Creating the companion bridge
ip link add br100 type bridge
ip link set br100 addrgenmode none
# Attach interfaces to the bridge
ip link set dev vtep100 master br100 addrgenmode none
ip link set vtep100 type bridge_slave neigh_suppress on learning off
ip link set dev eth0 master br100
# Enable interfaces
ip link set up dev vtep100
ip link set up dev br100
# Enabling FRR
systemctl start frr
vtep2.startup

## Slide 40: the EVPN-BGP control-plane
vtep1# show evpn mac vni all
VNI 100 #MACs (local and remote) 2
Flags: N=sync-neighs, I=local-inactive, P=peer-active, X=peer-proxy
MAC Type Flags Intf/Remote ES/VTEP VLAN Seq #'s
a2:6d:75:c7:06:6f remote 193.204.0.2 0/0
c2:93:31:36:31:b6 local eth0 0/0

## Slide 41: a BGP update
AFI/SAFI of l2vpn/EVPN
announcement
from vtep2 to vtep1
MAC address of s1
VNI of s1
VTEP destination

## Slide 42: VXLAN encapsulation
overhead of 50 bytes
random Source Port to fully exploit Multi-Path

## Slide 43: a PING packet encapsulated in VXLAN
IPs of servers
MAC addresses of s1 and s2
MAC addresses of vtep1 and vtep2
Outer Layer 1
Outer UDP Header
VXLAN Header
Original Layer 2
Original Layer 3
Original ICMP Packet
IPs of VTEPs
Outer MAC Header
Outer IP Layer

## Slide 44: putting together
(EVPN-)BGP

## Slide 45: overview
containers or VMs of different tenants
where is the VTEP?
the Leaf-server links
inside the servers
dual attached servers
a complete lab experience

## Slide 46: servers in the fabric – recap
Servers
Containers or VMs

## Slide 47: containers or VMs of different tenants
different colours represent different tenants

## Slide 48: EVPN-BGP – where is the VTEP?
containers must be unaware of tunneling
different choices for positioning the VTEP
  in each server
    the server should have a BGP peering for enabling EVPN-BGP
    the server CPU would be used to route packets
  in each Leaf
    a Leaf already has a BGP peering
    a Leaf is a router, so it has dedicated routing hardware
    usage of VLANs in the link connecting a Leaf and a server to distinguish tenants

## Slide 49: inside the Leaves
VLANs are used
mapping between VNIs and VLAN IDs
  tenants are unaware of the mapping
Leaves decapsulate VXLAN received packets and encapsulate them into VLAN frames, according to the mapping
  and vice-versa

## Slide 50: inside the servers
the server uses the VLAN IDs to forward packets to the correct containers/VMs
the server untags the packets so that the containers/VMs are unaware of the VLANs
  containers/VMs of the same tenant share the same virtual Layer-2 network

## Slide 51: deploying VXLAN
VLAN ID VNI
10 5010
20 5020
… …
VXLAN
VLAN
no encapsulation
VLAN ID Container
10 1_1_1
20 1_1_3
… …

## Slide 52: EVPN-BGP Fat-Tree lab
hands on Kathará

## Slide 53: lab topology
AF
AA
AB
spine_1_1_2
spine_1_1_1
spine_2_1_1
spine_2_1_2
tof_1_2_1
tof_1_2_2
server_1_1
server_1_2
server_2_1
server_2_2
leaf_2_0_1
leaf_2_0_2
A
C
Z
W
M
O
L
N
K
E
B
D
Q
R
S
T
I
G
H
J
AS64512
AS64514
AS64513
AS64515
AS64516
AS64517
AS64518
AC
AD
1_1_1
1_1_2
1_1_3
1_2_2
1_2_1
2_1_1
AE
2_2_1
VNI: 5010, VLAN ID 10
Prefix: 200.10.0.0/16
VNI: 5020, VLAN ID 20
Prefix: 200.20.0.0/16
VNI: 5030, VLAN ID 30
Prefix: 200.30.0.0/16
.0.1
.0.2
.0.1
.0.1
.0.2
.0.2
.0.3
lo: 192.168.0.2/32
leaf_1_0_2
leaf_1_0_1
lo: 192.168.0.4/32
lo: 192.168.0.1/32
lo: 192.168.0.4/32

## Slide 54: vtep1 bridge configuration
ip address add 193.204.0.1/30 dev eth1
# Setting up VXLAN interfaces
ip link add vtep100 type vxlan id 100 dev eth1 dstport 4789 local 193.204.0.1 nolearning
ip link set up dev vtep100
# Creating the companion bridge
ip link add br100 type bridge
# Attach interfaces to the bridge
ip link set dev vtep100 master br100 addrgenmode none
ip link set vtep100 type bridge_slave neigh_suppress on learning off
ip link set dev eth0 master br100
# Enable bridge vlans
ip link set dev br100 type bridge vlan_filtering 1
bridge vlan add vid 100 dev vtep100 pvid untagged
bridge vlan add vid 100 dev eth0 pvid untagged
ip link set up dev br100
# Enabling FRR
systemctl start frr
vtep1.startup
enable VLANs on the bridge

## Slide 55: vtep1 bridge configuration
ip address add 193.204.0.1/30 dev eth1
# Setting up VXLAN interfaces
ip link add vtep100 type vxlan id 100 dev eth1 dstport 4789 local 193.204.0.1 nolearning
ip link set up dev vtep100
# Creating the companion bridge
ip link add br100 type bridge
# Attach interfaces to the bridge
ip link set dev vtep100 master br100 addrgenmode none
ip link set vtep100 type bridge_slave neigh_suppress on learning off
ip link set dev eth0 master br100
# Enable bridge vlans
ip link set dev br100 type bridge vlan_filtering 1
bridge vlan add vid 100 dev vtep100 pvid untagged
bridge vlan add vid 100 dev eth0 pvid untagged
ip link set up dev br100
# Enabling FRR
systemctl start frr
vtep1.startup
configure VLANs on bridge ports

## Slide 56: leaf configuration example – part 1
# Create loopback
ip addr add 192.168.0.1/32 dev lo
ip route add 192.168.0.1/32 dev lo
# Setting up VXLAN interfaces
ip link add vtep5010 type vxlan id 5010 dev lo dstport 4789 local 192.168.0.1 nolearning
ip link set up dev vtep5010
ip link add vtep5020 type vxlan id 5020 dev lo dstport 4789 local 192.168.0.1 nolearning
ip link set up dev vtep5020
ip link add vtep5030 type vxlan id 5030 dev lo dstport 4789 local 192.168.0.1 nolearning
ip link set up dev vtep5030
leaf_1_0_1.startup
configure an IP address on the loopback interface
set source IP for the VTEPs to be the loopback IP

## Slide 57: leaf configuration example – part 2
# Creating the companion bridge
ip link add br100 type bridge
# Attach interfaces to the bridge
ip link set dev vtep5010 master br100 addrgenmode none
ip link set vtep5010 type bridge_slave neigh_suppress on learning off
ip link set dev vtep5020 master br100 addrgenmode none
ip link set vtep5010 type bridge_slave neigh_suppress on learning off
ip link set dev vtep5030 master br100 addrgenmode none
ip link set vtep5010 type bridge_slave neigh_suppress on learning off
ip link set dev eth2 master br100
# Enable bridge vlans
ip link set dev br100 type bridge vlan_filtering 1
bridge vlan add vid 10 dev vtep5010 pvid untagged
bridge vlan add vid 20 dev vtep5020 pvid untagged
bridge vlan add vid 30 dev vtep5030 pvid untagged
bridge vlan add vid 10 dev eth2
bridge vlan add vid 20 dev eth2
ip link set up dev br100
systemctl start frr
leaf_1_0_1.startup – part 3
enable VLANs on the bridge
configure the vtep ports to receive/send untagged traffic of specific VLANs
configure the server ports to receive/send VLAN tagged traffic of specific VLANs

## Slide 58: leaf configuration example – part 3
# Creating the companion bridge
ip link add br100 type bridge
# Attach interfaces to the bridge
ip link set dev vtep5010 master br100 addrgenmode none
ip link set vtep5010 type bridge_slave neigh_suppress on learning off
ip link set dev vtep5020 master br100 addrgenmode none
ip link set vtep5010 type bridge_slave neigh_suppress on learning off
ip link set dev vtep5030 master br100 addrgenmode none
ip link set vtep5010 type bridge_slave neigh_suppress on learning off
ip link set dev eth2 master br100
# Enable bridge vlans
ip link set dev br100 type bridge vlan_filtering 1
bridge vlan add vid 10 dev vtep5010 pvid untagged
bridge vlan add vid 20 dev vtep5020 pvid untagged
bridge vlan add vid 30 dev vtep5030 pvid untagged
bridge vlan add vid 10 dev eth2
bridge vlan add vid 20 dev eth2
ip link set up dev br100
systemctl start frr
leaf_1_0_1.startup – part 3
enable VLANs on the bridge
configure the vtep ports to receive/send untagged traffic of specific VLANs
configure the server ports to receive/send VLAN tagged traffic of specific VLANs

## Slide 59: leaf BGP configuration example
router bgp 64512
timers bgp 3 9
bgp router-id 192.168.0.1
no bgp ebgp-requires-policy
bgp bestpath as-path multipath-relax
neighbor TOR peer-group
neighbor TOR remote-as external
neighbor TOR advertisement-interval 0
neighbor TOR timers connect 10
neighbor eth0 interface peer-group TOR
neighbor eth1 interface peer-group TOR
bgpd.conf - part 1
address-family ipv4 unicast
neighbor TOR activate
redistribute connected route-map LOOPBACKS
maximum-paths 64
exit-address-family
address-family l2vpn evpn
neighbor TOR activate
advertise-all-vni
exit-address-family
route-map LOOPBACKS permit 10
match interface lo
bgpd.conf - part 2
route-map to announce the loopback IP
enable the l2vpn evpn AFI/SAFI A.F.

## Slide 60: spine BGP configuration example
router bgp 64514
timers bgp 3 9
bgp router-id 192.168.0.5
no bgp ebgp-requires-policy
bgp bestpath as-path multipath-relax
neighbor TOR peer-group
neighbor TOR remote-as external
neighbor TOR advertisement-interval 0
neighbor TOR timers connect 10
neighbor eth0 interface peer-group TOR
neighbor eth1 interface peer-group TOR
bgpd.conf - part 1
neighbor fabric peer-group
neighbor fabric remote-as external
neighbor fabric advertisement-interval 0
neighbor fabric timers connect 10
neighbor eth2 interface peer-group fabric
neighbor eth3 interface peer-group fabric
address-family ipv4 unicast
neighbor fabric activate
neighbor TOR activate
maximum-paths 64
exit-address-family
address-family l2vpn evpn
neighbor fabric activate
neighbor TOR activate
exit-address-family
bgpd.conf - part 2
activate the l2vpn evpn AFI/SAFI A.F.

## Slide 61: ToF BGP configuration example
router bgp 64518
timers bgp 3 9
bgp router-id 192.168.0.13
no bgp ebgp-requires-policy
bgp bestpath as-path multipath-relax
bgpd.conf - part 1
neighbor fabric peer-group
neighbor fabric remote-as external
neighbor fabric advertisement-interval 0
neighbor fabric timers connect 10
neighbor eth0 interface peer-group fabric
neighbor eth1 interface peer-group fabric
neighbor eth2 interface peer-group fabric
neighbor eth3 interface peer-group fabric
address-family ipv4 unicast
neighbor fabric activate
maximum-paths 64
exit-address-family
address-family l2vpn evpn
neighbor fabric activate
exit-address-family
bgpd.conf - part 2
activate the l2vpn evpn AFI/SAFI A.F.

## Slide 62: server configuration example – part 1
ip link add bond1 type bond miimon 100 mode 802.3ad xmit_hash_policy layer3+4 all_slaves_active 1
ip link set dev eth0 down
ip link set dev eth1 down
ip link set dev bond1 down
ip link set eth0 master bond1
ip link set eth1 master bond1
ip link set dev eth0 up
ip link set dev eth1 up
ip link set dev bond1 up
# Creating the bridge
ip link add br100 type bridge
# Attach interfaces to the bridge
ip link set dev bond1 master br100
ip link set dev eth2 master br100
ip link set dev eth3 master br100
server_1_1.startup
create the bond interface
disable interfaces
connect physical interfaces to the bond
enable the interfaces
create the bridge
connect the bond and container interfaces to the bridge

## Slide 63: why 802.3ad with active-backup?
usually the right policy is active-active with hash policy
to support dual attached servers in active-active mode to different switches (leaves), Multi-Chassis Link Aggregation (MLAG) is needed
  MLAG enables a server or switch with a two-port bond, to connect those ports to different switches and operate as if they are connected to a single, logical switch. This provides greater redundancy and greater system throughput.
classic Linux kernels do not support MLAG

## Slide 64: server configuration example – part 2
# Enable bridge vlans
ip link set dev br100 type bridge vlan_filtering 1
bridge vlan add vid 10 dev bond1
bridge vlan add vid 20 dev bond1
bridge vlan add vid 10 dev eth2 pvid untagged
bridge vlan add vid 20 dev eth3 pvid untagged
ip link set up dev br100
server_1_1.startup
configure the bond port of the bridge to receive tagged VLAN packets
configure the container ports to send untagged frames

## Slide 65: a leaf data plane
root@leaf_1_0_1:/# ip route
10.0.0.0/30 dev eth0 proto kernel scope link src 10.0.0.1
10.0.0.4/30 dev eth1 proto kernel scope link src 10.0.0.5
192.168.0.1 dev lo scope link
192.168.0.7 nhid 10 proto bgp metric 20
nexthop via 10.0.0.2 dev eth0 weight 1
nexthop via 10.0.0.6 dev eth1 weight 1

## Slide 66: a leaf BGP control plane
leaf_1_1_1# show ip bgp
BGP table version is 2, local router ID is 192.168.0.1, vrf id 0
Default local pref 100, local AS 64512
Status codes: s suppressed, d damped, h history, * valid, > best, = multipath,
i internal, r RIB-failure, S Stale, R Removed
Nexthop codes: @NNN nexthop's vrf id, < announce-nh-self
Origin codes: i - IGP, e - EGP, ? - incomplete
Network Next Hop Metric LocPrf Weight Path
*> 192.168.0.1/32 0.0.0.0 0 32768 i
*> 192.168.0.7/32 10.0.0.2 0 64514 64518 64517 64515 i
*= 10.0.0.6 0 64514 64518 64517 64515 i

## Slide 67: a leaf EVPN control plane
leaf_1_1_1# show evpn mac vni 5010
Number of MACs (local and remote) known for this VNI: 3
Flags: N=sync-neighs, I=local-inactive, P=peer-active, X=peer-proxy
MAC Type Flags Intf/Remote ES/VTEP VLAN Seq #'s
8e:cf:26:1f:44:16 local eth2 10 0/0
d2:23:78:4a:e9:02 local eth2 10 0/0
76:76:b2:f0:18:6d remote 192.168.0.7 0/0

## Slide 68: EVPN-BGP and Bond

## Slide 69: lab topology
AF
AA
AB
spine_1_1_2
spine_1_1_1
spine_2_1_1
spine_2_1_2
tof_1_2_1
tof_1_2_2
server_1_1
server_1_2
server_2_1
server_2_2
leaf_2_0_1
leaf_2_0_2
A
C
U
V
Z
W
M
F
P
O
L
N
K
E
B
D
Q
R
S
T
I
G
H
J
AS64512
AS64514
AS64513
AS64515
AS64516
AS64517
AS64518
AC
AD
1_1_1
1_1_2
1_1_3
1_2_2
1_2_1
2_1_1
AE
2_2_1
VNI: 5010, VLAN ID 10
Prefix: 200.10.0.0/16
VNI: 5020, VLAN ID 20
Prefix: 200.20.0.0/16
VNI: 5030, VLAN ID 30
Prefix: 200.30.0.0/16
.0.1
.0.2
.0.1
.0.1
.0.2
.0.2
.0.3
lo: 192.168.0.1/32
leaf_1_0_2
leaf_1_0_1
lo: 192.168.0.2/32

## Slide 70: anycast BGP
technique that allows different devices to share the same IP address
often used in the Internet with DNS servers and CDN servers
BGP chooses among the nearest instance of the IP address
in the data center, multipath is exploit to balance over multiple instances of the same anycast IPs

## Slide 71: the last problem to overcome
if a Leaf-server link breaks down, the server is severed off the data center
if a Leaf breaks, all the servers connected to that Leaf are severed off the data center
if a maintenance needs to be done on a Leaf, all the servers connected to that Leaf are temporarily severed off the data center

## Slide 72: dual attached servers – bonding
aggregates multiple NICs into a single virtual interface
Layer-2 technology
different policies are possible
  active-backup
  active-active
    balance-rr
    balance-xor
    802.3ad
    and more…

## Slide 73: the full picture
VLAN ID VNI
10 5010
20 5020
… …
VXLAN
VLAN
no encapsulation
VLAN ID Container
10 1_1_1
20 1_1_3
… …

## Slide 74: bibliography and further readings
[Dutt ‘18] Dutt, “EVPN in the Data Center”, O’Reilly, 2018
[Bernat ‘17] Bernat, “VXLAN: BGP EVPN with FRR“, https://vincent.bernat.ch/en/blog/2017-vxlan-bgp-evpn
[Bernat ‘17] Bernat, “VXLAN & Linux”, https://vincent.bernat.ch/en/blog/2017-vxlan-linux
[RFC-7432] Sajassi, Aggarwal, Bitar, Isaac, Uttaro, Drake, Henderickx, “BGP MPLS-Based Ethernet VPN ” Internet Engineering Task Force (IETF) Request for Comments: 7432
[RFC-8365] Sajassi, Drake, Bitar, Shekhar, Uttaro, Henderickx, “A Network Virtualization Overlay Solution Using Ethernet VPN (EVPN)” Internet Engineering Task Force (IETF) Request for Comments: 8365